## Slide 1: Discussion on further SL enhancement in Rel-18
5G Team / Lenovo Research / MBG
Agenda Item: 9.0.2
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN Meeting #93-e RP-212060
Electronic Meeting, September 13 - 17, 2021

## Slide 2: Motivation
Requirements for sidelink communication are quite diverse with emerging use cases.
On data rate:
  The required data rate can be ranged from several Mbps (e.g., for sidelink communication between the wearable devices to the smart phone) to Gbps (e.g., for AR/VR/cloud gaming applications, or for the extended sensors for vehicle to vehicle to exchange the raw or processed data gathered through local sensors or live video images among vehicles, road site units, and V2X application servers)
On latency:
  The required latency can be varied from tens of microseconds (e.g., for AR/VR and V2X applications) to tens of milliseconds (e.g., for smart home and wearable devices).
  On reliability:
  High reliability is required to support URLLC-type sidelink use cases.

## Slide 3: Motivation
Table 7.6.1-1 KPI Table for additional high data rate and low latency service
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area (note 2)
Gaming or Interactive Data Exchanging (note 3) | 10ms (note 4) | 0,1 to [1] Gbit/s supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to120 frames per second content. | 99,99 % (note 4) | ≤ [10] | Stationary or Pedestrian | 20 m x 10 m; in one vehicle (up to 120 km/h) and in one train (up to 500 km/h)
Consumption of VR content via tethered VR headset (note 6) | [5 to 10] ms (note 5) | 0,1 to [10] Gbit/s (note 5) | [99,99 %] | - | Stationary or Pedestrian | -
NOTE 3: Communication includes direct wireless links (UE to UE). NOTE 4: Latency and reliability KPIs can vary based on specific use case/architecture, e.g. for cloud/edge/split rendering, and may be represented by a range of values. NOTE 5: The decoding capability in the VR headset and the encoding/decoding complexity/time of the stream will set the required bit rate and latency over the direct wireless link between the tethered VR headset and its connected UE, bit rate from 100 Mbit/s to [10] Gbit/s and latency from 5 ms to 10 ms. NOTE 6: The performance requirement is valid for the direct wireless link between the tethered VR headset and its connected UE. |  |  |  |  |  | 
Note: cited from TS22.261
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message /Sec) | Max end-to-end Latency (ms) | Reliability (%) | Data rate (Mbps) | Min required communication range (meters)
Scenario | Degree |  |  |  |  |  |  | 
Sensor information sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-001] | 1600 | 10 | 100 | 99 |  | 1000
 | Higher degree of automation | [R.5.4-002] |  |  | 10 | 95 | 25 (NOTE 1) | 
 |  | [R.5.4-003] |  |  | 3 | 99.999 | 50 | 200
 |  | [R.5.4-004] |  |  | 10 | 99.99 | 25 | 500
 |  | [R.5.4-005] |  |  | 50 | 99 | 10 | 1000
 |  | [R.5.4-006] (NOTE 2) |  |  | 10 | 99.99 | 1000 | 50
Video sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-007] |  |  | 50 | 90 | 10 | 100
 | Higher degree of automation | [R.5.4-008] |  |  | 10 | 99.99 | 700 | 200
 |  | [R.5.4-009] |  |  | 10 | 99.99 | 90 | 400
NOTE 1: This is peak data rate. NOTE 2: This is for imminent collision scenario. |  |  |  |  |  |  |  | 
Table 5.4-1 Performance requirements for extended sensors
Note: cited from TS22.186

## Slide 4: Motivation
It is not sufficient to use the existing limited ITS spectrum for sidelink communication to satisfy the stringent requirements especially when there are many devices/vehicles in the serving area.
For commercial use cases, the ITS spectrum can’t be used.
For V2X use cases, the existing ITS spectrum is too limited to satisfy the requirements of data rate for video sharing among vehicles and collective environment perception.
More spectrum resources are needed, e.g., FR2 or FR2x bands, as well as the corresponding multi-carrier operation, e.g., carrier aggregation, cross-carrier scheduling from FR1 to FR2.

## Slide 5: Objectives
Objective 2: FR2 support for sidelink communication
  Specify beam management between transmission UE and reception UEs
  Specify directional sensing-based resource allocation mechanism
Objective 1: Multi-carrier operation
  Specify carrier aggregation for support of Gbps data rate including cross-carrier scheduling
  Specify multi-carrier duplication for reliability improvement
Objective 3: Feedback enhancement
  Specify new PSFCH format for support of more than 1 bit (e.g., CA/CBG-based feedback)
  Specify CSI measurement and feedback for link adaptation