## Slide 1: RedCap Evolutions in Rel.18
5G Team / Lenovo Research / MBG
Agenda Item: 9.0.2
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN #93 RP-212068
Electronic Meeting, September 13 – 17, 2021

## Slide 2: Motivation
Rel.17 RedCap with 20MHz maximum UE BW for FR1, 100MHz maximum UE BW for FR2 meet the data rate requirement up to 150Mbps DL for high-end wearables and high-end videos.
Devices like industrial sensors, economic videos, etc., require much lower reference bit rate even less than 5Mbps, while cost reduction is significant for wide deployment of such devices and is vital for commercial success for RedCap.
Further cost/complexity breakdown specific for the RedCap devices therefore needs to be studied and specified.
Besides, further power consumption needs to be studied to ensure longer battery life.
Use cases | Reference bit rate | Latency | Reliability | Battery life
Industrial wireless sensors | <2Mbps | <100ms; 5-10ms for safety related sensors. | 99.99% | At least few years.
Video surveillance | 2-4Mbps for economic video; 7.5-25Mbps for high-end video | <500ms | 99%-99.9% | NA
Wearables | 5-50Mbps in DL, 2-5Mbps in UL. peak data rate <=150Mbps in DL, <=50Mbps in UL. | NA | NA | <= 1-2 weeks
RedCap use case requirements

## Slide 3: Scope
Lower maximum BW supported in Rel.18 RedCap with e.g.,
  5MHz for FR1
  20MHz for FR2
Lower reference bit rate down to 5~10Mbps.
Lower UE power class with maximum transmit power of e.g., 14dBm.
Lower power consumption to ensure longer battery life.
Improved transmit efficiency/latency/reliability.
Improved coverage.

## Slide 4: Proposed objectives
Further cost/complexity reduction with lower max. UE BW
  Study the potential impact for both initial access and after initial access.
  Study co-existence of Rel.18 RedCap UEs with legacy UEs (incl. Rel.17 RedCap UEs).
Further power saving
  Introduction the supporting of lower power class UEs.
    study coverage enhancement for such UEs.
  Study power efficient wake-up signals/procedures (maybe in a separate SI/WI).
Study upper layer support for Rel.18 RedCap new UE type, including UE identification and access control, etc.
Specify Rel.17 leftovers if any.