## Slide 1: Discussion on Working Areas of XR for 5G Advanced
3GPP TSG RAN #93
Electronic Meeting, Sep 13 - Sep 17,2021
Source: ZTE, Sanechips
Agenda: 9.0.2
RP-212377

## Slide 2: Outline
Overview of RAN1 Evaluation Results for Rel-17 XR
Considerations on XR Working Areas for 5G Advanced
- Enhancement on Capacity
- Enhancement on Power Consumption
Solutions for Considerations on XR Working Areas
Proposed WID for Rel-18 XR

## Slide 3: Evaluation Results Overview
Up to RAN1#106-e, initial evaluation results focus on capacity and power saving:
Input on capacity from 15 sources
  15 sources have submitted results for DL VR or CG
  10 sources have submitted results for UL pose/control or aggregated data
Input on power from 9 sources
  6 sources have submitted results for DL
  1 source have submitted results for UL
  4 sources have submitted result for DL + UL

## Slide 4: Evaluation Results Overview - Capacity
  The range of capacity statistics (90% of the UE per cell is satisfied) is listed as follows under similar settings (traffic setting,
  PDB/PER setting, scheduler etc.)
Source: R1-2108665 'Summary of XR evaluation results RAN1-106e'

## Slide 5: Evaluation Results Overview - Power
The simulation results of power saving scheme (e.g. eCDRX) are summarized as follows:
eCDRX schemes:
Source#1: R1-2106631 Performance evaluation results for XR vivo.
Source#2: R1-2108007 XR performance evaluation results Ericsson.
Source#3: R1-2108273 Performance Evaluation Results for XR ZTE, Sanechips.

## Slide 6
Potential Working Areas - Capacity
Potential Enhancement
  XR coexistence with existing service
    Preemption/cancellation for achieving inter/intra-UE multiplex based on QoS parameter/traffic characteristic difference, e.g. importance/PDB/PER, among different data streams.
  Link adaptation techniques for (Re-)Tx
    Link adaptation for re-Tx, e.g. delta MCS, enhanced CBG-based retransmission.
    Note: The CSI measurement/reporting can be enhancement on the top of Rel-17 uRLLC/IIoT.
  Network coding
    Enhanced RAN protocol stack based on network coding to adapt to application layer traffic characteristic and requirements.
  Enhancements related to Delay-Aware Scheduler
    Further investigate the potential spec. impact in interaction with ADU (Application Data Unit)
    Potential differentiation on 5QI PDB requirement differentiation within a single stream.

## Slide 7
Potential working areas - Capacity
Potential Enhancements (continued from previous page)
  Inter-cell Interference Coordination
    Mechanism to mitigate interference of neighboring cell to aide scheduling
    Assistance of high layer to achieve gNB coordination
  Adaptive Tx for multiple stream
    Answering to SA4 initiative on 5QI, SA4 needs to standardize 5QI and convey it to RAN1 so that it can perceive the difference in QoS of data.

## Slide 8: Solution for XR Coexistence - Enhanced Preemption Scheme
In current network, coexistence between uRLLC and eMBB can be improved by preemption.
Due to XR service characteristic of uRLLC-like latency requirement and eMBB-like data amount, XR coexistence (e.g. XR coexists with uRLLC) is likely to have great negative impact on capacity performance by using Rel-15 preemption scheme. To this end, the preemption scheme needs to be enhanced for XR coexistence.
Rel-15 Pre-emption mechanism
Potential Enhancement
Finer granularity should be considered for improving Rel-15 pre-emption mechanism.
Inter/intra-UE multiplex based on QoS parameter/traffic characteristic difference.

## Slide 9: Solution for Link adaptation: Enhanced CBG-based re-transmission
One of the characteristic of XR service is large data amount (i.e. large transport block). When gNB receives an NACK, retransmitting large TB is likely to cause network congestion.
CBG-based transmission is capable of indicating and re-transmitting the CBG in error to reduce data amount of retransmission and save the radio resource.
Rel-15 Pre-emption mechanism
Rel-15 CBG-based transmission for XR traffic
  Capable of improving the capacity by significantly reducing retransmission radio resource.
  Enlarge the feedback length of HARQ-ACK information, increasing the feedback overhead.

## Slide 10: Solution for Link adaptation: Enhanced CBG-based re-transmission
Problem of concurrent CBG-based retransmission
  Exhaustive state indication for Re-Tx TB.
  Variant Re-Tx payload/resources corresponding to the erroneously decoded CBG.
Outer Coder for CBG-based retransmisssion
  One state indication only for Re-Tx TB: reduced feedback overhead.
  Uniform Re-Tx payload/resources: throughput increase.

## Slide 11
Both DL and UL
  Non-integer traffic cycle (e.g. 16.67ms per frame) – mismatch between traffic cycle and legacy CDRX
    Appropriate DRX setting (DRX periodicity/DRX on duration timer) delivering trade-off between decent power saving gain & acceptable capacity loss.
  Non-integer traffic cycle (e.g. 16.67ms per frame) – mismatch between traffic cycle and legacy CG/SPS cycle
  Variable packet size of video stream
    Challenging to directly apply legacy CG/SPS settings to harness the power saving gain w.r.t. DG
  DL
  Further mismatch between traffic cycle and legacy CDRX cycle due to jitter
    Even more challenges calling for dynamic adaptation
  UL
  Frequent transmission of pose/control information (4ms per pose)
    No chance to enter light sleep state
Challenges of power saving schemes for XR

## Slide 12: Potential Working Areas – Power saving
Aspects of power saving schemes that could impact XR performance
  CDRX
    Semi-statistic configuration can not fit the non-integer traffic cycle.
  Cross-slot scheduling
    Large K0min/K2min will cause large latency
  WUS
    Not-wake up indication may increase the latency.
  PDCCH skipping/PDCCH switching
    Long PDCCH skipping duration or large PDCCH monitoring period may have impact on capacity.
Note: This topic has been discussed under Rel-17 power saving
Potential enhancement
  eCDRX (Enhancements of CDRX)
    Dynamically changing DRX parameters to align the DRX cycle and traffic cycle. e.g., changing the start time of DRX ON Duration or changing DRX cycle according to fixed patterns or indicated by DCI.
    Jitter handling
  Power saving schemes jointly considering UL and DL
    e.g., DL and UL alignment
  FFS: Modified R16/R17 power saving schemes. e.g., cross slot scheduling, WUS, PDCCH skipping/switching
  FFS: UE Assistance Information

## Slide 13: Potential Enhancement For CDRX
Since the DRX cycle is always an integer value, there is a mismatch between the DRX cycle and traffic, which affects the capacity. To this end, dynamic change of DRX parameters to match the traffic can be considered.
Jitter will increase the difficulty of applying UE power saving techniques because the packet arrival time fluctuates around the periodicity benchmarks. An additional active time can be used for jitter handling.

## Slide 14
XR Performance Improvement by Proposed Solution
XR coexistence
Enhanced Preemption scheme
Enhanced preemption scheme is capable of reducing resource utilization and improving the XR capacity performance by finer granularity indication.

## Slide 15
XR Performance Improvement by Proposed Solution
Enhanced CDRX scheme
Application | Scheme | avg # UEs/ cell = N1 | C1=floor(Capacity) | % of satisfied UEs when #UEs/cell = N1 | Average PS gain (%)
VR_30MHz | Baseline | 11 | 11 | 93.18% | /
 | eCDRX(16,6,4) | 11 | 11 | 87.12% | 30.87%
VR_45MHz | Baseline | 7 | 7 | 91% | /
 | eCDRX(16,6,4) | 7 | 7 | 86.3% | 29.64%
FR1 power consumption results in Indoor Hotspot scenario(DL evaluation)
Enhanced CDRX scheme can provide 30% power saving gain .

## Slide 16: Proposed WID for Rel-18 XR
    Motivation
      Enable decent XR capacity and concurrent delivery of XR and other services in NW
      Strive to fulfill UE power saving gain under acceptable capacity loss
    A work item with study phase can be considered:
      Specify enhancements on dynamic grant including link adaptation techniques for (Re-)Tx, Pre-emption /Cancellation under DL/UL current Transmission, Network Coding [RAN1, RAN2]
        Enhanced CSI measurement/reporting for better Tx efficiency, e.g., report of delta MCS, enhanced CBG based Tx
        Pre-emption/Cancellation for achieving inter/intra-UE multiplex based on QoS parameter/traffic characteristic difference, e.g. importance/PDB/PER, among different data streams
        Enhanced RAN protocol stack based on network coding to adapt to application layer traffic characteristic and requirements
      Support of inter-cell interference coordination [RAN3, RAN1]
        Interface/Signaling to facilitate interference related information exchange
        Mechanism to mitigate interference of neighbor cell to aide scheduling

## Slide 17
      Study and if needed, specify the 5QI aspects and relevant pre-emption/cancellation mechanism to enable efficient delivery of (concurrent) XR services [SA4, RAN1]
        Further study the potential spec. impact in interaction with ADU (Application Data Unit), differentiation on 5QI PDB requirement differentiation within a single stream
        Adaptive Tx for multiple stream including priority based pre-emption/cancellation
      Specify enhancements on dynamic grant including eCDRX(Enhancements of CDRX) [RAN1, RAN2]
        Dynamically changing DRX parameters to align the DRX cycle and traffic cycle. e.g., changing the start time of DRX ON Duration or changing DRX cycle according to fixed patterns or indicated by DCI
      Study and if needed, specify Power saving schemes jointly considering UL and DL, modified R16/R17 power saving schemes, UE Assistance Information [RAN1,RAN2]
        Mechanism to ensure DL and UL alignment
        Modified cross slot scheduling, WUS, PDCCH skipping/switching
        Dropping of some consecutive UL transmission(s)
Proposed WID for Rel-18 XR (Continued)

## Slide 18: Thanks