## Slide 1
Rel-17 scope for SDT
3GPP TSG RAN Meeting #93e
Electronic Meeting, September 13 – 17, 2021
Source: ZTE, Sanechips
Agenda: 9.3.2.7
RP-211433

## Slide 2: General status
Small Data Transmission (SDT) feature enables the UE to send and receive small data packets whilst the UE is in INACTIVE state
Two mechanisms are being specified to support SDT
  RA-SDT: Where the SDT transmission is initiated by RACH procedure and both 2-step and 4-step RACH are supported for this
    RA-SDT is supported with and without anchor relocation and RAN3 will define procedures to enable both
  CG-SDT: Where type 1 configured grant resources are configured for the UE to be used in INACTIVE state in a given cell
RAN2 continues to work on the Rel-17 SDT feature based on the above framework and the progress of the work so far seems be to inline with the expectations
Some of the features discussed as part of the above framework have either been de-prioritised or agreed to be not part of Rel-17 in RAN2 and the work item can be updated clarifying this renewed scope
  RAN2 has agreed to deprioritise the RRC-less solution for SDT
  RAN2 agreed not to optimise the system for late anchor relocation (i.e. anchor relocation during SDT session)

## Slide 3: RRC-less SDT
When the Rel-17 WID was approved, both RRC-based and RRC-less solutions were on the table and RAN2 had an early discussion on these solutions
Whilst RRC-based SDT (i.e. the solution which includes the CCCH message in the first UL message) supports for both RA-SDT and CG-SDT and also supports both same cell and different cell use cases
RRC-less solution would be an optimisation for the same cell case and is not essential for the feature to work
Given the time left in Rel-17 and given the decision early in RAN2 to deprioritise this, the proposal is to explicitly preclude this now in the Rel-17 WI
Proposal 1: Remove RRC-less solution from the scope of Rel-17 SDT WI

## Slide 4: Optimisations for late anchor relocation
In case of RA-SDT, two solutions will be defined:
  Solution 1: With anchor relocation:
    In this solution, the anchor is relocated to the new target gNB and path-switch is performed prior to SDT data/control message transfer
  Solution 2: Without anchor relocation
    In this solution, the anchor is not relocated and path switch is not performed
    Data and CP messages are tunnelled through the old anchor gNB and this reuses the mechanisms that have been defined for RAN Area Update without anchor relocation in Rel-15
    In addition to the above, subsequent data transmission both in UL and DL is possible with SDT and it is also possible that anchor relocation may be required during this subsequent data transmission phase
  However, supporting relocation of the anchor during the SDT will present additional work in RAN3 and RAN2 and may also need some feedback from SA3
  To simplify the feature, RAN2 has agreed to not support any optimisations for the above case and instead move the UE back to INACTIVE state
  This may result in data duplication/redundancy but this is found to be acceptable for Rel-17
Proposal 2: Optimisations for late-anchor-relocation are not supported in Rel-17

## Slide 5: Conclusion and proposals
The overall scope of Rel-17 SDT WI is discussed in this document and the following proposals are made:
  Proposal 1: Remove RRC-less solution from the scope of Rel-17 SDT WI
  Proposal 2: Optimisations for late-anchor-relocation are not supported in Rel-17
  An Updated WID implementing the above proposals is provided in RP-211860

## Slide 6: Thanks