## Slide 1: Way forwards on AI for NG-RAN in Rel-18
CMCC
3GPP TSG RAN Meeting #94e RP-213039
Electronic Meeting, December 6 -17, 2021
Agenda Item: 8.A.3
Source: CMCC
Document for: Discussion

## Slide 2: Status of Rel-17 SI
In the ongoing study on AI for NG-RAN in Rel-17, the general AI framework and following three prioritized use cases are under discussion:
  Energy saving
  Load balancing
  Mobility optimization
The overall Completion level is about 70%

## Slide 3: Discussion on Pre-RAN#94e for follow-up WI
Conclusion1) The RAN3 led R18 AI for NG-RAN WI to be approved in Dec.
Conclusion2) Take the draft WID below as the baseline to be approved
  The detailed objectives of the WI are listed as follows:
  Specify data collection enhancements and signaling support within existing NG-RAN interfaces and architecture (including non-split architecture and split architecture) for AI/ML-based Network Energy Saving, Load Balancing and Mobility Optimization. (RAN3)
  Note: On security impacts, coordination with SA3 when needed. On OAM aspects, coordination with SA5 when needed. Editor’s Note: The objectives and any other involved working groups are subject to further refinement when the Rel-17 SI is completed.

## Slide 4: Discussion on Pre-RAN#94e for new SI
Conclusion3) It is proposed to take option1b) as a compromised way to handle R18 SI, with the understanding that 6 months TU will be reserved for R18 SI if needed. [no consensus]
Conclusion4) Take the objective list below as a starting point for the draft SID, which needs to be revisited after the WI is completed. [no consensus]
The potential objectives of the SI are listed as follows:
  Study new use cases for NG-RAN (e.g., AI/ML for slicing, QoE and other potential use cases);
  Study network functionality and interface procedures to support the agreed use cases enabled by AI/ML, including:
    Multi-vendor interoperability between different AI/ML functions (e.g., Data Collection, Model Training, Model Inference).
    Integration and collaboration of OAM AI/ML, 5GC AI/ML, NG-RAN AI/ML if identified. Note: Integration and collaboration with air interface AI/ML to be considered based on progress of Air interface AI/ML SI.

## Slide 5: Organization of follow-up WI and new SI
5G+AI is a topic that will last for several releases, it seems no urgent and not sensible to have a WI + SI in parallel in Rel-18
Following the conclusion of the Rel-17 SI, approval of a WI and accomplishment of the normative work should be the prioritized task in Rel-18
The new R18 SI could be approved only after the R18 WI is completed, which allow us to apply whatever we learn from R18 WI and make a better proposal for R18 SI
Proposal 1: A Rel-18 follow-up WI should be first approved and finished before starting any further study
Proposal 2: The new R18 SI could be approved only after the R18 WI is completed

## Slide 6
Thank you!