## Slide 1: Proposed update for REL18 Mobile IAB WI
RP-213109

## Slide 2: IAB/VMR
Draft WID RP-212718 Mobile IAB from [RAN94e-R18Prep-18] Additional topological improvements – IAB (Integrated Access and Backhaul)/VMR (Vehicle Mounted Relay) is generally agreeable as baseline.
The detailed objectives of the WI are listed as follows: Define Procedures for migration/topology adaptation to enable IAB-node mobility [RAN3, RAN2] Enhancements for mobility of an IAB-node together with its served UEs. It is FFS whether surrounding UEs shall also be served [RAN3, RAN2] Note: Solutions should avoid to touch upon topics where Rel17 discussions already occurred and where the topic was excluded from Rel17. Mitigation of interference due to IAB-node mobility, including the avoidance of reference and control signal collisions (e.g. PCI, RACH). [If is FFS whether RAN2 or RAN3 should be leading the activity] The following principles should be respected: Mobile IAB-nodes should be able to serve legacy UEs. Solutions providing optimisation for Mobile IAB may entail Rel18 UE enhancements, provided that such enhancements are backwards compatible - Draft WID (RP-212718) Objectives

## Slide 3: Inclusion of VMR within this WID
Discussion regarding the inclusion of VMR within the context of mobile IAB-node was left unresolved during discussion (RP-212678), due to concerns that SA2 may not base their VMR work on the IAB architecture.
Since this RAN discussion SA2 have agreed the study item VMR in S2-2109325, which states
    “NOTE 1: The study focuses on the IAB only. Any other alternative of base station relay depends on the RAN study output if any.”
Hence reference to VMR the TS22.839 and therein the requirements incorporated in TS22.261section 6.42 should be included within the work item for REL18.
We accept that it will not be possible to include all scenarios captured in TS22.839 in REL18 due to possible solution complexity and available time units. We can support the use case captured during [R18Prep] discussions, namely
  Focus on the mobile-IAB/VMR-nodes mounted on vehicles scenario providing 5G coverage/capacity enhancement to onboard and/or surrounding UEs

## Slide 4: Surrounding UEs mobility
The current WID draft includes an FFS regarding handling of surrounding UEs within the possible mobility aspect
    “Enhancements for Mobility of IAB-node together with served UEs. It is FFS whether surrounding UEs shall also be served”
We think there are scenarios of IAB-node/VMR-node mobility where UEs may not be truly inside the vehicle, but rather may be also in the close proximity to the mobile repeater node but with only slightly varying relative speed from the mobile node.
Also we feel a need to determine inside and surrounding categories is arbitrary and other mobility related criteria are more consistent with RAN decision making and predictable for mobility algorithms.
If a limitation in scope is considered necessary then as a first step relatively slower moving surrounding UEs could be considered in this release

## Slide 5: WID RP-212718 Objectives Amendment
<NEW> Focus on the mobile-IAB/VMR-nodes mounted on vehicles scenario providing 5G coverage/capacity enhancement to onboard and/or surrounding UEs in Rel-18 as discussed by TR22.839 and requirements incorporated in TS22.261section 6.42.
  Note: VMR to only to consider solutions based on IAB architecture in this Release
Define Procedures for migration/topology adaptation to enable IAB-node mobility [RAN3, RAN2]
Enhancements for mobility of an IAB-node together with its served and surrounding UEs. It is FFS whether surrounding UEs shall also be served [RAN3, RAN2]
  Note: Solutions should avoid to touch upon topics where Rel17 discussions already occurred and where the topic was excluded from Rel17.
Mitigation of interference due to IAB-node mobility, including the avoidance of reference and control signal collisions (e.g. PCI, RACH). [If is FFS whether RAN2 or RAN3 should be leading the activity]