## Slide 1: Motivation on Rel-18 Further Measurement Gap Enhancement (RAN4)
MediaTek Inc.
3GPP TSG RAN 94E RP-213358
December 6th-17th, 2021 Agenda Item 8A.5

## Slide 2: Background
Rel-17: RAN4-led WID NR and MR-DC measurement gap enhancements
  Pre-configured gap (pre-MG)
  Concurrent gap
  Network control small gap (NCSG)
It is highly likely RAN4 can only finalize the basic individual requirements for the above objectives
  i.e. no time to work on more advanced options or deal with joint requirements, e.g., concurrent legacy gap and NCSG
A new Rel-18 WI is proposed to cover these issues

## Slide 3: Rel-17 MG Enhancements leftovers Concurrent gap
RAN4 agreement to work on priority rule on collided gap occasion
  Simple but potentially inefficient in some gap config. e.g. some gaps are never used
  Gap sharing rule was proposed to address the inefficiency but decided to be postponed to Rel-18
  Data scheduling resumption on the dropped gap occasion is worth investigating
Proposal 1: Concurrent Gap: In Rel-18, further work on the requirements based on gap sharing rule, considering how to resume data scheduling on the dropped gap occasion

## Slide 4: Rel-17 MG Enhancements leftovers Network-controlled small gap
UE Capability reporting likely to follow NeedforGap i.e. UE reports whether a target band can be measured via NCSG based on its currently configured serving cells
  Not all configured serving cells are active
  If one serving cell is current deactivated, it is believed that this serving cell will not occupy a dedicated RF chain i.e. the UE is able to use the idle RF chain for NCSG-assisted measurement
  Differentiation activated/deactivated cells can be further investigated in Rel-18 to increase the benefit of NCSG
Proposal 2: Network-controlled small gap: In Rel-18, investigate and introduce a mechanism and requirements to allow UE to report NCSG capability based on its active serving cells

## Slide 5: Rel-17 MG Enhancements leftovers Joint requirements for Pre-MG, Concurrent Gap and NCSG
High interest in RAN4 on
  Joint working of Concurrent Gap and NCSG
    This allows the network to better configure legacy MG and NCSG to UE, when UE is not able to use NCSG to perform measurement on all target frequency bands.
    By reconfiguring a legacy MG to NCSG, data interruption can be reduced and higher throughput can be achieved.
  Joint working on Concurrent Gap and Pre-MG
    This allows network to configure one pre-MG to handle intra-frequency layers (FFS for PRS measurement), while associated all the other measurements to a legacy gap.
    In this way, the network configuration can be more flexible to reflect the instantaneous need of UE without suffering the latency due to RRC reconfiguration.
Proposal 3: Joint requirements:
  Concurrent Gap and NCSG
  Concurrent Gap and Pre-MG

## Slide 6: Summary
Further Measurement Gap Enhancements in Rel-18
Proposal 1: Concurrent Gap: In Rel-18, further work on the requirements based on gap sharing rule, considering how to resume data scheduling on the dropped gap occasion.
Proposal 2: Network-controlled small gap: In Rel-18, investigate and introduce a mechanism and requirements to allow UE to report NCSG capability based on its active serving cells.
Proposal 3: Joint requirements:
  Concurrent Gap and NCSG
  Concurrent Gap and Pre-MG

## Slide 7: Thank You!