## Slide 1: On scope of frequency bands for Redcap in Rel-17
Ericsson
3GPP TSG RAN Meeting # 94-e
Electronic meeting, December 6-17, 2021
Agenda item: 9.3.1.7
Document for: Approval
RP-213427

## Slide 2: Background
RAN#93-e agreements on V2X/PC5 on n47, unlicensed bands, SUL bands [1]:
No consensus on whether a RedCap UE can support V2X/PC5 on n47, unlicensed bands, SUL bands.
Moderator’s proposal for discussion in Friday GTW:
  In Rel-17, there will be no work on any RedCap specific specification update for any of the following:
    RedCap UEs also supporting V2X/PC5 on n47
    RedCap UEs operating in unlicensed bands
    RedCap UEs supporting SUL
  The specification will not contain any explicit restriction to prevent implementation of RedCap UEs with these features.
  Note: The consequence of this agreement would be:
    If any spec change/addition is found necessary in order to enable one of the options above then it will not happen in Rel-17.

## Slide 3: Interpretation of RAN#93-e Agreements
Our interpretation of RAN#93-e agreement is that any of the following bands/features which require RedCap specific specification update, shall be clearly identifiable in the RAN4 specs as not applicable for RedCap UE in Rel-17:
    RedCap UEs also supporting V2X/PC5 on n47
    RedCap UEs operating in unlicensed bands
    RedCap UEs supporting SUL
But RAN#93-e agreement is misinterpreted by some companies in RAN4.

## Slide 4: RF Impact of Introduction of Redcap bands
UE RF spec (TS 38.101-1) specifies large number of receiver and transmitter requirements which are dependent on channel BW.
RF specification TS 38.101-1 needs to be updated to add the RedCap operating bands:
  The supported band # needs to be added for the RedCap supported operating band
    Different features in TS 38.101-1 have specific clause to add the supported band with different suffix
      It is agreed add new suffix for RedCap feature[4].
  1 RX branch REFSENS needed to be updated for RedCap supported operating band
    It is agreed to specify the RF REFSENS [4]
      Specify REFSENS:
        For one Rx branch.
RF specification TS 38.101-1 needs to be updated to add the SUL and V2X band combo for SUL band/V2X_n47+ RedCap bands and NR-U bands (n46 and n96):
  Channel bandwidth in current band combo needs to be updated for the Redcap Band to limit up to 20MHz
  For V2X band combo, if the RedCap bands is 1RX /HD-FDD only, additional REFSENS impact needs to be analysed
  For SUL band combo, if the RedCap bands is 1RX/ HD-FDD only, additional REFSENS impact needs to be analysed
  Channel BWs and associated requirements for n46 and n96 need to be limited to 20 MHz.

## Slide 5: RRM Impact of Redcap in Unlicensed bands
Following requirements specific to Redcap UEs are being specified in Rel-17:
  Measurement requirements with eDRX cycle in RRC idle and RRC inactive states
  Measurement requirements for UE power saving in RRC idle and RRC inactive states
  Measurement requirements for UE power saving in RRC connected states are FFS
Above requirements are being specified for Redcap UE for both 1Rx and 2Rx
Above requirements do NOT exist for UE supporting unlicensed bands in Rel-16
Observations:
  Introduction of Redcap in unlicensed bands even for 2 Rx UE will require at least new requirements for eDRX and UE power saving.
  Redcap in unlicensed bands even for 2 Rx UE due to spec impact cannot be specified in Rel-17 in RAN4 specifications.

## Slide 6: WF on V2X/PC5 on n47, unlicensed band and SUL bands
Observations:
  There is specification impact for introducing the above bands:
    Redcap in unlicensed bands even for 2 Rx UE require new requirements for eDRX and UE power saving.
    BWs for redcap in unlicensed bands even for Rx UE needs update.
    Redcap in unlicensed bands needs to be specified with 1 RX REFSENS to fulfil the Rel-17 WID objective
    Redcap in V2X bands combos needs to be specified with limited channel bandwdith for RedCap Band and additional RF impact analysis needed when RedCap Band is 1 Rx /HD-FDD.
    Redcap in SUL bands combos needs to be specified with limited channel bandwidth for RedCap Band and additional RF impact analysis needed when RedCap Band is 1 Rx /HD-FDD.
Proposal:
  Go one step further than the RAN#93e agreement and clarify that the following bands/features will be clearly identifiable in the specs as not applicable for RedCap UE in Rel-17:
    Redcap bands supporting V2X/PC5 on n47,
    Redcap operation in unlicensed band,
    Redcap bands supporting SUL.

## Slide 7: References
RP-212634, “Moderator's summary for discussion [93e-16-RedCap-WI] (for discussion in Friday GTW)”.