## Slide 1: Detailed Scope for Potential RAN R18 Items
Source: RAN Chair
3GPP RAN#94-e
December 6th – 17th, 2021

## Slide 2: Details Scope for potential RAN R18 Projects
The detailed scope for potential RAN R18 projects is provided in the sequel, to be used to for further discussion during the meeting
  The scope is based on the Oct. email discussion, with modifications for the purpose of proper load-dimensioning, necessary clarification, etc.
The goal to finalize the corresponding SIDs/WIDs before the end of the meeting

## Slide 3: Detailed Scope of RAN1-led Projects

## Slide 4: RAN1-led: MIMO Evolution
Study, and if justified, specify CSI enhancement, and possibly CSI-RS enhancement in high/medium velocities for exploiting time-domain correlation/Doppler-domain information to assist codebook based CSI acquisition mechanisms for DL precoding
Specify extension of Rel-17 Unified TCI framework, e.g.,
  For indication of multiple DL and UL TCI states (e.g., M>1 and/or N>1, and inter-band) for multi-TRP and/or single-TRP schemes
Study, and if justified, specify larger number of orthogonal DMRS ports for uplink MU-MIMO (without increasing the UL DM-RS overhead)
Study, and if justified, specify enhancements of CSI acquisition (further clarification on the limited scope) for Coherent-JT for both FDD and TDD targeting FR1
Study, and if justified, specify overhead and/or Latency reduction for UE-initiated beam management/beam acquisition procedures
Study, and if justified, specify [at least] UL DMRS, SRS to enable 6 and 8 Tx UL operation to support more than 4 layers per UE in UL targeting CPE/ FWA/vehicle/Industrial devices
Study, and if needed, specify features to facilitate simultaneous multi-panel UL transmission for higher UL throughput/reliability
Study, and if justified, specify panel-specific timing/power control for UL multi-TRP/panel scenario
Study, and if justified, specify frequency-selective precoding targeting devices with >=4 Tx
Study, and if justified, specify 2 CW for >=2layers in uplink
For 1 & 4, it is critical to have a clear and a *very* limited scope for them to be possibly considered; otherwise, both will be dropped

## Slide 5: RAN1-led: Uplink Coverage Enhancements Evolution
Specify following PRACH coverage enhancements (RAN1, RAN2)
  Multiple PRACH transmissions with same beams targeting 4-step RACH [and 2-step RACH] procedures
  [Study, and if justified, specify PRACH transmissions with different beams targeting 4-step RACH [and 2-step RACH] procedures] for FR2
  Note: The enhancements of PRACH are targeting for FR2, which can also apply to FR1 when applicable.
  Note: The enhancements of PRACH are [format-agnostic and] targeting [for PRACH format B4, which can also apply to other] short PUCCH formats when applicable.
[Study and if necessary specify following power domain enhancements]
  [Enhancements to realize dynamic power aggregation based on Rel-17 RAN4 work on “Increasing UE power high limit for CA and DC”, with checking relevant regulations ([RAN1,] RAN4)]
    [Note: The study can start after RAN4 work on “Increasing UE power high limit for CA and DC” is done depending on conclusions from RAN4.]
  [Enhancements to reduce MPR/PAR, including new transmission mechanism such as spectrum shaping, [reduced spectrum utilization with relaxed requirements on channel filtering,] [and potential adjustments to MPR and test tolerance relations] (RAN4[, RAN1])]
Study and if necessary specify following enhancements for multi-carrier UL operation (moved to CA)
  UL Tx switching schemes across [more than 2] bands with restriction of 2 Tx simultaneous transmission for FR1 UEs, including mechanisms to enable more configured UL bands than its simultaneous transmission capability and to support dynamic Tx carrier switching across the configured bands (RAN1)
  Switching time and other RF aspects for above UL Tx switching schemes across [more than 2] bands (RAN4)
Alt.1: [Study and if necessary specify following enhancements for DFTS-OFDM (RAN1)]
    [Dynamic switching between DFTS-OFDM and CP-OFDM]
    [Multi-layer transmission with DFTS-OFDM, with considering LTE design]
    [Note: the study targets to select only one of above enhancements, unless necessity to specify both enhancements is justified in the study]
Alt.2: [Specify following enhancements for DFTS-OFDM (RAN1)]
    [Dynamic switching between DFTS-OFDM and CP-OFDM]

## Slide 6: RAN1-led: Additional topological improvements – smart repeater
Start with study item. RAN1 is the primary working group. Secondary working groups are RAN2, RAN3, and RAN4.
Study and identify which side control information below is necessary for smart repeaters including assumption of max transmission power including at least [RAN1, RAN2, RAN4]
  Beamforming information
  Timing information to align transmission / reception boundaries of smart repeater
  Information on UL-DL TDD configuration
  Power control information for efficient interference management
  ON-OFF information for efficient interference management and improved energy efficiency
Study the following aspect of smart repeater
  Identification and authorization of smart repeaters [RAN2, RAN3 (check the possibility of assumed architecture for smart repeater so that identification part for RAN3 may be removed)]
  RF requirements for smart repeater, including max transmission power and other applicable RF requirements [RAN4]
Focus Rel-18 smart repeater work on the following scenario / assumptions:
  Consider smart repeaters used for extension of network coverage on FR1 and FR2 bands Prioritize FR2 TDD deployments for both outdoor and O2I scenarios.
  For only single hop stationary smart repeaters
  Assuming smart repeaters are transparent to UEs
  Smart repeater can maintain the gNB-repeater link and repeater-UE link simultaneously
  Cost efficiency is a key consideration point for smart repeaters

## Slide 7: RAN1-led: Sidelink enhancements (excluding positioning and relaying)
For Rel-18 sidelink enhancement, start as a work item with a study phase for a subset of objectives.
  For the objectives subject to a study phase, RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of this work.
For sidelink enhancement, RAN1 is the primary working group. Secondary working groups are RAN2 and RAN4.
Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4] (This part of the work is to be started after RAN#98)
  Prioritize supporting LTE sidelink CA features for NR (i.e. SL carrier (re-)selection, synchronization of aggregated carriers, handling the limited capability, power control for simultaneous sidelink TX, packet duplication)
  At least for FR1 licensed spectrum and ITS band
    Whether or not to support sidelink CA for FR2 and/or unlicensed band is to be decided in RAN#98 after the relevant studies are done
  This feature is backwards compatible in the following regards
    Rel-16 UEs can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carriers on which they receive and transmit the corresponding sidelink HARQ feedback.
    Assuming this sidelink functionality would co-exist in the same resource pools as Rel-16/Rel-17 functionalities (e.g., no changes to reservations in SCI, etc.)

## Slide 8: RAN1-led: Sidelink enhancements (excluding positioning and relaying), Cont’d
Study and specify, if the necessary, support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only [RAN1, RAN2, RAN4]
  Evaluation methodology for sidelink operation on unlicensed spectrum
  Sidelink channel access mechanism for unlicensed spectrum based on regional regulation requirement and use the existing channel success schemes from NR-U as a starting point
    Reuse Rel-16 resource allocation mechanism as much as possible
  Required changes to NR sidelink physical channel structures and procedures to operate on unlicensed spectrum
    No specific optimizations for existing NR SL feature
  Frequency bands for the unlicensed spectrum in FR1 are 5GHz and 6GHz
  No specific optimizations for FR2 unlicensed spectrum
RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.
Study enhanced sidelink operation on FR2 licensed spectrum [RAN1, RAN2, RAN4]
  Work is limited to the support of sidelink beam management (including initial beam-pairing, beam maintenance, and beam failure recovery) by enhancing existing sidelink CSI framework and reusing Uu beam management concepts wherever possible.
RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.
Study mechanism(s) to enable for co-channel coexistence for LTE sidelink and NR sidelink including performance, necessity, feasibility, and potential specification impact if any [RAN1, RAN2, RAN4]
  Reuse the in-device coexistence framework defined in Rel-16 as much as possible
  RAN to determine in RAN#98 whether or not there is to be specification support in Rel-18 and if there is specification support, the scope of the work.

## Slide 9: RAN1-led: RedCap Evolution SI
6-month study (1 TU)
To further reduce the complexity/cost of RedCap devices, the following should be studied:
Study further UE complexity / cost reduction techniques based on Rel-17 evaluation methodology [RAN1]
  Consider network impact, compatibility operation in a cell supporting Rel-17 RedCap UEs, with Rel-17, coexistence of RedCap and non-RedCap UEs, UE impact, specification impact
  Potential solutions, which may complement each other, for reducing device complexity/cost are, e.g., focusing on:
    UE bandwidth reduction to 5MHz in FR1
      Including the possibility of relaxing UE processing timeline
    reduced the UE peak data rate.
      Including the possibility of relaxing UE processing timeline
    etc.

## Slide 10: RAN1-led: RedCap Evolution: the follow-up WI
Expected WID at RAN#97:
  Power saving/energy efficiency enhancements
  Enhanced eDRX in RRC_INACTIVE (>10.24s) [RAN2, RAN3, RAN4]
    Note that this objective requires SA2, CT1 involvement
  Complexity/cost reduction
  TBD based on SI outcome: Further reduced UE cost / complexity [RAN1]
  Support for lower UE power class [RAN4]
    Focus on non-coverage-limited scenarios, e.g., indoor industrial (i.e., no intention to specify any dedicated coverage recovery schemes)
  Notes:
  The work defined as part of this WI is not to overlap with LPWA use cases.
  Coexistence with non-RedCap UEs and Rel-17 RedCap UEs should be ensured.
  This WI focuses on SA mode and single connectivity with operation in a single band at a time.
  This WI considers all frequency ranges and all applicable duplex modes unless otherwise specified.

## Slide 11: RAN1-led: Low-Power WUS SI
The study should primarily target low-power WUS/WUR required by IoT use cases, i.e., power-sensitive, small form-factor devices such as industrial sensors or controllers. Other use cases are not precluded.
As opposed to the work on UE power savings in previous releases, this study will not require existing signals to be used as WUS. All WUS solutions identified shall be able to operate in a cell supporting legacy UEs fully backward compatible. Solutions should give justifiable gains compared to the existing Rel-15/16/17 UE power saving mechanisms. Aspects such as UE power consumption, detection performance, coverage, UE complexity, should be covered by the evaluation.
The study item includes the following objectives:
  Identify use cases, evaluation methodology & KPIs [RAN1]
  Study and evaluate low-power wake-up receiver architectures [RAN1, RAN4]
  Study and evaluate wake-up signal designs to support wake-up receivers [RAN1, RAN4]
  Study and evaluate L1 procedures and higher layer protocol changes needed to support the detection of wake-up signals [RAN2, RAN1]
  Study potential system impact, such as network power consumption, coexistence with non-low-power-WUR UEs, network coverage/capacity, latency, and gains compared to the existing Rel-15/16/17 UE power saving mechanisms [RAN1, RAN2]

## Slide 12: RAN1-led: Expanded and improved Positioning 1/1
9 month SI + 9 month WI
Study (for study phase of 9 months) solutions for sidelink positioning considering the following: [RAN1, RAN2]
  Scenario/requirements [Moderator comment: These could be moved to the justification section in the final WID]:
    Coverage scenarios to cover: in-coverage, partial-coverage and out-of-coverage
    Requirements: Based on requirements identified in TR38.845 and TS22.261 and TS22.104
    Use cases: V2X (TR38.845), public safety (TR38.845), commercial (TS22.261), IIOT (TS22.104)
    Spectrum: ITS, licensed, [unlicensed]
  Identify specific target performance requirements to be considered for the evaluation [RAN1]
  Define evaluation methodology with which to evaluate SL positioning for the identified uses cases and coverage scenarios, reusing existing methodologies from sidelink communication and from positioning as much as possible [RAN1].
  Study and evaluate performance and feasibility of potential solutions for SL positioning, considering: [RAN1, RAN2]
    Relative positioning, ranging and absolute positioning
    Study of positioning methods (e.g. TDOA, RTT, AOA/D, etc) including combination of SL positioning measurements with other RAT dependent positioning measurements (e.g. Uu based measurements) [RAN1]
    Study of sidelink reference signals for positioning purposes, including signal design, phy layer control signalling, resource allocation, physical layer measurements, associated physical layer procedures, etc [RAN1]
    Study of positioning architecture and signalling procedures (e.g. configuration, measurement reporting, etc) to enable sidelink positioning covering both UE based and network based positioning [RAN2, including coordination and alignment with SA2 as required]
    Recommend solutions, if any, to be specified in the normative phase [RAN1, RAN2]

## Slide 13: RAN1-led: Expanded and improved Positioning 2/2
Improved accuracy, integrity, and power efficiency:
  Study (for study phase of 9 months) solutions for Integrity for RAT dependent positioning techniques [RAN2, RAN1]:
    Identify the error sources, failure modes, [RAN1, RAN2].
    Study methodologies, procedures, signalling, etc for determination of positioning integrity for both UE-based and UE-assisted positioning [RAN2, RAN1]
  Study (for study phase of 9 months) and, if found beneficial, specify solutions for accuracy improvement based on PRS/SRS bandwidth aggregation for intra-band carriers[RAN1, RAN4, RAN2, RAN3]:
    RAN4 to consider implications of PRS/SRS bandwidth aggregation (e.g. timing errors, phase coherency, frequency errors, power imbalance, etc).
  Study (for study phase of 9 months and, if found beneficial, specify solutions for accuracy improvement based on NR carrier phase measurements [RAN1, RAN4, RAN2, RAN3]
    Reference signals, physical layer measurements, physical layer procedures to enable positioning based on NR carrier phase measurements for both UE-based and UE-assisted positioning [RAN1]
    Focus on reuse of existing PRS and SRS, with new reference signals only considered if found necessary
    Signalling for configuration and measurement reporting [RAN2, RAN3]
  Study (for study phase of 9 months) the requirements on LPHAP as developed by SA1 and evaluate whether existing RAN functionality can support these power consumption and positioning requirements. Based on the evaluation, and, if found beneficial, specify identify potential enhancements to help address any limitations [RAN2, RAN1]
Positioning support for RedCap UEs, considering the following:
  Evaluate positioning performance of existing positioning procedures and measurements with RedCap UEs[RAN1, RAN4]
  Based on the evaluation, assess the necessity of enhancements and, if needed, identify enhancements to help address limitations associated with for RedCap UEs [RAN1, RAN2]
  Define core and performance requirements for positioning measurements performed by RedCap UEs [RAN4]

## Slide 14: RAN1-led: Evolution of Duplex Operation SI
The objective of this study is to identify and evaluate the potential enhancements to support duplex evolution for NR TDD in unpaired spectrum. In this study, the followings are assumed:
  Duplex enhancement at the gNB side
  Half duplex operation at the UE side
  No restriction on frequency ranges
The detailed objectives are as follows:
  Identify applicable and relevant deployment scenarios and use cases (RAN1).
  Develop evaluation methodology for duplex enhancement (RAN1).
  Study the subband non-overlapping full duplex and potential enhancements on dynamic/flexible TDD (RAN1, RAN4)
    Identify possible schemes and evaluate their feasibility and performances (RAN1).
    Study inter-gNB and inter-UE CLI handling and identify solutions to manage them (RAN1).
      Study their impacts on inter-gNB interfaces if needed (RAN3).
      Consider intra-subband CLI and inter-subband CLI in case of the subband non-overlapping full duplex.
    Study the performance of the identified schemes as well as the impact on legacy operation assuming their co-existence in co-channel and adjacent channels (RAN1).
      Study the impact on RF requirements considering adjacent-channel co-existence with the legacy operation (RAN4).
    Study the impact on RF requirements considering the self-interference, the inter-subband CLI, and the inter-operator CLI at gNB and the inter-subband CLI and inter-operator CLI at UE (RAN4).
    RAN4 should be involved early to provide necessary information to RAN1 as needed and to study the feasibility aspects due to high impact in antenna/RF and algorithm design, which include antenna isolation, TX IM suppression in the RX part, filtering and digital interference suppression.
    Summarize the regulatory aspects that have to be considered for deploying the identified duplex enhancements in TDD unpaired spectrum (RAN4).
Note: For potential enhancements on dynamic/flexible TDD, utilize the outcome of discussion in Rel-15 and Rel-16 while avoiding the repetition of the same discussion.

## Slide 15: RAN1-led: AI (Artificial Intelligence)/ML (Machine Learning) for Air interface SI
Focus on a limited set of use cases
  CSI feedback enhancement, e.g., overhead reduction, improved accuracy, prediction [RAN1]
  Beam management, e.g., beam prediction in time, and/or spatial domain for overhead and latency reduction, beam selection accuracy improvement [RAN1]
  Positioning accuracy enhancements for different scenarios including, e.g., those with heavy NLOS conditions [RAN1]
  RS overhead reduction [RAN1]
  RRM Mobility, e.g., prediction in time or frequency for robustness, interruption and overhead reduction [RAN2]
Other details can be found in RP-212668 RP-212708

## Slide 16: RAN1-led: Network Energy Savings
The objectives of the study are the following:
  Definition of a network base station energy consumption model [RAN1]
    Adapt the framework of the power consumption modelling and evaluation methodology of TR38.840 to the network base station side, including relative energy consumption for DL and UL (considering factors like PA efficiency, number of TxRU, network load, etc), sleep states and the associated transition times, and one or more reference parameters/configurations.
  Definition of an evaluation methodology and KPIs [RAN1]
    The evaluation methodology should target for evaluating system-level network energy consumption and energy savings gains, as well as assessing/balancing impact to network and user performance (e.g. spectral efficiency, capacity, UPT, latency), energy efficiency, and UE power consumption/complexity. The evaluation methodology should not focus on a single KPI, and should reuse existing KPIs whenever applicable; where existing KPIs are found to be insufficient new KPIs may be developed as needed.
  Study and identify techniques on the gNB and UE side to improve network energy savings in terms of both BS transmission and reception [RAN1, RAN2, RAN3, [RAN4]]
The study should prioritize idle/empty and low/medium load scenarios (the exact definition of such loads is left to the study), and different loads among carriers and neighbor cells are allowed. (moving below to justification)The following example scenarios (mapping between scenarios and network loads is left to the study) including single-carrier and multi-carrier deployments are used as the starting point for discussion on prioritized scenarios for the study.
  Urban micro in FR1, including TDD massive MIMO (note: this scenario can also model small cells)
  FR2 beam-based scenarios (note: this scenario can also model small cells)
  Urban/Rural macro in FR1 with/without DSS (no impact to LTE expected in case of DSS)
  EN-DC/NR-DC macro with FDD PCell and TDD/Massive MIMO on higher FR1/[FR2] frequency
Note 1: legacy UEs should be able to continue accessing a network implementing Rel-18 network energy savings techniques, with the possible exception of techniques developed specifically for greenfield deployments.
The study should coordinate with SA5 and RAN4 as needed.

## Slide 17: RAN1-led: DSS
Study and if needed specify NR PDCCH reception in symbols with LTE CRS REs.
  Investigate the performance, and enabling LTE CRS to puncture NR PDCCH and how to interact with DMRS if there is the performance gain from the additional PDCCH resources.
  Specify necessary, if any, UE performance requirements for improvement of NR spectrum efficiency for LTE-NR co-existence
    Specify necessary UE demodulation performance requirements (RAN4)

## Slide 18: RAN1-led: CA enhancements
Specify a solution for multi-cell PUSCH/PDSCH scheduling (one PDSCH/PUSCH per cell) with a single DCI [RAN1]
  Identify the maximum number of cells that can be scheduled simultaneously
  Consider both intra-band and inter-band CA operation
  Consider both FR1 and FR2
  The single DCI shall be optimized for 3 or more cells for the multi-cell PUSCH/PDSCH scheduling
Study and if necessary specify following enhancements for multi-carrier UL operation
  UL Tx switching schemes across [3 or 4] bands with restriction of 2 Tx simultaneous transmission for FR1 UEs, including mechanisms to enable more configured UL bands than its simultaneous transmission capability and to support dynamic Tx carrier switching across the configured bands (RAN1)
  Switching time and other RF aspects for above UL Tx switching schemes across [3 or 4] bands (RAN4)
Introduce support for Scells without SSB in inter-band CA (so that an SSB in one band can provide DL timing/ frequency synchronization for an Scell in a different band), via the following steps:
  identify for which bands this is feasible and the related UE requirements [RAN4]
  introduce the related UE capability and signalling support [RAN2]
  Note: This aspect is expected to be implicitly/explicitly considered as part of network energy savings

## Slide 19: Detailed Scope of RAN2-led Projects

## Slide 20: RAN2-led: Mobility Enhancements
To specify mechanism and procedures of L1/L2 based inter-cell mobility for mobility latency reduction:
  Configuration and maintenance for multiple candidate cells to allow fast application of configurations for candidate cells [RAN2, RAN3]
  Dynamic switch mechanism among candidate serving cells (including SpCell and SCell) for the potential applicable scenarios based on L1/L2 signalling [RAN2, RAN1]
  L1 enhancements, including inter-cell beam management, L1 measurement and reporting, beam indication, and for non-synchronized scenario to handle TA management [RAN1, RAN2]
    Note: early RAN2 involvement is necessary, including the possibility of further clarifying the interaction between this bullet with the previous bullet
  CU-DU interface signaling to support L1/L2 mobility, if needed [RAN3]
  Note 1: FR2 specific enhancements are not precluded, if any.
  Note 2: The procedure of L1/L2 based inter-cell mobility are applicable to the following scenarios:
    Standalone, CA and NR-DC case with serving cell change within one CG
    Intra-CDU case and intra-CU inter-DU case (no new RAN interfaces are expected) (applicable for Standalone and CA)
    Both intra-frequency and inter-frequency
    Both FR1 and FR2
To specify mechanism and procedures of MR-DC with selective activation of the cell groups via L3 enhancements:
  To allow subsequent CPC/CPAC after changing SCG without reconfiguration and re-initiation of CPC/CPAC [RAN2, RAN3, RAN4]
  TBD: whether Rel-17 CPC/CPAC mechanism is used as the baseline
  TBD: whether to limit MR-DC to EN-DC and NR-DC  limit to NR-DC only
To specify CHO including target MCG and target SCG if it cannot be completed in Rel-17 [RAN3, RAN2]
To specify CHO including target MCG and candidate SCG for CPC/CPAC [RAN3, RAN2]
  CHO including target MCG and target SCG is used as the baseline

## Slide 21: RAN2-led: Enhancements for XR
9-month study for RAN1 and 6-month study for RAN2, followed by WI
  XR-awareness in RAN (RAN2):
    Study and identify the XR traffic (both UL and DL) characteristics, QoS metrics, and application layer attributes beneficial for the gNB to be aware of, e.g. [the QoS flow association, frame-level QoS, ADU-based QoS, XR specific QoS].
    Study how this information aids XR-specific traffic handling.
    Cooperation is needed with the corresponding study work of SA2 //add latest SA2 reference
  XR-specific Power Saving (RAN1, RAN2)
    Study XR specific power saving techniques to accommodate XR service characteristics (periodicity, jitter, latency, reliability, etc...)
      C-DRX enhancement;
      PDCCH monitoring enhancement
  XR-specific capacity considerations (RAN1, RAN2)
    Study mechanisms that provide more efficient resource allocation and scheduling for XR services:
      Enhancement to SPS and CG;
      Enhancement for dynamic grants

## Slide 22: RAN2-led: Sidelink relay enhancements
Specify mechanisms to support single-hop Layer-2 and Layer-3 UE-to-UE relay (i.e., source UE -> relay UE -> destination UE) for unicast [and groupcast] [RAN2, RAN3, RAN4].
  Common part for Layer-2 and Layer-3 relay to be prioritized until RAN#98
    Relay discovery and (re)selection [RAN2, RAN4]
    Necessary signalling support for Relay and remote UE authorization [RAN3]
  Layer-2 relay specific part
    UE-to-UE relay adaptation layer design [RAN2]
    Control plane procedures [RAN2]
    QoS handling if needed, subject to SA2 progress [RAN2]
  Note 1A: This work should take into account the forward compatibility for supporting more than one hop in a later release.
  Note 1B: A remote UE is connected to only a single relay UE at a given time. and the relay (re)selection criterion is the same in uncast and groupcast.
Specify mechanisms to enhance service continuity for single-hop Layer-2 UE-to-Network relay for the following scenarios [RAN2, RAN3]:
  Inter-gNB indirect-to-direct path switching (i.e., “UE 1 <-> relay UE A <-> gNB X” to “UE 1 <-> gNB Y”)
  Inter-gNB direct-to-indirect path switching (i.e., “UE 1 <-> gNB X” to “UE 1 <-> relay UE A <-> gNB Y”)
  Intra-gNB indirect-to-indirect path switching (i.e., “UE 1 <-> relay UE A <-> gNB X” to “UE 1 <-> relay UE B <-> gNB X”)
  Inter-gNB indirect-to-indirect path switching (i.e., “UE1 <-> relay UE A <-> gNB X” to “UE1 <-> relay UE B <-> gNB Y”)
Note 2A: Scenario D is to be supported by reusing solutions for the other scenarios without specific optimizations.
Study the benefit and potential solutions for multi-path support in Layer-2 and Layer-3 UE-to-Network relay to enhance reliability and throughput (e.g., by switching among or aggregating the multiple paths) in the following scenarios [RAN2]:
  * A UE is connected to the same gNB using one direct path and one indirect path via 1) layer-2/layer-3 UE-to-Network relay, or 2) via another UE (where the UE-UE inter-connection is assumed to be ideal), where the solutions for 1) are to be reused for 2)
Note 3A: Study on the benefit and potential solutions are to be completed in RAN#98 which will decide whether/how to start the normative work
.[Support of SL DRX for sidelink relay operation if not done in Rel-17] [RAN2]
[Note 4A: This objective is to be checked in RAN#94e.]

## Slide 23: RAN2-led: NTN (Non-Terrestrial Networks) evolution, NR
(RAN4-led)
  Study and identify NTN bands (example band(s)?): Analysis of regulations and adjacent channel co-existence scenarios [RAN4]
  Specify Rx/Tx requirements for satellite BS and different VSAT UE class (not only 60 cm aperture) as appropriate for the identified example band [RAN4]
  Identify values for physical layer parameters chosen from the existing FR1 and FR2 sets (RAN4)
Have a 1-TU [6]-month study phase focusing on the following (there are more aspects in the email discussion)? (to derive clear & limited scope)
  Coverage
    Evaluate the coverage performance and identify the candidate channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1]
      VoIP and low-data rate services for commercial handset terminals
    Study, and if justified, specify NTN-specific repetitions enhancements beyond techniques covered in Rel-17 CovEnh WI for the relevant channels [RAN1]
    Study, and if justified, specify NTN-specific techniques for improved diversity and/or reduced polarization loss [RAN1]
    Study, and if justified, improve the performance of low-rate codecs in link budget limited situation including reducing RAN protocol overhead for VoNR [RAN2] [Liaise with SA2/SA4 as necessary]
      NOTE: Intent is to optimize the RAN to work with the lowest rate codec currently available and will not introduce a new codec.
  Network verified location
    Study detailed regulatory requirement for network-verified UE location, e.g. accuracy requirement (at RAN plenary, from RAN#95 to RAN#96)
    Study and evaluate solutions for network to verify UE reported location information [RAN1]
      For Network based UE location, re-use of Rel-17 UE-specific Timing Advance report can be considered as baseline

## Slide 24: RAN2-led: NTN (Non-Terrestrial Networks) evolution, IoT
IoT-NTN Performance Enhancements in Rel-18 to address remaining issues from Rel-17
  Disabling of HARQ feedback to mitigate impact of HARQ stalling on UE data rates [RAN1,RAN2]
  Study and specify, if needed, improved GNSS operations for a new position fix for UE pre-compensation during long connection times and reduced power consumption [RAN1]
Mobility enhancements
  Enhancements on RLF and RRC reestablishment, e.g., conditional RRC reestablishment. [RAN2]
  Support of neighbor cell measurements and corresponding measurement triggering before RLF. This may include legacy (Rel-17) [RAN2]
  Solutions introduced in Rel-17 NR NTN for mobility enhancements (e.g. location-based CHO and timing-based CHO) for eMTC [RAN2]
  [NB-IoT carrier selection based on the coverage level, and associated carrier specific configuration] [RAN1, RAN2]
Further enhancement to discontinuous coverage
  Efficient power saving mechanisms (e.g., eDRX/PSM) for sparse satellite constellations [RAN2]
  Improvements to UE mobility among sparse cells [RAN2]
  Enhancements in RRC reestablishment or recovery based on the discontinuity of coverage
  [Further power saving enhancements for IoT NTN to support discontinuous coverage including PUR for NGSO (2nd priority)] [RAN2]

## Slide 25: RAN2-led: Evolution for broadcast and multicast services
Specify the enhancements of SFN for [inter-DU and inter-CU] scenario based on existing numerology and Cyclic Prefix [RAN3]
  [Study and specify mechanism to support coordination and synchronization across gNBs/DUs for SFN [RAN3]]
Specify support of multicast reception by UEs in RRC_INACTIVE [and RRC_IDLE] states [RAN2, RAN3, RAN1?]
  PTM configuration for UEs receiving multicast in RRC_INACTIVE [and RRC_IDLE] states [RAN2, RAN1?]
  Study this impact of mobility and state transition for UEs receiving multicast in RRC_INACTIVE [and RRC_IDLE states] [(Seamless/lossless mobility is not required)] [RAN2, RAN3]
Study and if necessary, specify enhancements to improve the resource efficiency for MBS reception in RAN sharing scenarios [RAN3]
[Specify signalling enhancements for improved support of Free-To-Air (FTA) / Receive Only Mode (ROM), i.e. ‎including UE capability related assistant information report regarding simultaneous reception of ‎FTA / ROM and unicast services provided by the same or different operator [RAN2]]
[(Low priority) Specify enhancements of power saving mechanism for MBS [RAN2, RAN1]]

## Slide 26: RAN2-led: UAV
Specify the following enhancements on measurement reports [RAN2]:
  UE-triggered measurement report based on configured height thresholds
  Reporting of height, location and speed in measurement report
  Flight path reporting
  Measurement reporting based on a configured number of cells (i.e. larger than one) fulfilling the triggering criteria simultaneously
Note: Work done in LTE is a starting point for this objective. NR-specific enhancements can be considered, if needed
Specify the signaling to support subscription-based aerial-UE identification [RAN3/SA2 interaction/RAN2]
Note: Work done in LTE is a starting point for this objective.
[Specify needed enhancements for broadcast of UAV identification [RAN2, RAN1, SA2 interaction]]
  Applicable to both LTE and NR
Note: This description is a placeholder for a more detailed objective to be drafted once SA2 will have concluded their study on the architectural aspects.
4. [Second priority] Study and, if needed, specify additional trigger condition(s) for CHO [RAN2].
5. [Second priority] Study and, if needed, specify the enhancements on beam management, with the following assumptions [RAN1, RAN4, RAN2]:
FR1 with directional antenna at UE side
gNB uptilt beamforming

## Slide 27: RAN2-led: Multiple SIM (MUSIM) Enhancements (WI)
9-month 1-TU WI
Enhancements for MUSIM procedures to operate in RRC_CONNECTED state simultaneously in NW A and NW B. [RAN2, RAN3, RAN4].
  Specify mechanism to indicate preference on temporary UE capability restriction (e.g. capability update, release of cells, (de)activation of configured resources) with NW A when UE prefers to start/stop connecting to NW B for MUSIM purpose
  RAT Concurrency: Network A is NR SA (with CA) or NR DC. Network B can either be LTE or NR.
  Applicable UE architecture: Dual-RX/Dual-TX UE
The work item shall identify whether the WI will have RAN3 or RAN4 impacts by RAN#99 [RAN2].

## Slide 28: RAN2-led: In-Device Co-existence (IDC) Enhancements
9-month 1-TU WI
This WI expects to address Interference between 3GPP (including various MR-DC architectures, i.e. NR-DC and EN-DC) and other RAT (e.g. WiFi).
  Prioritize enhancements to FDM solution, to allow more granular indication of affected frequencies (e.g. granularity of BWP or PRB level). (RAN2)
  Introduction of TDM solution (e.g. indication of UE preferred TDM pattern for UL/DL). (RAN2).
  Note: The TDM solution is considered complementary to the FDM solution
  Note: LTE should be considered a baseline for the solutions developed in this WI.

## Slide 29: SDT: RAN2-led
Target a 6-month project (WI)
Specify the support for paging-triggered SDT (MT-SDT) [RAN2, RAN3]
  MT-SDT triggering mechanism for UEs in RRC_INACTIVE, supporting RA-SDT and CG-SDT as the UL response;
  MT-SDT procedure for initial DL data reception and subsequent UL/DL data transmissions in RRC_INACTIVE.

## Slide 30: Detailed Scope of RAN3-led Projects

## Slide 31: RAN3-led: Additional topological improvements – IAB
Focus on the mobile-IAB-nodes mounted on vehicles scenario providing 5G coverage/capacity enhancement to onboard and/or surrounding UEs
  It is FFS whether to reference to use cases in TS22.261
Requirements (to be considered also for objectives description)
  Solutions should apply to FR1 and FR2 including In-band and out-of-band backhauling
  Solutions should be limited to a single hop backhauling, i.e. one hop between UE and the mobile IAB-node (i.e. no descendant node). It is FFS whether The mobile IAB node can connect to a one hop or a multiple hop IAB network of stationary parent/ancestor nodes
  Solutions should support UE HO and DC. It is FFS whether further clarifications are needed
It is proposed to wait for further progress in other WGs (e.g. SA2) on VMR. If such discussions conclude before the start of Rel18, a WID modification can be pursued to include support for the VMR use case in the WI (if agreeable). If such discussions do not conclude before the start of Rel18, it can be decided whether a SI on VMR needs to be started in RAN WGs.
Objectives:
  Define Procedures for migration/topology adaptation to enable IAB-node mobility [RAN3, RAN2]
  Enhancements for mobility of an IAB-node together with its served UEs. It is FFS whether No optimization to target serving surrounding UEs [RAN3, RAN2]
    Note: Solutions should avoid to touch upon topics where Rel17 discussions already occurred and where the topic was excluded from Rel17.
  Mitigation of interference due to IAB-node mobility, including the avoidance of reference and control signal collisions (e.g. PCI, RACH). If is FFS whether RAN2 or RAN3 should be leading the activity
  RAN4 should be involved to study impact on e.g. RRM, demodulation and coexistence is taken into account and addressed. RAN1 may be involved, depending on work progress.

## Slide 32: RAN3-led: AI/ML for NG-RAN – Email Discussion
Target a 2-TU 12-month WI
  Possible continuation of NG-RAN AL/ML SI for more new use cases can be revisited later (target 6-month)
Specify data collection enhancements and signaling support within existing NG-RAN interfaces and architecture (including non-split architecture and split architecture) for AI/ML-based Network Energy Saving, Load Balancing and Mobility Optimization. (RAN3)
Note: On security impacts, coordination with SA3 when needed. On OAM aspects, coordination with SA5 when needed.
Editor’s Note: The objectives and any other involved working groups are subject to further refinement when the Rel-17 SI is completed.

## Slide 33: RAN3-led: SON/MDT Enhancements
1-TU project
Support of data collection for SON features, including “left-over” features (i.e. MR-DC CPAC and MRO successful PScell change report, fast MCG recovery, NR-U) and MRO enhancement for inter-system handover voice fallback [RAN3, RAN2]
  Specification of the UE reporting necessary to enhance the mobility parameter tuning [RAN2].
  Specification of the inter-node information exchange, including possible enhancements to interfaces [RAN3]
Support of SON/MDT enhancements for RACH enhancements, NPN. [RAN3, RAN2]
If needed, co-operate with RAN1, SA2, SA5, CT4.
Editor’s Note1: Details of Rel-17 leftover could be further refined when the Rel-17 SON/MDT WI finishes.
Editor’s Note2: Whether to include LTE MDT improvement (UE’s height location) can be decided later based on R17 progress in RAN2.
Editor’s Note3: More Rel-16/17 new features are not precluded in this WI which can be decided later after Rel-17 SON/MDT WI finishes.

## Slide 34: RAN3-led: QoE Enhancements
Support for new service type, such as AR, MR, MBS and other new service type defined or to be supported by SA4, also combined with high mobility scenarios e.g., High Speed Trains. Support RAN-visible parameters for additional service types, and the coordination with SA4 is needed[RAN3, RAN2].
Specify for QoE configuration, measurement collection and reporting in RRC_INACTIVE, RRC_IDLE and RRC_CONNECTED state for MBS broadcast service, in collaboration with SA4[RAN3, RAN2].
  Specify the QoE measurement configuration, collection and reporting, including both legacy QoE and RAN visible QoE.
  Specify the mechanism to support the alignment of the existing radio related measurement and QoE reporting.
Specify to support for QoE in NR-DC[RAN3, RAN2].
  Specify the QoE configuration, measurement reporting over MN/SN for NR-DC architecture, and specify the QoE measurement reporting over the other DC leg when the network node configured with receiving the reports is overload (is it already supported currently? If so, this bullet can be removed)
  Note 1: The QoE measurements are not perform for per-leg.
  Support RAN-visible and radio related measurement configuration and reporting in NR-DC scenarios.
  Specify the QoE measurement continuity in mobility scenarios in NR-DC.
  Specify the alignment of QoE and radio related measurements in NR-DC.
Left-over features which are not included in Rel-17 normative phase[RAN3, RAN2].
[Support the continuity of QoE measurement job during inter-system or inter-RAT handover process] [RAN3, RAN2].
Note2: If there are any left-over issues in R17, these features may be supported to continue to complete them in R18 to ensure that the QoE feature is stable and useful. The details could be decided by the end of Rel-17 NR QoE WI.
Note3: If needed, co-operate with other working groups, e.g. SA4/SA5/SA2/CT1.
Note4: Radio related measurement report should be specified in the SON/MDT WI.

## Slide 35: Detailed Scope of RAN4-led Projects

## Slide 36: RAN4-led: bandwidths lower than 5 MHz in dedicated spectrum
Identify and specify necessary changes to NR physical layer with minimum impact to operate in spectrum allocations from approximately 3 MHz up to below 5 MHz [RAN1]:
  Restrict to subcarrier spacing of 15kHz and the use of normal cyclic prefix.
  For SSB:
    Reuse PSS/SSS specification without puncturing.
    PBCH based on current design [while minimizing performance degradation]
  Identify and specify necessary minimum changes to PDCCH, CSI-RS/TRS, PUCCH, and PRACH for functional support without optimization
Specify necessary RAN4 requirements to support deploying NR in dedicated spectrum allocations from approximately 3 MHz up to below 5 MHz [RAN4]:
  The dedicated spectrum in this WI include RMR-900 band, n8, n26 and n28.
  Specify system parameters (including channel and sync rasters) for the associated dedicated spectrum.
  Minimize impact on RF requirements:
    Reuse 5 MHz channel bandwidth at least for FRMCS use case (assuming co-located NR and GSM-R with same operator).
    Specify the required RF requirement for 3 MHz channel bandwidth in bands: RMR 900 (874.4 - 880 MHz/919.4 MHz – 925 MHz), n8, n26 and n28.
  Specify RRM requirements while minimizing specification impact to support operation in dedicated spectrum allocations from approximately 3 MHz up to below 5 MHz.