## Slide 1: Summary of [94e-18-R18-NTN-IoT]
MediaTek Inc. (Moderator)
3GPP TSG RAN 94E RP-213537
December 6th-17th, 2021 Agenda Item 8A.2

## Slide 2: Intermediate Phase [1/2] Proposals
Objective 1: Performance Enhancements
  Disabling HARQ Feedback:
  Proposal 7: Stick to the original wording in RP-213469’s appendix i.e. “Disabling of HARQ feedback to mitigate impact of HARQ stalling on UE data rates [RAN1,RAN2]”. Conclude the discussion.
  Other: stable
Objective 2: Mobility Enhancements [1/2]
  Rel-17 NR NTN for mobility enhancements (e.g. location-based CHO and timing-based CHO) for eMTC [RAN2]
  Mixed views expressed whether to keep the objective or not, whether to keep “e.g.” or expand the list
  Moderator view: two options
      Remove the objective altogether
      [Default] Keep the objective as originally phrased i.e. “Solutions introduced in Rel-17 NR NTN for mobility enhancements (e.g. location-based CHO and timing-based CHO) for eMTC [RAN2]”
  Proposal 8: The Moderator proposes a decision be made in GTW between a) and b) (The Moderator expects falling back to b) (i.e. as in RP-213469’s appendix) may be the default option).

## Slide 3: Intermediate Phase [1/2] Proposals
Objective 2: Mobility Enhancements [2/2]
  Support of neighbor cell measurements and corresponding measurement triggering before RLF. This may include legacy (Rel-17) [RAN2]
  Clarification required on this
  Proposal 9: Support of neighbor cell measurements and corresponding measurement triggering before RLF, using Rel-17 (TN) NB-IoT, eMTC as a baseline. This may include legacy (Rel-17) [RAN2]
Objective 3: Discontinuous Coverage
  Conclusion:
    An objective placeholder for Further enhancements for Discontinuous Coverage (without any sub-objective) is confirmed including a NOTE to revisit the status on Rel-17 discontinuous coverage in RAN2, SA#94e and CT#95e, at RAN#95e.

## Slide 4: Intermediate Phase [1/2] Proposals
RAN4 Core&Perf Requirements
  Conclusion:
    RAN4 parts for the Rel-17 IoT NTN WI and RAN4 parts for the Rel-18 IoT NTN WI will be discussed at RAN#95e
      Whether a single or separate WI will be used is for discussion and decision at RAN#95e
    RAN4 parts for the Rel-18 IoT NTN WI will not be included in the Rel-18 IoT NTN WI at this RAN#94e plenary
    For consistency RAN4 responsibility is removed from the Rel-18 IoT NTN WI for the time being. This will be revisited at RAN#95e as per the above.
Conclusion of Intermediate Phase: Updated WID:
  The moderator has updated the WID (see blue highlights) in the inbox/drafts/[94e-18-R18-NTN-IoT] folder
  See r02 MOD

## Slide 5: Appendix Initial phase summary
See also RP-213494

## Slide 6: Initial Phase [1/2] Proposals
Proposal 1: Justification: The Moderator proposes to park the discussion on the justification (unless objectives change drastically)
Proposal 2: Performance Enhancements: The Moderator recommends to confirm the objectives on Disabling HARQ feedback and Improved GNSS operation (with minor wording clarification to avoid confusion). The Moderator proposes not to expand the scope at this stage.
Proposal 3: Mobility Enhancements: The Moderator proposes:
  To reinstate the ”RLF” in the first sub-objective
  To keep the parenthesis on CHO but to remove the ”e.g.”
  To confirm the removal of [NB-IoT carrier selection based on the coverage level and associated carrier specific configuration] [RAN1, RAN2]

## Slide 7: Initial Phase [2/2] Proposals
Proposal 4: Discontinuous Coverage: The moderator proposes to keep an objective placeholder for Further enhancements for Discontinuous Coverage (without any sub-objective) with a NOTE to revisit the status in RAN#95e
Proposal 5: Store and Forward operation: The moderator proposes that no objective be added to the scope of the WID. The Moderator proposes to close this debate
Proposal 6: RAN4 requirements: The Moderator proposes that handling of the RAN4 part be discussed alongside the proposal to this meeting (RP-213361) to define the RAN4 core&perf requirements for Rel-17 IoT-NTN, as these two discussions are interrelated as already indicated in the draft WID §4.2.
Conclusion of initial Phase: Updated WID: The moderator has updated the WID (see blue highlights) in the inbox/drafts/[94e-18-R18-NTN-IoT] folder

## Slide 8: Thank You!