## Slide 1: [95e-13-RAN4-R18-NonColloc] Summary of Extended discussion
Moderator(KDDI)
3GPP TSG RAN Meeting #95-e
Electronic Meeting, March 17 - 23, 2022
Agenda Item: 9.1.4.6
Document for: Discussion
RP-221004
(Revision of RP-220873)

## Slide 2: Summary of Extended discussion (1/2)
The core part of the work item includes:
Phase I:
  Study the feasibility to support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA except for 2-layer case of EN-DC already specified in Rel-16 and Rel-17.
    Investigate the tolerable power imbalance between carriers
    Investigate the required arrival time difference between CCs
    Evaluate the UE performance under the power imbalance and arrival time difference
      Discuss and decide reference UE architecture considering the UE capability of interBandMRDC-WithOverlapDL-Bands-r16 for 2-layer MIMO case for NR-CA, and 4-layer MIMO case for both EN-DC/NR-CA
    Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78
    Investigate whether the power imbalance should be explicitly (e.g. as an RF requirement) or implicitly specified (e.g. through a demodulation performance test). Specify the power imbalance based on the outcome of the investigation.
    If any change in RAN1 or RAN2 spec is needed, it will be triggered by RAN4 LS
    NOTE: Revisit whether or not to study the feasibility for support of 4Rx chains with up to 4-layer MIMO at RAN#97. This 4-layer is only for DL in Rel-18. And 4Rx chain with up to 2 layer MIMO for each CC is assumed as starting point.
    NOTE: Revisit whether or not to study the technical solutions can be applied to EN-DC case regardless of band contiguity at RAN#97.
Phase II:
  Phase II work will get started after the feasibility in phase I is confirmed
  Specify MRTD and MTTD requirements in non-collocated deployment
  Discuss and decide if the different requirements will be specified based on UE capability of interBandMRDC-WIthOverlapDL-Bands-r16.

## Slide 3: Summary of Extended discussion (2/2)
The performance part of the work item includes:
Phase II:
  Phase II work will get started after the feasibility in phase I is confirmed
  Specify PDSCH demodulation requirements for non-collocated scenarios for intra-band non-contiguous EN-DC and NR-CA
    Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
    Power imbalance between the carriers is limited
Moderator’s Proposal
Agree the current objectives shown in slide-2 and 3.

## Slide 4: Clarification scope of this WI
At the beginning of final round, the moderator proposed to study the scope of Rel-18 highlighted in following yellow part.
Red square part will be revisit at RAN#97.
Green square part can be triggered from at the beginning of Rel-18 RAN4.
 | Inter-band DC_42_n77/78 |  |  | Intra-band non-contiguous NR CA |  | 
 | RF (power difference) | RRM (MRTD) | Performance (Demod) | RF (power difference) | RRM (MRTD) | Performance (Demod)
Not support non-collocated scenario (Type 1) | Specified (6dB) | Specified | Specified | Specified (6dB) | Specified | Specified
Support non-collocated scenario with limitation of only supporting 2x2 in each CC (Type 2) | Specified in RAN4 #102e | Specified (interBandMRDC-WithOverlapDL-Bands-r16) | Not specified (will be specified in R16/R17) | Not specified | Not specified | Not specified
Support non-collocated scenario with supporting 4x4 in each CC (New type?) | Not specified | Not specified | Not specified | Not specified | Not specified | Not specified

## Slide 5: EOF