## Slide 1: Scenarios and Requirements for the IMT-2020 Evaluations
3GPP TSG-RAN Ad Hoc, Next Generation Access Barcelona, Spain, January 28 - 29, 2016 RPa160024

## Slide 2: Summary
Requirements on the new radio should
  1) Enable the usage scenarios outlined in the IMT vision, by the NGMN etc., including eMBB, mMTC, and URLLC
  2) Be verifiable
  3) Be reachable
In this contribution we discuss the requirements of the multi-company text proposal RPa160018, and find that
  1) The requirements were developed to enable the desired usage scenarios
  2) The evaluation methodologies and deployment scenarios are of reasonable scope and complexity
  3) The requirements are reachable, but with a significant effort

## Slide 3: Usage Scenarios
Principle: Map the IMT vision, and others, to a limited set of well-defined performance metrics and test in relevant scenarios

## Slide 4: Requirements I
Performance Measure | Requirement | Comment
Peak spectral efficiency | DL: 30 bps/Hz UL: 15 bps/Hz | 
Bandwidth | TBD | 
Peak data rate | DL: 20 Gbps UL: 10 Gbps | Peak data rates may not be reached at all frequencies and only in some usage scenarios.
Control plane latency | 10 ms | Detailed definition to be discussed
User plane latency, one-way | 1 ms | Based on IMT-Advanced definition.
Mobility interruption time | 0 ms | 
Mobility | Up to 500 km/h | 
TRP spectral efficiency | [3x IMT-A requirement] | Value depends on deployment scenario
User spectral efficiency at 5% percentile | [3x IMT-A requirement] | Value depends on deployment scenario
Area traffic capacity | Report value, no requirement | Spectrum and site density not in control of proponent.
User experienced datarate | Report value, no requirement | Spectrum and site density not in control of proponent.

## Slide 5: Requirements II
Performance Measure | Requirement | Comment
Connection density | 1,000,000 devices/km2 | Fulfilling a specific QoS
Coverage | 164dB coupling loss | Coverage for 160bps, for MMTC
Battery life | 10 years | 200B/day UL, 5Wh, as in TR 45.820
Reliability | 1-10-5 in 1ms | Mainly for URLLC
NW energy efficiency | Qualitative KPI (ffs.) | Consider evaluation by inspection, with optional quantitative evaluation
UE Energy efficiency | Qualitative KPI (ffs.) | 
Inter-system mobility | Yes | Support mobility with at least one other IMT system.
Bandwidth scalability | Yes | 
Spectrum flexibility | Yes | 
Support of wide range of services | Yes | 

## Slide 6: Deployment Scenarios
Deployment Scenario | Indoor Hotspot | Dense Urban | Rural | Urban Macro (optional)
Description and objective | Similar to indoor hotspot for IMT-Advanced, more TRPs. Show that high frequencies can be used indoors | Similar to urban macro-cell for IMT-Advanced, but more dense. Small cell layer added for data rate and area capacity. Show that high frequencies can be used in dense outdoor networks | Similar to rural macro-cell for IMT-Advanced. Show importance of lower frequencies for coverage | Characterized by continuous and ubiquitous coverage in urban areas.
ISD | 20 m (12 TRPs in 120x50 m) | 200 m for macro 3 outdoor micros per macro cell | 1732 m | 500 m
Carrier frequency | ~30 GHz or ~70 GHz | ~4 GHz and ~30 GHz | ~700 MHz or ~4 GHz | ~4 GHz
Bandwidth, DL+UL | 1GHz | 200 MHz at 4GHz 1 GHz at 30GHz | 20 MHz at 700 MHz 80 MHz at 4 GHz | 200 MHz
#Antenna elements BS / UE | 256 / 32 | 256 / 8 at 4 GHz 256 / 32 at 30 GHz | 64 / 4 at 700 MHz 256 / 8 at 4 GHz | 256 / 8

## Slide 7: Reachability
Technology components
Wider bandwidth, new numerology
Large number of antennas and processing
Multi-site and layer connectivity
Diversity in many dimensions
Signaling and control plane design
  Beam based
  System plane
Requirements
Datarates
Latencies
Area capacity
Spectral efficiency
Coverage
Reliability
Energy Efficiency
Feasible but challenging!

## Slide 8: Spectrum Efficiency
Possible to reach 3x IMT-Advanced requirements with large number of antennas and associated processing
Modelling of non-idealities important

## Slide 9: Energy Efficiency
Deserves great attention in design of new radio
Comprehensive evaluation quite complex
  Segment country from rural to dense urban.
  Characterize subareas with subscriber distributions, traffic models and 24h profiles, propagation characteristics, and deployment and system models.
  Run system level evaluations and log activity and power traces
  Map these to power consumption using power models for the equipment used in each area.
  Combine the results per area to an into a country-level energy efficiency metric
Large savings achievable, despite higher traffic
Key component is allowing efficient BS sleep
Proposal: check this, e.g. >95% silence when no traffic
See e.g., G.Auer et al., “How much energy is needed to run a wireless network?”, IEEE Wireless Communications, 2011

## Slide 10: Traffic density
Traffic density = site density x spectrum x spectrum efficiency
The SRIT proponent (3GPP) is only in control of means for spectrum efficiency
  Sites and spectrum provided by operators and regulators
It appears reasonable to ask proponents for means for decent spectrum efficiency improvements
Proposal: Evaluate spectrum efficiency and assess how much spectrum and what site density is required to reach certain traffic densities

## Slide 11: User Experienced Datarate
As for cell (TRP) spectral efficiency, it appears reasonable to ask proponents for means for decent cell-edge user spectrum efficiency improvements
Proposal: Evaluate cell-edge user spectrum efficiency and assess how much spectrum is required and at what traffic load (simultaneous users) the user experienced datarates are reached
As an option, evaluate with FTP traffic