## Slide 1: Technical Requirements for Next Generation Radio Access Technologies
AT&T
3GPP RAN Ad-Hoc – Next Generation Access
January 28-29, 2016; Barcelona, Spain

## Slide 2: Next Generation Radio Access Technologies HIGH LEVEL OBJECTIVES
Performance
Greater throughput
Lower latency
Ultra-high reliability
Higher connectivity density –IoT
Mobility on demand
Capabilities
Control a highly heterogeneous environment
Help ensure security, trust, identity, and privacy
Consistent user experience

## Slide 3: Next Generation Radio Access Technologies SPECTRUM REQUIREMEMTS (1 of 2)
5G RAT shall support mmWave as well as sub 6GHz spectrum:
L1 design (PHY) can be different for mmWave and sub 6GHz, but L2 and L3 (MAC/RLC/PDCP) design must be common between these two RATs to the extent possible.
5G RAT shall support all legacy spectrum currently supported by LTE (Rel 13) and new spectrum:
This includes licensed, unlicensed and shared licensed spectrum.
For unlicensed standalone operation the 5G RAT shall co-exist with other systems operating in the same spectrum on par with LAA operation for all scenarios and use cases.
For unlicensed standalone operation the 5G RAT shall co-exist with other systems operating in the same spectrum at least on par with LAA operation. For asynchronous sharing with another 5G RAT (e.g. inter-operator), spectrum sharing efficiency shall be improved over LAA
The 5G RAT shall support low overhead FD-MIMO operation in high mobility.
5G RAT shall support flexible system bandwidth at least on the physical data channels in increments of X MHz (X is FFS):
This is similar to Rel 12 NCT SI where on the physical data channel the number of resource blocks could be arbitrary as long as the system bandwidth is less that maximum system bandwidth.
The need for such requirement for the physical control channel is FFS.

## Slide 4: Next Generation Radio Access Technologies SPECTRUM REQUIREMEMTS (2 of 2)
The 5G PCell cannot be completely turned off in order to carry the control channels and support RRM measurements
The Sub 6GHz RAT shall support dynamic co-existence with LTE on same/overlapping spectrum:
Avoids the need for carving out large turn-around spectrum when deploying 5G in legacy spectrum.
This is to be supported ONLY on LTE SCell and not on PCell for LTE Release 10 – 13.
For LTE Release 14 and beyond whether this can be supported on LTE PCell is FFS.
This is to be supported on both the 5G PCell and SCell.
For example, the need for supporting this on 5G PCell has an impact on the RRM measurement design:
Support the ability to dynamically reconfigure the RRM measurement region.
Support Sub-band RRM measurement.

## Slide 5: Next Generation Radio Access Technologies FUNCTIONAL REQUIREMEMTS
The 5G RAT should support UE specific or radio bearer specific numerology and timing on the physical layer (vis-à-vis Network Slicing):
Whether this is dynamically configured, or semi-statically configured, or is static is FFS.
The 5G RAT shall support integration of backhaul and access and support multi-hop configuration:
Whether this is a L2 multi-hop or L3 multi-hop is FFS at this point. Possibly both should be evaluated.
The integrated backhaul shall support and be optimized for both the eS1 interface as well as the eX2 interface (see architecture diagram in companion contribution).
  The 5G RAT shall support dynamic TDD where the partition between DL-access, UL-access, DL-backhaul and UL-backhaul is dynamically configured.
  How the TDD frame structure is chosen to avoid eNB-eNB or UE-UE interference is implementation specific. Could be done with some degree of coordination.

## Slide 6: Next Generation Radio Access Technologies THROUGHPUT REQUIREMEMTS
IMT-Advanced offered, per-user Peak Speeds of:
100 Mbps in high mobility situations
1 Gbps in low mobility situations
Next Generation Radio Technologies should offer at least 100 times greater throughput.

## Slide 7: Next Generation Radio Access Technologies SUMMARY of REQUIREMEMTS
In summary, it is proposed to add the following the TR on Performance & Technical Requirements:
The NG-RAT shall support mmWave as well as sub 6GHz spectrum.
The NG-RAT shall support all legacy spectrum currently supported by LTE (Rel 13) and new spectrum.
    This includes licensed, unlicensed and shared licensed spectrum.
    For unlicensed standalone operation the 5G RAT shall co-exist with other systems operating in the same spectrum on par with LAA operation for all scenarios and use cases.
The NG-RAT shall support flexible system bandwidth at least on the physical data channels in increments of X MHz (X is FFS).
    The need for such requirement for the physical control channel is FFS.
The Sub 6GHz RAT shall support dynamic co-existence with LTE on same/overlapping spectrum.
    This is to be supported ONLY on LTE SCell and not on PCell for LTE Release 10 – 13.
    For LTE Release 14 and beyond whether this can be supported on LTE PCell is FFS.
    This is to be supported on both the 5G PCell and SCell.
The NG-RAT should support UE specific or radio bearer specific numerology and timing on the physical layer (vis-à-vis Network Slicing).
The NG-RAT shall support integration of backhaul and access and support multi-hop configuration.
  The NG-RAT shall support dynamic TDD where the partition between DL-access, UL-access, DL-backhaul and UL-backhaul is dynamically configured.
  The NG-RAT should offer at least 100 times greater throughput than LTE-Advanced.

## Slide 8: THANK YOU