## Slide 1
Long Distance Coverage:
Requirement for next generation access
Telstra, Sprint, Orange, Telefónica, AT&T, Telus, Rogers, C-Spire, SouthernLINC, Bell Mobility
RPa160004

## Slide 2: Purpose and motivation
We propose that cell range beyond 100 km be included as a requirement for next generation access
  We provide wording to be included in the draft TR for Scenarios and Requirements for Next Generation Access Technologies
Motivation
  Support extreme coverage scenarios in rural and remote areas
  Expand capability of ultra low cost networks for low density and low ARPU areas
  Provide coverage at sea for maritime industries, for example fishing and oil exploration
  Provide greater reach for air to ground use cases

## Slide 3: Text proposal
The following text should be added to section 6.1 (Deployment scenarios for eMBB)
6.1.x Extreme Rural
The extreme rural and ultra-low cost scenario focuses on very large cells in remote locations. The key characteristics of this scenario are very wide area coverage supporting basic services with modest traffic load. This scenario will therefore be noise-limited using macro cells. Cellular layout in the RAN will be ad hoc and / or isolated.
Some of its attributes include:
• Carrier frequency: below 3 GHz
• Network layout: ad hoc / isolated
• 150 km for bands above 1GHz
• 250 km for between 700 MHz and 1 GHz
• 400 km or more for bands below 700 MHz
The following text should be added to section 7.2 (Deployment scenario specific requirements)
7.2.x Coverage
Standard cell range shall be supported up to 100 km propagation distance. It shall be possible to define an extended cell range to suit extreme rural and ultra-low cost coverage scenarios in which propagation distances in excess of 200 km are supported. Extended range capability may require the sacrifice of capacity in the eNB, but shall be readily supportable by all devices.
[Values for relevant deployment scenario(s)]

## Slide 4
Further Commentary

## Slide 5: Telstra’s experience with long distance coverage
We’ve demonstrated WCDMA coverage beyond 200 km in Australia
  “Outback” locations with expansive, flat, uncluttered environments
  Proprietary techniques applied to the network
We think extended range coverage is applicable to most countries
  We see frequent use at sea – maritime industries really appreciate long distance coverage
  We also see use by light aircraft
Many countries with a coastline and / or an interest in aviation!

## Slide 6: Technology options to support long distance coverage
Long distance coverage is only required for certain use cases
  Typically only required for low band frequencies (<3 GHz) understanding that frequencies >1 GHz may not have as much coverage as lower frequencies (ATG may be interested in higher frequencies)
  Typically not required in built-up areas
We can typically trade-off long distance coverage with capacity
  Will almost certainly need to give up some capacity to support long distance
  Sites requiring long distance coverage do not typically have high capacity needs
Address long distance coverage as an aspect of flexible numerology
  Long distance coverage typically limited by uplink timing and frame structure
  Allow these to be modifiable to support greater distance

## Slide 7: Suggested specific requirements in support of long distance coverage
We suggest consideration for target maximum distances as follows
  150 km for bands above 1 GHz
  250 km for between 700 MHz and 1 GHz
  400 km or more for bands below 700 MHz
Fully functional physical layer
  Long distance carrier shall be fully functional as for a standard range carrier (albeit with less capacity)
Full interoperability with standard range carriers and other RATs
  Support handover with standard range carriers, both intra- and inter-frequency; also inter-RAT