## Slide 1: Non-eMBB enhancements for Rel-18 Considerations on 3GPP Release 18 for Content Distribution
EBU input to 3GPP Release 18 Workshop, June 2021

## Slide 2
Unified Service Layers are vital
  Alignment between broadcast and unicast (Internet) protocols for media delivery
    Potential role of initiatives such as DVB-I for extension to Rel-18
  Service continuity between broadcast/unicast
    Seamless usage of LTE-based 5G Terrestrial Broadcast and (NR) unicast
This is a collection of ideas around service requirements and enhancements presented by individual EBU members
General Points

## Slide 3
Service Requirements
  Connection of EnTV RAN (FeMBMS) to 5G Core
    Enables MNOs to make use of EnTV features (in addition to Broadcast Network Operators)
  Public Warning capability
    Operation independent of unicast (receive-only broadcast)
    Study the applicability of existing MNO-centric 3GPP systems (e.g. ETWS/PWS/CMAS?)
    Consider support of other signalling mechanisms available in existing broadcast systems
      e.g. DAB/FM-RDS traffic announcements
  Support for low-latency streaming
    CMAF, look at applicability of e.g. ROUTE compared with FLUTE.
  Specification of a minimum set of audio/video codecs on UEs
    Negotiation of capabilities not possible in a downlink-only scenario
    Codec support in hardware ensures best performance
New Features/Technical Enhancements
  Efficiency enhancements
    e.g. Time Interleaving, MIMO (existing antennas/RF stages in handsets), Overhead Reduction
5G Broadcast: LTE-based 5G Terrestrial Broadcast

## Slide 4
5MBS: 5G Multicast/Broadcast
  Seen as having a role to optimise delivery over existing mobile networks if/where there are capacity constraints
  Service Requirements
    Universal Access
      Receive-only mode/Free-to-air for 5MBS
      Examine alternative approaches (multicast/broadcast and unicast)
        e.g. 5G Networks Providing Access to Localized Services (FS_PALS)
    Extension of EnTV Service Layer to 5MBS
      If not completed in Release 17
  New Features/Technical Enhancements
    Efficiency enhancements
      Physical Layer Time Interleaving, non-orthogonal techniques (e.g. BMUST)
      Considerations on backwards compatibility essential
Unicast Coverage
  Service Requirements
    Study applicability of techniques to enhance cell coverage for media delivery
      Release 17 Coverage Enhancements, NB-IoT, NR RedCap?
      Delivery of radio (audio) services and streams in rural areas
5G for Media Distribution over Mobile Networks