## Slide 1: Challenges of XR in Rel-18
Agenda Item: 4.2
Source: FGI, Asia Pacific Telecom
Document for: Discussion
3GPP TSG RAN Rel-18 workshop RWS-210191
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Justification
[background/observation] eXtended Reality (XR) and cloud gaming are the important 5G media applications that are under consideration in NR.
[use case/scenario] XR SID concluded to consider at least the following XR applications.
  VR1: Viewport dependent streaming
  VR2: Split Rendering: Viewport rendering with Time Warp in device
  AR1: XR Distributed Computing
  AR2: XR Conversational
  CG: Cloud Gaming

## Slide 3: Issues/Challenges
Power consideration
  There is a mismatch between XR DL traffic arrival periodicity and DRX monitoring periodicity.
  XR applications involves frequent UL and DL transmissions. Unaligned UL and DL could lead to extra power wastage.
  If there is a jitter in a DL XR traffic, the UE may not be able to receive the DL XR traffic during DRX on state.
Capacity consideration
  XR devices have higher throughput, higher reliability, and lower latency requirements as compared with eMBB devices. Current NR cell supports very limited XR users.
Mobility and coverage consideration
  XR devices have high throughput, low latency, and high reliability requirements. Minimizing user experience degradation in the presence of mobility or at the cell edge is required.

## Slide 4: Objectives (1/2)
To resolve the identified issues/challenges, the following aspects should be studied:
Power consideration
  Enhancement on power saving mechanism for XR traffic
    Adjustment of DRX periodicity to match XR DL traffic arrival periodicity.
    Dynamic adaptation of DRX parameters to realign the UE’s DRX periodicity with XR DL traffic arrival periodicity.
  Alignment of UL and DL transmission for XR applications
    Alignment of UL and DL transmission with DRX state.
  Mechanisms to handle jitter in a DL XR traffic
    Mechanisms to wake the UE up on time upon arrival of DL XR traffic.
    Dynamic adaptation of DRX parameters to ensure the UE wakes up upon arrival of DL XR traffic.
Capacity consideration
  Mechanisms to improve system capacity for XR devices
    Reducing control signaling overhead via SPS/CG configuration enhancements.
      Other mechanisms can also be considered.

## Slide 5: Objectives (2/2)
Mobility and coverage consideration
  Mechanisms for mobility enhancements to reduce user experience degradation of moving XR devices
    Support of mobility events (e.g., handover) in the presence of CA, DC, and/or multiple TRP links to ensure the throughput is maintained.
  Mechanisms to minimize user experience degradation for cell edge XR devices
    Enhancement on duplication/repetition of XR packets for cell edge XR devices.
    Dynamic adaptation of L1 parameters for cell edge XR devices.
    Enhancement on SUL to improve the reliability of UL XR traffics for cell edge XR devices.

## Slide 6: Conclusion
In this contribution, the following aspects have been studied:
  Power consideration
  Capacity consideration
  Mobility and coverage consideration
Proposal #1: For XR applications, solutions for power consumption reduction, system capacity improvement, and user experience degradation reduction while moving or at cell edge should be studied in Rel-18.
Proposal #2: Support the following enhancements in Rel-18 for XR applications:
  Enhancement on DRX mechanism specifically for XR traffic
  Alignment of UL and DL transmission for XR applications
  Mechanisms to handle jitter in a DL XR traffic
  Mechanisms to improve system capacity for XR devices
  Mechanisms for mobility enhancements to reduce user experience degradation of moving XR devices
  Mechanisms to minimize user experience degradation for cell edge XR devices