## Slide 1: Enhancement for RAN slicing

## Slide 2: Motivation
In Rel-17, RAN slicing solutions are being discussed for the scenarios where all cells within a tracking area support the same slice availability.
  RAN2 aligns with SA2 assumption that support of slices in a tracking area is homogeneous for Rel-17 although RAN2 studied heterogeneous deployments during SI phase.
SA1 identified new use cases and new requirements in Rel-18.
  SA1 studied the enhanced supports for the network slice.
  SA1 is being discussed support of a UE’s access to a network slice when different types of restrictions apply (e.g. related to radio resources, frequency bands), with minimized interruption of services when there is a change of network slices or allocated resources.
  SA1 is also being discussed support of additional service exposure for 3rd party control/configuration of network slices.

## Slide 3: Motivation
In Rel-18, RAN should work on enhancements for RAN slicing to support new use cases and new requirements as follows.
  Multiple and different slices are supported on different frequencies or geographical area (regardless of tracking area).
  Restriction on simultaneously supported network slices at UE.
  Different users or services have different priority for the available network slices.
A mechanism to efficiently minimize power consumption (e.g., cell search, cell measurement) should be discussed considering different types of slice restrictions and priority.
  When usage of network slices is restricted depending on frequencies, geographical area or registration of other network slices, the UE does not need to search a cell supporting the network slices unused.
  It is beneficial for a UE to minimize power consumption for cell search where there is unused network slices.

## Slide 4: Potential enhancement
Support slice aware mobility when usage of network slices is restricted.
  Restriction is based on frequency, geographical area, timely-manner, simultaneous usage of network slices
  Consider both idle mode and connected mode mobility
Support power saving mechanisms based on slice priority and/or disjoint network slices information.
  RRM relaxation
  DRX optimization