## Slide 1: Motivation for new SI: Study on Carrier Phase Positioning
3GPP RAN-Rel-18 workshop
Electronic Meeting, June 28 – July 02, 2021
RWS-210285
Agenda Item: 4.2
DanKook University
Jaihyung Cho
Hyeon Woo Lee
jaihyung.cho@gmail.com
woojaa@dankook.ac.kr

## Slide 2
Introduction
Definition
  Carrier phase positioning method is the timing or distance measurement method using the wavelength of the carrier or subcarrier signal.
  Contrast to the "Code-phase" or RSTD (Reference Signal Time Difference) measurement method, the phase measurement method uses frequency domain signal phase estimation.
  Commercial GPS carrier phase product is already widely used and they provides centimeter level accuracy.
Figure 1 : Carrier / Subcarrier Based Positioning

## Slide 3
Motivation
and Justification
  TS22.261 and others require submeter-level positioning performance.
  GPS Carrier Phase, Bluetooth[6], etc. use the phase measurement base technology for providing centimeter level high accuracy positioning service.
  Such phase measurement based technology, compared to RSTD timing measurement, AoD/ZoD method defined in Release-17, may provide better accuracy and resource utilization when it is applied to 3GPP system.
  There are contributions [1][2][3][4][5] proposing use of the phase measurement for the improvement of 5G NR positioning, however, the feasibility and performance were not sufficiently studied in 3GPP.

## Slide 4
Objective
Objective
  It is necessary to study the achievable accuracy, resource consumption and efficiency, etc. that can be obtained by the carrier/sub-carrier phase based measurement method.
  Issues involving efficient method for phase measurement, solutions necessary to support various use cases, and required impact to the 3GPP system need to be studied.
  Not only for the enhancement in release-18 positioning, but some potential applications and improvement to other 3GPP functions (e.g Beam Direction Finding, gNB synchronization, etc) also need to be investigated.
  Criteria for performance evaluation and scenarios for comparison to release-17 positioning method need to be established.

## Slide 5
Scope of the Work
Feasibility study for phase based positioning
  Solutions for different frequency range (FR1/FR2) and wavelength
  Phase signal structure & harmonization with existing reference symbols (e.g PRS, SRS)
  Antenna configuration and signaling resource mapping suitable for various applications
    (e.g horizontal / vertical antenna spacing, co-located or distributed antennas)
  Uplink/downlink phase measurement for the cases of UE/network based positioning, etc.
  Effective multipath detection & mitigation method
    (e.g CIR based, eigen/singular decomposition based)
  Efficiency in terms of resource utilization and accuracy in various scenarios
    (e.g LoS/NLoS, stationary/mobile)
  Phase measurement based solutions for AoA / AoD / ZoA / ZoD
  Criteria for performance evaluation in various scenarios

## Slide 6
Scope of the Work
2) Feasibility study for gNB synchronization using the positioning signal
  Solutions for mitigating phase noise between multiple gNBs/TRPs
  Study on the requirement for structural impact
  Achievable timing accuracy and resource consumption, comparison to existing methods (such as PTRS)
Figure 2 : An Example for gNB synchronization using the phase signal

## Slide 7
Reference
[1] R1-2104844 , " Carrier Phase Based Downlink Angle of Departure Measurement " , Dankook University , RAN WG1 #105-e e-Meeting, May 10th – 27th, 2021
[2] R1-2104880 , " Carrier/Subcarrier Phase Based Enhancement for 5G NR Positioning " , Dankook University , RAN WG1 #105-e e-Meeting, May 10th – 27th, 2021
[3] R1-2003701 ," Potential positioning enhancements ", BUPT, ZTE, CAICT , RAN WG1 #101, e-Meeting, May 25th – June 5th, 2020
[4] R1-1903055 , " Carrier Phase enhanced potential solution for NR positioning schemes " , Fraunhofer IIS, Fraunhofer HHI, RAN WG1 Meeting 96 Athens, Greece, 25th February – 1st March, 2019
[5] R1-2103172 , " Potential Enhancements on DL-AoD positioning " , Qualcomm Incorporated , RAN WG1 #104b-e e-Meeting, April 12th – 20th, 2021
[6] Martin Wooley, "Bluetooth Direction Finding:A Technical Overview", Bluetooth SIG, Version 1.0.2, 22 Feb. 2021