## Slide 1: Mobile IAB (mIAB) in Release18
3GPP TSG RAN Rel-18 workshop RWS-210320
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: mIAB – A new IAB Use Case Motivation
Improving coverage (& capacity) for UEs in cars, trains and busses
  Overcoming vehicular enclosure signal attenuation, particularly in FR2
Augmenting capacity & coverage through creation of additional (portable) hot-spots/backhaul links
  Bringing coverage into out-of-coverage/poor coverage areas
Boosting mIAB deployments by supporting a combination of access links in unlicensed & backhaul links in licensed spectrum
BH link
Access
mIAB
Fixed IAB

## Slide 3: mIAB Scope: Connectivity & service continuity
Proposed objectives for Rel-18 (1/2)
Addressing challenges in mobility procedures associated with moving nodes/networks
  Study required enhancements to HO/DC mechanisms for mIABs and UEs
  Study group-mobility management procedures for improved signalling efficiency & reduced latency
Fixed IAB node
IAB Donor 1
Provide flexible mechanisms for a frequent (ex)change of Master/Secondary nodes
Fixed IAB node
mIAB HO
UEs HO
Address signalling overhead & latency
IAB Donor 2
IAB Donor 3
IAB Donor 1
IAB Donor 2
SN
MN
MN
SN
MN
MN

## Slide 4: mIAB Scope: Shared infrastructure & in-vehicle NR-U; Minimising interference
Proposed objectives for Rel-18 (2/2)
Enable variety of implementation options for shared infrastructure
  Enhancements to enable NR-U on the access (DU) with single/multiple backhaul connections (MT)
  Study mechanisms for connectivity/service continuity when moving from a shared to a non-shared network
Addressing a more complex interference environment due to dynamic network topology
  Specify further enhancements to radio resource coordination & CLI framework
Shared IAB node
DU (e.g. NR-U)
MT
Shared IAB Donor
CN (PLMN1)
CN (PLMN2)
IAB Donor (PLMN1)
Shared IAB node
MT
DU (e.g. NR-U)
IAB Donor (PLMN2)
MT