## Slide 1: Motivation of Study on Inter-gNB Coordination
NTT DOCOMO Inc., AT&T, Deutsche Telekom, Verizon, Telecom Italia, Vodafone, KDDI, China Telecom, Dish Networks, SoftBank, Bell Mobility
3GPP TSG RAN Rel-18 Workshop
Electronic Meeting, June 28 - July 2, 2021
RWS-210327

## Slide 2: Introduction
NG-RAN enables operators to deploy the logical entities flexibly in their network
In this paper, to enable more deployment scenarios, following enhancements involving inter-gNB coordination are discussed
  Inter-gNB/gNB-DU multi-carrier operation
  Inter-gNB/gNB-DU multi-TRP operation
  Enhancement for resiliency of gNB-CU

## Slide 3: Multi-Carrier Operation – Background
Carrier aggregation plays an essential role for user experience and efficient use of frequency resources
With the growth and penetration of 5G services, more and more spectrum is used for NR
How to accommodate and aggregate the frequency bands is a challenge for operators, in terms of:
  increasing number of fragmented bands that are re-farmed from LTE
  bands with different coverage areas due to different link budgets and/or antenna sites
High bands
Mid bands
Low bands

## Slide 4: Multi-Carrier Operation – Challenges of CA (1)
Currently in 3GPP, cells that can be aggregated by CA is constrained within a single gNB-DU
From accommodation perspective, the single-DU constraint of CA impacts e.g. cost and throughput
For example, when introducing a new frequency band there are several ways, all of which have downsides:
Band A
Band B
…
Reserved
gNB
Band A
Band B
…
New Band
Increased cost by capacity reservation
Band A
Band B
…
gNB
Band C
Band A
Band B
…
New Band
Move Band C to another gNB to aggregate new band and Band A/B
Add new band to a new gNB
Band C
…
Complicated operation and downtime due to reallocation
Band C cannot be aggregated
Reserve some capacity for potential new cells
Add new band using the reserved capacity
Band A
Band B
…
gNB
Band C
gNB occupied with legacy bands
gNB occupied with legacy bands
Band A
Band B
…
Band C
…
New Band
New band cannot be aggregated

## Slide 5: Multi-Carrier Operation – Challenges of CA (2)
From area design perspective, the single-DU constraint of CA directly limits deployment scenarios
  For example, the following scenarios cannot be realized
gNB #1
gNB #2
Band x gNB redundancy for important areas
gNB #1
gNB #2
Add-on cells on the gNB border
for capacity boosting
cannot be aggregated by CA
cannot be aggregated by CA

## Slide 6: Multi-Carrier Operation – Challenges of DC
Although many challenges of current CA stated in the previous slides can be solved by dual connectivity, DC has following challenges:
  Service area of DC is smaller than that of CA in some scenarios due to the need for two UL paths
  DC requires additional UE capability, e.g. two ULs
  CA performs more flexible resource handling than DC
DC area
DC area
1. DC with UL power sharing
2. DC with severe UL link budget (e.g. FR2)
2 ULs subject to
UL power sharing
Coverage
of FR2 DL
DC coverage is limited by FR2 UL
CA area
CA area

## Slide 7: Multi-Carrier Operation – Summary and Proposal
Challenges of single-node CA
  Restriction on accommodation design leads to increased capital/operational cost
  Restriction on area design limits e.g. end-user throughput/capacity and service reliability
Challenges of DC
  Smaller service coverage due to two ULs
  Need for additional UE capability
  Less flexible resource assignment than CA
Proposal 1: RAN to study the feasibility of standardized solutions for previously stated challenges of CA and DC, e.g. inter-gNB/gNB-DU carrier aggregation.

## Slide 8: Multi-TRP Operation – Background
In Release 16, RAN specified various flavors of multi-TRP solutions including multi-TRP with multi-DCI
Rel-16 multi-TRP operation supports independent scheduling between 2 TRPs with same or separate MAC over non-ideal backhaul as shown below
Multi-DCI multi-TRP operation

## Slide 9: Multi-TRP Operation – Challenges
In Release 17, the objectives of feMIMO WI include inter-cell multi-TRP operation
Due to e.g. limited TU, Rel-17 multi-TRP operation might be limited to intra-DU case only
The information and mechanisms for coordination required to support this feature across different gNBs/gNB-DUs are not currently supported by existing interfaces
  Required coordination would include e.g. timing coordination or resource allocation between TRPs

## Slide 10: Multi-TRP Operation – Proposal
Proposal 2: RAN to study the feasibility of standardized solutions to enable inter-gNB/gNB-DU multi-TRP operation
Following aspects should be considered in the study
  Backwards compatibility for UEs supporting Rel-15 CA and/or Rel-16/Rel-17 Multi-TRP features
  Architecture-aware enhancements for Rel-18 UEs
  Requirements on (non-ideal) backhaul latency
  Whether existing interfaces can support these use cases

## Slide 11: Resiliency of gNB-CU – Background
In current TS 38.401, it was defined that one gNB-DU is connected to only one gNB-CU
  One exception might be RAN sharing scenario in 38.401 where separate F1 signaling to PLMN-specific gNB-CUs is assumed
Under this principle, if the gNB-CU become inoperative, the gNB-DU cannot operate any NR cells

## Slide 12: Resiliency of gNB-CU – Proposal
If multiple gNB-CUs can be connected to a gNB-DU, it can continue to operate by using other normal gNB-CU as back-up, increasing service reliability of the area
Furthermore, if UE context in the failed gNB-CU is taken over to another normal gNB-CU completely, no call loss would occur on gNB-CU failure
Improved resiliency of gNB-CU would enable highly centralized gNB-CU deployment with large coverage area per gNB-CU
Proposal 3: RAN to study the feasibility of standardized solutions to improve the resiliency of gNB-CU

## Slide 13: Resiliency of gNB-CU – Options
Potential coordination options that improve gNB-CU resiliency include the following:

## Slide 14: Conclusions
In this paper, in order to flexibly deploy and make effective use of NG-RAN and its features, the following proposals are made.
Proposal 1: RAN to study the feasibility of standardized solutions for previously stated challenges of CA and DC, e.g. inter-gNB/gNB-DU carrier aggregation.
Proposal 2: RAN to study the feasibility of standardized solutions to enable inter-gNB/gNB-DU multi-TRP operation
Proposal 3: RAN to study the feasibility of standardized solutions to improve the resiliency of gNB-CU