## Slide 1
Further enhancement for RAN slicing
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28- July 2, 2021
Source: ZTE, Sanechips
Agenda: 4.3
RWS-210482

## Slide 2: Further enhancement for RAN slicing
New requirement from SA
Left over issues from R17 RAN slicing

## Slide 3: New requirement identified in FS_EASNS
Some new requirements about NW slicing have been identified in SA1 SI FS_EASNS
  [CPR-001] For a UE authorized to access multiple network slices of one operator which cannot be simultaneously used by the UE (e.g. due to radio frequency restrictions), the 5G system shall be able to support the UE to access the most suitable network slice in minimum time (e.g. based on the location of the UE, ongoing applications, UE capability, frequency configured for the network slice).
  [CPR-002] For a UE authorized to access to multiple network slices of one operator which cannot be simultaneously used by the UE (e.g. due to radio frequency restrictions), the 5G system shall minimize service interruption time when the UE changes the access from one network slice to another network slice. (e.g. based on changes of active applications).
  [CPR-003] 5G system shall minimize signaling exchange and service interruption time for a network slice, e.g. when restrictions related to radio resources change (e.g., frequencies, RATs).
  [CPR-006] The 5G system shall be able to minimize power consumption of a UE (e.g. reduce unnecessary cell measurements), in an area where no authorized network slice is available.

## Slide 4: New requirement identified in FS_EASNS
  [CPR-007] When a UE moves out of the service area of a network slice for an active application, the 5G system shall be able to minimize impact on the active applications (e.g., providing early notification).
  [CPR-008] The 5G system shall support a mechanism for a UE to select and access network slice(s) based on UE capability, ongoing application, radio resources assigned to the slice, and policy (e.g., application preference).
  [CPR-009] The 5G system shall support a mechanism to optimize resources of network slices (e.g., due to operator deploying different frequency to offer different network slices) based on network slice usage patterns and policy (e.g., application preference) of a UE or group of UEs
  [CPR-010] For traffic pertaining to a network slice offered via a relay node, 5G system shall use only radio resources (e.g. frequency band) allowed for the network slice.

## Slide 5: New requirement identified in FS_EASNS
Although the study in SA has not been finalized, clear impact on RAN can be seen from the new requirement identified in FS_EASNS, which is captured as potential consolidated requirements in 22.835.
To address the requirement from SA, a new RAN SI is required in Rel-18 accordingly.

## Slide 6: Further enhancement for RAN slicing
New requirement from SA
Left over issues in RAN

## Slide 7: Left over issues in RAN
Besides the new requirement identified by SA, some leftover enhancement from RAN slicing can be considered as well.
Left over issues in RAN2
  Slice based reselection for MO
  Enhancement to slice based cell reselection (e.g. Different RSRP/RSRQ thresholds)
Left over issues in RAN3
  Service interruption due to slice not supported
  Further enhancement of network slicing on MR-DC

## Slide 8: Left over issues in RAN2
Slice based reselection for MO
  Following the existing procedure, cell reselection will not be triggered if the intended slice for MO access is not supported in the currently camped cell thus UE will continue the access attempt on the camped cell and get HO or release with redirection to another cell supporting the intended slice.
  Cell reselection is expected to be triggered after NAS layer forward the slice for MO access to the AS layer and the intended slice is not supported in the camped cell.
Enhancement to slice based cell reselection
  Different offsets or RSRP/RSRQ thresholds for inter and intra-frequency slice based cell reselection can be studied as a supplement to the slice specific reselection priority.

## Slide 9: Left over issues in RAN3 - Service interruption due to slice not supported
In Rel-17, Service interruption due to slice not supported (e.g the UE is moving towards/fallback an area that does not support at least one of UE’s ongoing slices) in TR 38.832 (as shown in the figure) has been identify as valid scenario in RAN3 and SA2. RAN3 has already provided candidate solutions for these scenarios in the TR.
Due to SA2 need more time to study feasible impact of these solutions to CN/UE, RAN3 did not adopt these solutions into normative stage.
Therefore, solutions identified for these scenarios in Study Item (FS_NR_Slice) can be continue in a new Study Item in Rel-18.
Scenario: Service interruption due to slice not supported
Scenario: Moving back for non-supported slice in case of Inter-RA mobility

## Slide 10: Left over issues in RAN3 - Further enhancement of network slicing on MR-DC
As specified in SA2, a network Slice may be available in the whole PLMN or in one or more Tracking Areas of the PLMN. The AMF learns the S-NSSAIs supported per TA by the NG-RAN when the NG-RAN nodes establish or update the connection with the AMF.
In the deployment shown right, the MN provides coverage and eMBB services in one S-NSSAI. In actual deployment, URLLC service and eMBB belong to different slices. The SN provides special URLLC service to enhances the throughput in another S-NSSAI. Since URLLC is not supported in the whole MN, the core network will not allocate URLLC S-NSSAI to the UE according to the current specifications. Therefore, the scenario where the SN and MN supports different slices need to be investigated.
The main work of the SI can be focus on the how to support a UE leverage different slice resource in MN and SN simultaneously. Coordinate with SA2 is necessary.
Scenario: SN supports different Slice from MN

## Slide 11: Thanks