## Slide 1
Sidelink Evolution
Sidelink Enhancements
Sidelink Relay
Sidelink Positioning
15th – 16th June, 2023
Source: Nokia, Nokia Shanghai Bell
RWS-230020 3GPP TSG RAN Rel-19 workshop

## Slide 2
Sidelink enhancements to consider on top of Release 18
Release 18 forms the baseline for sidelink. Few practical use cases are still expected to need improvements for automotive and public safety scenarios.
Potential enhancements (three main areas)
Sidelink enhancements:
  Sidelink FR2 will only complete the study in Rel. 18 => normative work postponed to Rel. 19.
  Completion of sidelink CA and extension to unlicensed bands in FR1 and licensed & unlicensed bands in FR2
Sidelink Relay:
  Support of Multi-hop U2N and U2U relay with both L3 and L2 relay solutions for extended coverage
  Extension of multipath U2N relay to have two indirect paths, and introducing multipath relay in U2U relay
Sidelink Positioning:
  Rel. 18 enhancements for reliability/accuracy, latency, low-power, and integrity
  Sidelink PRS on unlicensed spectrum, with option of joint operating licensed/ITS and unlicensed spectrum
  Study application of high accuracy techniques such as carrier-phase-based positioning for sidelink

## Slide 3
Sidelink PC5 Further Evolution
High-level view of sidelink evolution in Rel. 18 and proposals for Rel. 19
Release 18 Sidelink Enhancements:
Carrier aggregation (limited to intra-band CA in ITS band)
Unlicensed band operation (restricted to FR1)
FR2 beam management (study only in Rel. 18)

## Slide 4
Sidelink PC5 Further Evolution
Justification and proposed objectives
Justification:
To expand the applicability of NR sidelink operation to wider use cases in addition to support V2X and public safety use cases that require high throughput and low latency.
Sidelink operation in Rel.18 has some limitations:
Sidelink in unlicensed spectrum:
    Unlicensed spectrum in FR1 (no FR2),
    Limited/simple multi-channel operation with no FBE channel access,
Sidelink in FR2 licensed spectrum:
  Limited to study only (with no time to study resource allocation enhancements)
  Beam management study ins for unicast (w/o multiple UC links) but no broadcast and groupcast support,
Sidelink carrier aggregation:
  Limited to intra-band CA in ITS band 47
  Other limitations ; e.g. Mode 2 only, no handling of limited capability, same SCS, and aligned PSFCH.
Objectives:
Study and specify enhanced SL-U operation in FR1 and support SL-U in FR2-2:
  Complete/enhance Rel.18 features (e.g. FBE channel access, resource allocation for MCSt),
  Support SL-U in FR2.2 with the associated beam management and shared channel coexistence schemes
Complete study and specify beam management schemes:
  Extend SL beam operation to carriers where the use of beams is necessary for all operations in all cast types,
  Specify enhanced resource allocation and multiple unicast
  Introduce multi-carrier support for the beam management operations (e.g. SL or Uu in FR1 aiding operation of SL BM in FR2).
Remove Rel.18 limitations and extend SL-CA support to inter band operations in unlicensed bands in FR1 and licensed & unlicensed bands in FR2
In addition, 3GPP can consider further enhancements to enable
  Study necessity and possibilities of PC5 range extension
  Power saving (e.g. DRX optimization for groupcast, SL-WUS)

## Slide 5
Sidelink Relay Evolution
High-level view of Sidelink Relay enhancements in Rel.18 and expectation for Rel.19

## Slide 6
Sidelink Relay Evolution
High-level view of Sidelink Relay enhancements in Rel. 18 and expectation for Rel. 19
Justification:
To support higher data rate or reliability as well as increased power efficiency in sidelink relayed communication for public safety as well as commercial use cases.
Sidelink relay operation in Rel.18 has some limitations:
  Multi-path Relay is limited to U2N relay with one direct path and one indirect path. It does not consider two indirect path and does is not supported in U2U case.
  Rel. 18 focuses on single-hop U2U and U2N Relay use cases, and does not consider enhancement/extension to network coverage as well as extended U2U operation range utilizing multi-hop
  Power efficiency is only considered with low priority with basic DRX configuration.
Objectives:
Study and specify mechanisms for Multipath relay extension:
  Multipath of L2 and L3 U2N relay with one direct path and one or more indirect path with different gNB,
  Multipath of L2 and L3 U2N relay with two or more indirect paths (for L2 relay) with same or different gNB,
  Multipath of U2U relay with two or more indirect paths,
  Multipath of U2U communication with one direct PC5 path and one or more U2U indirect paths.
Study and specify mechanisms to support Multi-hop U2N and U2U relay of both L2 and L3 relay solutions:
  Extend Rel-18 one-hop relays to multi-hop relays,
  Multi-hop connection management with or without support for service continuity.
Further enhancements to enable
  Power saving (e.g. DRX optimization)
  SDT over L2 U2N

## Slide 7
Sidelink Positioning
Overview of Rel. 19 expectations for sidelink positioning
Frequency
Unlicensed
FR2
Carrier 1
Carrier 2
More reliable, accurate, low-latency, and resource-efficient SL positioning, including low-power UEs
Low Power UEs
LMF
Server & Anchor UE
TRP
SL PRS
DL/UL PRS/SRS
Integrity
RSUs
VRUs
Carrier-phase Positioning
Operation using unlicensed, FR2 spectrum, and carrier aggregation

## Slide 8
Sidelink Positioning
Overview of Rel. 18 and expectation for Rel. 19 for sidelink positioning
Justification:
Sidelink positioning extends the 5G positioning framework with the addition of the PC5/SL interface, targeting higher performance requirements for vehicular, industrial, commercial, and public safety use cases under in-coverage, partial-coverage, and out-of-coverage scenarios, in terms of absolute or relative positioning, as well as angle and/or distance ranging.
Rel. 18 introduced sidelink reference signal for positioning (SL PRS), its measurement and reporting, and resource allocation. Further, signaling and procedures between UEs are introduced as a part of new sidelink positioning protocol.
Sidelink positioning functionality needs improvements considering the high QoS requirements to be supported given limited spectrum available for different use cases (e.g., ITS band), different types of devices (e.g., low-power UEs), and considering highly dynamic and mobile nature of sidelink.
Objectives:
Specify mechanisms for Rel. 18 enhancements:
  Reliability/accuracy and latency enhancements for SL PRS
  Latency and signaling enhancements to procedures
  Support for low-power UEs
Study and specify integrity of sidelink positioning
Study and specify sidelink positioning in unlicensed spectrum
Study and specify sidelink carrier-phase-based positioning
Study sidelink positioning operation on FR2 spectrum
Study CA operation for sidelink positioning