## Slide 1: SON/MDT enhancements in Rel-19
Taipei, June 15-16, 2023
Agenda Item: 5
Source: Nokia, Nokia Shanghai Bell
RWS-230024 3GPP TSG RAN Rel-19 workshop

## Slide 2
SON/MDT enhancements
Motivation
SON/MDT mechanisms are key for autonomous network performance optimization
Further enhancements of the SON/MDT framework are needed with each new 3GPP release and the new features they bring
Potential candidates for Rel-19 include:
  MRO for new mobility mechanisms
  Cross feature MRO enhancements
  Leftover topics from Rel-18

## Slide 3
SON/MDT enhancements
MRO for new mobility mechanisms
Rel-18 is introducing a series of new mobility mechanisms
    L1/L2 Triggered Mobility (LTM)
    CHO + MR-DC
    selective activation of SCG
In order to achieve optimal network performance in terms of user throughput, latency and network resource utilization, the existing MRO framework needs updates:
    New failure and near-failure scenarios description
    New information to be collected from the UE and network side
    New KPIs and root cause analysis methods

## Slide 4
SON/MDT enhancements
Cross feature MRO enhancements
With every new 3GPP release, more and more features can be configured to each UE
When some of these features are activated, they may inadvertently introduce new failures
  Examples includes MPE (Maximum Permissible Exposure), Multi-panel UE, slicing and energy saving
MRO mechanisms need to be adapted so that the correct source of these failures can be identified (mobility or different active feature)

## Slide 5
SON/MDT enhancements
Leftover topics from Release 18
Topics initially included in the Rel-18 WID but not finished due to lack of time (TBD at end of release)
  Enhancements for SPR (Successful PScell Change/Addition Report)
Topics that were proposed but not included in the Rel-18 WID
  SON/MDT for MBS: MDT measurement collection and MLB measurement
  Beam level MRO : instead of cell-to-cell MRO, optimization could be carried at beam or beam group level