## Slide 1
GSMA:
MNOs’ perspective on R19

## Slide 2: Introduction
The contribution provides an overview of the MNOs prospective on relevant items to be considered in R19 for RAN.
The contribution is the result of consensus amongst all participants of the GSMA 3GPPOP community and hence can interpreted as items for which there were no objections from any MNOs in the group, but not necessarily being the highest priority items. The following 9 MNOs are supporting the contribution:
CK Hutchison
Dish,
Deutsche Telekom,
EE,
KDDI,
KPN,
KT Corp,
Orange,
Telecom Italia

## Slide 3: The perspective of 11% of all 5G connections
The 8 MNOs groups collective represent the 11% of all 5G connections in Q1 2023, according to GSMA Intelligence.
Chart: 5G Connections in Millions
| Other 5G connections | 9 MNOs collective 5G connections
5G connections in Millions | 1017 | 131.5

## Slide 4: Key consideration for MNOs on R19 and onward
In order to select the important features and set priorities for R19, and onward, MNOs are always considering the following topics as key indicators:
Security
Energy
Privacy
Roaming
Complexity
Flexibility
API in support of GSMA Open Gateway
5G Deployment standards enhancements/bug fixes

## Slide 5
Security
The 3GPP system is still trusted as secure system to protect users and operators from malicious attacks and fraud. Each new feature and functionality needs to be assessed to comply with existing security standards and shall not deteriorate the overall system security. Rel-19 shall further improve protection of assets, examine potential threats associated with vulnerabilities and enhance system resilience against external attacks.
Energy
In accordance to SA guidance ( SP-211621) to all TSGs and WGs to consider Energy Efficiency even more as a guiding principle when developing new solutions and evolving the 3GPP systems specification, 5G System wide and coordinated support of energy efficiency/energy saving in NG-RAN, 5GC (NFs and UPF), NG-RAN, UE and OAM.
Privacy
One of the key role of the MNO is safeguarding the data of their users. Together with security and identity it creates trust which is of primary importance for the end user. Hence it is of primary importance that the 5G system provides security mechanism for protection of a variety of trusted information regarding human as well as machine-users

## Slide 6
Roaming
One of the vital roles of MNOs is to provide roaming services. 5G roaming has been developed with security by design. However, the roaming ecosystem is complex, with many players, such as MNOs, IPX, RH, RVAS providers. The 5G system should support all entities of the roaming ecosystem while maintaining a high level of security and flexibility but should try to reduce the complexity.
Complexity
The 5G system should reduce the complexity of planning, configuration and optimization of the whole system. 5G system should allow for easy deployment and management. Flexible network deployment/topology should be possible to address highly diversified service requirements and use cases and also be able to adapt to diversified network configurations.
Flexibility
5G Advanced should continue to evolve flexible wireless network topologies and deployments to meet wide ranging connectivity demands. From dense concentrations of mobile users, temporary and static traffic patterns, to users/devices in remote locations, the 5G system should be dynamic and integrate a variety of wireless connectivity. As part of deploying flexible network topologies, operators will have an even greater challenge of managing their networks and require advanced solutions to ensure high performance/reliability. It is imperative that 3GPP recognizes that the speed of a release is far less important than the quality of the release. Recent 3GPP work has resulted in non-backwards compatible features, errors, non-deployable features, and verticals that have no market interest. This has degraded the quality of the specifications and slowed down release roll out from both device and infrastructure vendors and should not be allowed to repeat itself. .

## Slide 7
API in support of GSMA Open Gateway
GSMA Open Gateway is a framework of APIs designed to provide universal access to operator networks for developers. Southbound interface of some APIs needs NEF/SCEF. The number of APIs will be increasing, so enhancement of 3GPP features is likely to be required.
General
As a guidance we recommend that features/capabilities developed by 3GPP do not exceed development on 3 releases. They need to have time to get commercially deployed and get feedback on the deployment before continue to evolve in futher releases

## Slide 8: 5G Deployment standards enhancements/bug fixes
5G standalone will be essential to delivering the real benefits of the technology. At the end of 2022, there were 237 live 5G networks globally, of which 35 were 5G SA.
While this represents a small proportion, momentum for 5G SA is building. Most operators are in the midst of 5GSA deployments. At a global level, the percentage of live 5G networks that are 5G SA or planned to become 5G SA is around 50%.
Asia Pacific has the highest 5G SA ratio, with more than 75% of live 5G networks already 5G SA or planned to become 5G SA.

## Slide 9: 5G Deployment standards enhancements/bug fixes
These deployments are identifying standards gaps that require immediate attention in 3GPP
For operators it is essential that 3GPP addresses them as soon as possible
These issues are deployment related and should not be going through work prioritization process
Most of these issues that we have been identified so far can be handled either as TEI19 or by small studies
We request that RAN allocates time for this activity from out of R-19 time units.
This time should be in addition to regular TEI 19 time unit allocation.
It is essential that 3GPP releases are driven by features that generate enough interest amongst the operator community to result in widespread deployment

## Slide 10: 5G Deployment standards enhancements/bug fixes
Having support from operator community in study proposals would indicate its need. Topics that do not generate significant interest in operator community should be deprioritized.
To improve prioritization process we propose that supporting companies of study provide a supporting document along with the study proposal that explains why that feature should be pursued in 3GPP e.g. explain its need for regulatory reasons, commercial deployment interests amongst operators resulting in new revenue streams etc..
Topics that already have gone through Phase 3 or more of studies in prior releases we recommend additional study proposals on them be scrutinized more closely and perhaps narrowed to the very essential – e.g. TEI 19 for such items could be allowed to handle minor enhancements.

## Slide 11: GSMA OP Rel-19 topics for consideration
The following slides are a cross section of potential important topics based on the 8 key
MNO considerations.
  Each of the GSMA MNOs operate in different market(s) and focused on potentially different market segments.
  As such, MNOs will have individual requirements that are of priority for them, but they are not represented in this contribution.

## Slide 12: Evolution of Network Energy Savings (eNES)
Definition | Next Step of Network Energy Savings as follow up of Rel-18 SI/WI, which does not provide sufficient saving potential.
Justification | RAN remains the largest consumer of energy in a cellular network. Reducing the energy consumption and the CO2 footprint, RAN functionalities shall be enhanced to allow consumption of as little energy as possible.
Usage scenario | Next level of energy savings for RAN: Define a WI covering the missing part from Rel-18 at least for: Network wake-up, SIB less cells, paging optimization, … (new functions could be defined in a non-backward compatible way, as for new bands (e.g. upper 6 GHz) anyway new UEs would be needed, directly benefitting from significant saving potential in RAN, e.g. total shut-off and wake-up …)
ENHANCEMENT
NEW CAPABILITIES
GREEN

## Slide 13: TN/NTN integration/interworking
Definition | Further optimisation of TN/NTN/TN interworking up to full integration of TN & NTN radio services and roaming capabilities should be studied for realisation for 3GPP NR NTN as well as for 3GPP IoT NTN.
Justification | Rel-17/-18 were mainly focussed on generic NTN access, internal NTN mobility and some minor TN/NTN aspects (as the main active companies were out side the classics cellular MNOs). New NTN constellations like IRIS2 [1] require full integration into the 5G ecosystem [2] and overall TN/NTN orchestration.
Usage scenario | Full interworking in any UE state incl. network steering shall be optimised for TN -> NTN and NTN -> TN. Aspects of full TN/NT integration incl. flexible, dynamic 3D orchestration (topology changes, mobility control and common resource allocation) should be studies and where appropriate defined.
ENHANCEMENT
NEW CAPABILITIES
[1] https://defence-industry-space.ec.europa.eu/eu-space-policy/eu-space-programme/iriss_en [2] https://www.atis.org/initiatives/non-terrestrial-networks-ntn-5g-integration/

## Slide 14: NR mobility enhancements
Definition | NR Mobility Enhancements for inter CU mobility support
Justification | Enhancements for serving cell change/mobility is always important for mobile operators to reduce its latency, overhead, and interruption time. In Release-18, 3GPP RAN work on functionalities such as L1/L2 based inter-cell mobility(only intra-CU support), NR-DC with selective activation of the cell groups, L1 enhancements for inter-cell beam management/reporting, RACH-less cell change with early candidate cell TA(Timing Advance) acquisition (using only contention-free RA) and others. But there are areas still needs to be enhanced in Release-19.
Usage scenario | Scenarios which are not addressed in Release-18 functionalities such as Inter CU mobility support, early TA acquisition using contention-based RA, and support partial MAC reset maintaining HARQ buffer after cell switch.
ENHANCEMENT

## Slide 15: SON/MDT enhancements
Definition | SON/MDT enhancements aiming overhead reduction between UE and gNB, improving efficiency
Justification | SON/MDT is a fundamental key feature to optimize mobile networks. But the current mechanism is not to sophisticated in terms of overhead and efficiency. Considering a common situation where there is only a small number of UEs having user consent for allowing data collection, improving efficiency is very important aspects to be addressed. Addition to that data collections for Release-18 features should be also included in the work.
Usage scenario | Efficient network optimisation using SON/MDT features, including Data collections for Release-18 features: SON/MDT enhancements for Release-18 features, such as network energy saving, mobility enhancement, MIMO, XR, UAV, and others. UE Simultaneous LTE/NR MDT logging: Support simultaneous configuration to avoid MDT re-configuration after UEs move to the other RAT. UE side MDT logging information filtering: Reduce logged MDT overhead and transactions between UE and gNB, with more efficient data collections, potentially includes discarding logging data without GPS location information, enhancement for event triggered logging.
ENHANCEMENT

## Slide 16: More than 32TRx MIMO
Definition | Extend CSI-RS resource to 64/96/128 ports and define related Type I codebook (e.g., N2>2 when N1=8)
Justification | Many operators are deploying lots of 64TRx radio now. However, beamforming flexibility of these new radios cannot be fully utilized in below cases due to the current 32 ports CSI-RS limitation. ① Cell Edge: if SRS is released, there is no performance difference between 32/64TRx radio in our field driving test as shown in figure 1. ② Low/Mid-Band NR CA: there is quite large mid-band 5G DL coverage for old 32P CSI-RS based operation even if new 64TRx radios are installed for mid-band. ③ Large number of UEs a Cell
Usage scenario | Maximizing the performance of 64TRx radio equipment which is already in live network.
ENHANCEMENT
Mid-band NR (3.5GHz)
Low Band NR
UL Data/Control
Mid-band SRS
is released here
Remained coverage
for old 32P CSI-RS
Coverage (NR CA)
Mid-band Coverage (SA or EN-DC)
SRS Released @1906m (Pathloss 129.7dB)
64TRx gain with SRS
(Average gain: ~30%)
Reciprocity based beamforming (w/SRS)
32P CSI-RS
64TRx gain
with no SRS
(No difference)
Chart: Distance (m)
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000 | 2050 | 2100 | 2150 | 2200 | 2250 | 2300 | 2350 | 2400
32TRx | 1165.7329 | 1068.4165 | 1139.9621 | 738.1317 | 726.9061 | 697.1191 | 562.8885 | 517.2512 | 568.9277 | 486.6482 | 431.2405 | 414.6213 | 363.1301 | 369.7175 | 363.3702 | 337.3604 | 312.3169 | 310.0412 | 321.009 | 339.43 | 347.3272 | 323.4146 | 302.3849 | 267.3053 | 247.8854 | 260.6974 | 227.9835 | 219.0909 | 241.9961 | 248.3741 | 168.6902 | 154.7808 | 196.0404 | 218.0272 | 247.5383 | 171.7127 | 254.2091 | 214.1501 | 106.6441 | 96.3562 | 62.0397 | 0.15214 | 8.9301 | 0.021941 | 0.22524 | 0.025333 | 0.038929 | 0
64TRx | 1457.1475 | 1454.3969 | 1139.7022 | 925.4911 | 833.4538 | 715.9491 | 574.6726 | 624.1386 | 680.0409 | 600.3467 | 540.233 | 562.4792 | 448.8362 | 448.7605 | 420.7231 | 359.1076 | 341.0137 | 345.1164 | 325.7045 | 369.8155 | 390.5036 | 359.5972 | 366.6951 | 301.3018 | 296.0326 | 343.3851 | 298.9139 | 263.4967 | 268.335 | 318.4966 | 337.0092 | 302.3274 | 334.8169 | 335.2438 | 358.5011 | 370.546 | 433.1976 | 320.1264 | 101.8787 | 95.5228 | 12.8266 | 1.4285 | 0.060793 | 0.0041176 | 0.24431 | 0.32059 | 0.0008 | 0.033529 | 0.0002
Figure 1. DL performance comparison of 32/64 TRx radio
in live network (Tx Power: 50.2/52dBm)

## Slide 17: Sub-band Full Duplex for Random Access Coverage Enhancement
Definition | Random access coverage enhancement using SBFD operation in RRC idle/inactive state
Justification | Mid-band TDD (e.g., 3.5GHz) is main frequency range of NR in terms of global usage. In LOS environment, mid-band NR TDD coverage is limited by possible PRACH detection distance (not UL data channel) ① NR Coverage Bottleneck: SBFD (sub-band full duplex) operation can enhance the NR data channel QoS coverage by utilizing increasing UL scheduling chance to reduce UL RB & MCS per each transmission. ② PRACH Coverage: Even if there are sufficient PRACH preamble formats in specification, limited continuous time duration for the uplink in TDD limits its allocation flexibility in real network. only short preamble sequence can be used for DDDSU pattern with 30kHz SCS (=0.5ms UL slot duration) → Max. PRACH detection distance = 4.6km
Usage scenario | Maximizing the mid-band 5G coverage in LOS environment
ENHANCEMENT
Direction | QoS | UL 1Mbps | 
Tx | UE Tx Power (dBm) | 23 | 23
 | Duplex (DL/UL) | DDDSU | FDD (or XXXXU)
 | UL RB | 75 | 28
 | MCS | 0 | 0
 | UE EIRP (dBm/RB) | 4.2 | 8.5
 | Required SNR (dB) | -3.0 | -3.0
 | Received Signal Strength (dBm/RB) | -117.2 | -117.2
Max Allowable Pathloss (dB) |  | 146.4 | 150.7
Max 2D Distance (UMa LOS, @3.65GHz, km) |  | 9.15km | 12.4km
Table 1. Mid-Band NR QoS Coverage (UL 1Mbps)
Category | Format | Maximum Cell Radius (m) |  |  | 
 |  | 15kHz SCS | 30kHz SCS | 60kHz SCS | 120kHz SCS
short | C2 | 9301 | 4648 | 2324 | 1162
Long | 0 | 12364 (SCS 1.25kHz) |  |  | 
Table 2. NR PRACH Cell Dimensioning

## Slide 18: AI/ML based Automation & Efficiency improvement
Definition | WI on AI/ML for NG-RAN in RAN3 and Physical Layer in RAN1 are ongoing in Rel-18, but the overall framework incl. Model handling and Life cycle management might not be ready and consistent between RAN/SA in Rel-18. Further work is to be done in Rel-19.
Justification | Definition of fully end-2-end AI/ML framework across domains (RAN/CN/OAM) incl. life-cycle management in 3GPP is required as baseline which should be achieved before further work is performed in RAN WGs.
Usage scenario | Addressing the e2e framework as well as defining additional Use Cases is the next step for AI/ML support in NG-RAN (Rel-19 SI followed by a Rel-19 WI). Normative work on AI/ML support for Physical Layer in Rel-19 based on Rel-18 SI as par of a consistent 3GPP AI/ML framework. Furthermore, also new Use Cases should be defined (Rel-19 SI).
ENHANCEMENT
NEW CAPABILITIES

## Slide 19
NR Mobile Integrated Access and Backhaul (mIAB) enhancements |  |  | 
Definition | Mobile Integrated Access and Backhaul enables extension of cell coverage in situations where coverage is either difficult or prohibitive, or when infrequent surges in bandwidth demand do not justify permanent network provision. mIAB employs UEs with the mIAB capability to extend network coverage and bandwidth where normal access is insufficient or unavailable to meet demand. |  | 
Justification | The focus of Rel-18 was on specification of supporting mobility for 5G standalone. Rel-19 aims to further enhance with support of multi-hop m-IAB, height measurement and NTN backhaul support which was down prioritized in Rel-18. These enhancements offer better portability/mobility for Public Safety (e.g., disaster/recovery deployments), special-event use cases, and also deployment flexibility for scalable user/enterprise deployments. |  | 
Usage scenario | Flexible and dynamic coverage, multi-frequency support for mIAB |  | 
ENHANCEMENT

## Slide 20
Thank you!
Contact: bpareglio@gsma.com