## Slide 1: Multi-hop Relaying for Sidelink Evolution in Rel-19 5G-Advanced NSC, AT&T, Johns Hopkins University APL, and MITRE
3GPP TSG RAN Rel-19 Workshop
June 15-June 16, 2023
RWS-230031
Agenda Item: 5

## Slide 2: Sidelink Enhancement in Rel-18
Sidelink carrier aggregation (CA) operation
Sidelink in unlicensed spectrum
Enhanced sidelink operation for FR2 licensed spectrum
Mechanism(s) for co-channel coexistence for LTE
Sidelink and NR sidelink
Sidelink relay enhancements

## Slide 3: Need for Sidelink Multi-hop Relay
Status in Rel-18: Sidelink multi-hop relay was de-prioritized in Rel-18 due to workload
In Rel-19, Sidelink needs to expand existing C-V2X and public safety capabilities:
  Sidelink relay enhancement is completed in Rel-18 ---- need for further enhancement
  Support new use cases: aerial networking with flexible network architectures, human-machine integration, wireless AR/VR headset networks, disaster relief operation, etc
Proposal: Study how Sidelink can be extended to support multi-hop relaying in Rel-19 Sidelink relay enhancement

## Slide 4: Multi-hop Relaying for Sidelink in Rel-19
Adopting multi-hop relaying for sidelink in Rel-19 should
  Largely reuse existing 3GPP specification support for multi-hop relaying
  Minimizing RAN1 specification impacts on signaling and measurements
The functionality of multi-hop relaying has already been supported in 5G NR
  Backhaul adaptation protocol (BAP) for integrated access and backhaul (IAB) allows for multi-hop backhauling using the same frequencies employed for UEs
  BAP is a Layer 2 protocol to enable multi-hop packet delivery among IAB nodes. It is located on the top of the RLC layer
Proposal: Study whether BAP can be extended to sidelink to support multi-hop relaying.

## Slide 5: Conclusion
Many important milestones of Sidelink enhancement have been achieved in Rel-18 3GPP 5G-Advanced.
There are pressing needs to enable Sidelink multi-hop relaying to support new use cases such as UAV networking.
Multi-hop relaying has already been supported in Rel-16 5G NR through BAP in IAB.
We propose:
    Study how Sidelink can be extended to support multi-hop relaying in Rel-19 Sidelink relay enhancement.
    Study whether BAP can be extended to sidelink to support multi-hop relaying.