## Slide 1: Proposed UAS Enhancements in Release 19 5/30/23
3GPP TSG RAN Rel-19 Workshop
June 15-June 16, 2023
RWS-230033
Agenda Item: 5

## Slide 2: Proposed UAS Enhancements
Flexible UAV-based Network Architectures

## Slide 3: Motivation for Additional UAS Architectures
Current Architecture. In a typical scenario supported by the 3GPP, the UAV is a UE. A 5G UE on a UAV communicates with an on-the-ground gNB to meet its communication needs. For example, the UAV UE can transmit a video to an Application Server using an on-the-ground gNB and the 5GC.
A UAV UE has limited processing capabilities. Hence, if a UAV needs to meet communication needs of UEs that have poor or no coverage from the gNBs, a typical UAV UE would be inadequate.

## Slide 4: Additional UAS Architectures
Additional UAS architectures could be investigated by the 3GPP, where a UAV can house a Network Function (UAVNF) to serve communication needs of PCUEs efficiently and cost-effectively. In one example, a UAVNF may be an integrated gNB. In another example, a UAVNF may be a gNB-DU.
Goal: Investigate potential architectures that provide additional flexibility to increase the utility of the UAS.
Example architectures.
  gNB on the UAV
  gNB-DU on the UAV
Note. Other architectures should also be explored (e.g., the use of sidelink and UE-to-Network Relays).
Study various architectures to define a new architecture that supports a Network Function in addition to the UE on the UAV. The architecture should aim to maximize the reuse of existing specifications (e.g., those related to disaggregated gNB, IAB (including mobile IAB), and sidelink).