## Slide 1
Regenerative NTN
gNB DU payload
3GPP TSG RAN Rel-19 workshop
June 12 - 16, 2023
Agenda: 5 (RAN1/2/3-led Rel-19 topics)
RWS-230045
Source: Lockheed Martin, Airbus, Eutelsat, OneWeb, Gatehouse,
Echostar/Hughes, Intelsat, Sateliot

## Slide 2: 3GPP – R19 Workshop : Regenerative NTN gNB DU payload
Payload Options for the Regenerative NTN
Transport Layer implications, Specification Enhancements – Key Areas
Justification for the Specification Enhancements for gNB DU payload
Proposals for R19 Regenerative NTN
Objectives
RWS-230045

## Slide 3: 3GPP – R19 Workshop : Regenerative NTN gNB DU payload
Payload options
For NTN Regenerative payloads the following two baseline options are possible. In this proposal considers alternatives for Option#2
Option 1: Full gNB Payload
  All logical gNB functions on satellite payload
  UE Mobility : Inter-gNB (gNB to gNB) via Xn
Option 2: gNB DU Payload
  Single DU or Multiple Distributed Units (DUs) of the gNB on the satellite payload(s)
  Central Unit (CU) of the gNB on the ground
  UE Mobility : Intra-gNB (DU-to-DU) via F1, Inter-gNB (CU-to-CU) via Xn
RWS-230045

## Slide 4: 3GPP – R19 Workshop : Regenerative NTN gNB DU payload
Key specification enhancement work areas may relate to the RAN3, including related RAN1 and RAN2 work.
 |  | Full gNB payload | gNB DU payload
Key Interfaces | NR-Uu | NTN Access link | 
 | NG | via NTN GW / Feeder link / Cross Links | On the ground / TN Transport
 | Xn | via ISL | On the ground / TN Transport
 | F1 | Payload | via NTN GW / Feeder link / Cross Links
 | E1 | Payload | via NTN GW / Feeder link / Cross Links
RAN Split Option in use |  |  | Option 2 (Study of alternative RAN Split Options is not precluded)
NTN Transport Layer implications (ISL/Feeder link) | Connectivity | NG/Xn – Inter gNB Handovers involving 5GC | F1/E1 – Intra-gNB Handovers (Not involving 5GC on the ground).
 | Latency | Impact on NG/Xn procedures | impact on F1/E1 procedures
 | Bandwidth |  | Anticipate slightly higher Overhead
 | Packet Loss | NG User plane, re-transmissions | F1 User plane, re-transmissions
R19 - Regenerative - NTN Specification , Procedures Enhancements - Key Areas |  | NG and Xn Transport Protocol Layers | Impact on F1 and E1 Transport Protocol Layers Note - Satellite ISL standardization is not required
Specification Enhancement - Key Areas
RWS-230045

## Slide 5: 3GPP – R19 Workshop Regenerative NTN gNB DU payload
Payload design complexity and resources:
Considering the need for FR2 band use for access links, having “centralized” / common gNB functions - on ground (i. e: CU on ground) will allow more DU (resources and capacity) on the payload. Payload power consumption will also be
Interaction with 5GC, optimized signaling: UE mobility scenarios, and Inter-DU handovers offer efficient User plane anchoring (less traffic forwarding to new gNB, no HO signaling towards 5G core network)*
Additional gNB DU advantages include:
NR Service capability features (e.g. BWP may be DU specific)
Flexible capacity options, like covering different device capabilities from single payload
Configurable functional splits enables adaptation to various use cases, such as variable latency on transport
Justification
*When applicable (NTN service in the same country, 5gNB-CU/5GC on the ground)
RWS-230045
Support of delay sensitive services, elevated user experience compared to “transparent” NTN payloads
Support of delay tolerant services in areas without NTN gateways (either not deployed or temporarily not operational)
Enable reduced user and/or control plane latency
Support unicast, multicast and broadcast communications
Support for Dynamic Beamforming (e.g. Mobility)
Support of edge computing/ (light) MEC on board
The following benefits of a Regenerative NTN payload continue to be available with a gNB DU architecture:
(Relative to those for a full gNB payload)

## Slide 6: 3GPP – R19 Workshop Regenerative NTN gNB DU payload
Multi Connectivity
Multi NR connectivity is going play an important role with NTN service availability. It will provide a great compliment to terrestrial NR service. With gNB DU payloads, the multi connectivity usage can be realized.
UPF / MEC
With CUPS (Control plane/User plane separation) already specified, we can host UPF on payload with gNB DU for delay sensitive, limited bandwidth MEC applications
It will still allow additional UPF on ground for delay tolerant services
Key Use Cases
*When applicable (NTN service in the same country, 5gNB-CU/5GC on the ground)
RWS-230045

## Slide 7: 3GPP – R19 Workshop Regenerative NTN gNB DU payload
Observations
RWS-230045
A regenerative payload provides nearly half the Uu RTT of a transparent payload. This may enhance closed loop processing functions. Service latency may also be reduced where the payload supports local breakout and/or loopback
SWAP may be orders of magnitude higher cost on the payload which encourages minimization of network functions on the payload.
Robustness of the satellite link is important which may be supported by dual/multi-connectivity. Inter-working between satellite and terrestrial networks also ensures a high-reliability NTN connectivity.
A gNB-DU payload with ground based gNB-CU components address the aforementioned requirements as well, minimizing SWAP while bonding dual connectivity in a ground based gNB-CU.
NTN Release 19 needs to Enhance the existing F1 to work over envisaged NTN feeder-link and multi-hop ISL scenarios.
Separating gNB-CU into gNB-CU-CP and multiple gNB-CU-UPs also enables the support for MEC.
NTN Release 19 may also need to enhance E1 to support the NTN feeder-link and multi-hop ISL scenarios.
Separated gNB-CU-CP and gNB-CU-UP instantiations for both on the ground and on the payload support the enhancement of E1.
Further optimizations may be possible by considering gNB functional splits other than Option 2 that is currently assumed.
NTN Release 19 may consider RAN functional split options other than Option2.

## Slide 8: 3GPP – R19 Workshop Regenerative NTN gNB DU payload
Proposals
RWS-230045
For a gNB DU payload the Xn specification does not need any changes.
Standardization impact : [RAN3]
Proposal 1: Study and if applicable define the necessary enhancements for the,
F1 interface protocol (both CP and/or UP)
Proposal 2: Study and if applicable define the necessary enhancements for the,
E1 Interface protocol
Proposal 3: Study and if applicable define the necessary enhancements for,
other RAN functional split options
Note: These proposals may be considered in order, for example it is possible to only consider Proposal 1 for support of gNB DU.

## Slide 9: References
RWS-230001, “Agenda for RAN Rel-19 workshop, “ RAN Rel-19 Workshop, June 15 - 16, 2023
RWS-210084, “gNB Disaggregation and CU-CP resiliency, ” RAN Rel-18 Workshop, June 28 – July 2, 2021
3GPP TR 38.821, “Solutions for NR to support non-terrestrial networks (NTN), V16.0.0 (2019-12)
3GPP TR 38.879, “Implementation options for CU-CP should allow Resiliency”, V18.0.0 (2022-09)
RWS-230045