## Slide 1
Release 19 - NTN Topic Overview
3GPP TSG RAN Rel-19 workshop
June 12 - 16, 2023
Agenda: 4 (High-Level Overview Proposals for Release 19)
RWS-230046

## Slide 2: 3GPP – R19 Workshop : NTN Topics
Regenerative Payload
Beamforming
Downlink Enhancement
IoT/eMTC Enhancement
Other considerations (MBS, RedCap, etc., ?)
RWS-230046

## Slide 3: 3GPP – R19 Workshop : Regenerative Payload
NR NTN - Full gNB Payload
All logical gNB functions on satellite payload
UE Inter-gNB handover via Xn
NR NTN - gNB-DU Payload
Single DU or multiple DU(s) of the gNB on the payload(s) with optional CU-UP & MEC
CU-CP and optional CU-UPs on the ground
Possibility of hosting edge compute in space
Direct device to device connectivity w/o ground hop
Lower latency
IoT/eMTC NTN eNB on Payload
EPC on ground
Massive machine type communication
Optional EPC on payload for store and forward capability
gNB
DU
CU
gNB-DU
RU
DU
CU-UP
MEC
CU
DU
Xn
Ng
eNB
eNB
S1
E1
RWS-230046
RU
Uu
Uu
F1,
Uu
EPC

## Slide 4: 3GPP – R19 Workshop : NTN Beamforming
Topics that need to be addressed for NTN include:
Handover between beams, and cells requires careful consideration for mobility, discontinuous coverage, cell edge performance
BCH, PDCCH may be challenged with Link Margin. Methods that enhance downlink coverage without scarifying latency are required
Power efficiency of IoT NTN may need careful consideration
Only a single BWP is currently supported, multiple BWP’s are needed
Beam specific PRACH support
NTN Beamforming is a Promising Technology for Addressing Spectral Efficiency and Coverage
RWS-230046

## Slide 5: 3GPP – R19 Workshop : NTN Downlink Enhancements
Methods for downlink enhancements include:
Downlink Waveform (e.g. DFT-s-OFDM)
PRACH, BCH, PDCCH/PUCCH Repetition
Narrow band (~ 180 kHz – 1.4 MHz) link discovery within BWP(s) (e.g. SSS, BSS, MSG3)
Support for MIMO (e.g. Polarization precoding)
Downlink Enhancements Required to Improve NTN Coverage
Source
S/P
DFT
Sub-Carrier
Mapping
IFFT
CP
DFT-s-OFDM Downlink
SSB’s within BWP(s)1
1R1-2009736, “Summary of … Aspects of NR-NTN“ RAN1#103e, Nov, 2020
RWS-230046

## Slide 6: 3GPP – R19 Workshop : IoT/eMTC Enhancements
5GC support for IoT
Multi-Connectivity
Broadcast/Multicast (mMTC NTN)
Paging Alert Channel
Inter-RAT TN/NTN Operation/Mobility
Support for Store & Forward Regenerative Payload
Support for RedCap in NTN
Semi-Persistent Scheduling
Random Ad hoc Scheduling
IoT FD-FDD Operation
IoT NTN over Beam Hopping
Co-existence of NR and NB-IoT
5GNB
5GNB
NTN IoT Service
RWS-230046

## Slide 7: 3GPP – R19 Workshop : Other topics
Integrated Access and Backhaul
Advanced Waveform for K Band
Enhanced HARQ
MBS
Dual Steer
GNSS Independent Operation
High Power UE
RWS-230046

## Slide 8
RWS-230046