## Slide 1: IAB Architecture for NTN in R19
3GPP TSG RAN Rel-19 workshop
June 12 - 16, 2023
Agenda: 5 (RAN1/2/3-led Rel-19 topics)
Source: Verana, Lockheed Martin
RWS-230050

## Slide 2: 3GPP – R19 Workshop : IAB Architecture for NTN
In Rel-17 and Rel-18 NTN related WIs, only “Transparent payload” architecture has been specified
  See TR 38.821, Solutions for NR to support NTN, Table 4.2-1, column #2
TR 38.821 also considered architectures for the regenerative payload and left application of IAB architecture to NTN for further study [section 5.2.3]
We propose that 3GPP add support for the regenerative payload architecture for the service link in Rel-19
We further propose that 3GPP approve in Rel-19 at least an SI to investigate regenerative NTN architectures that utilize IAB-like approaches for serving service, feeder and inter-satellite links using 5G NR in an integrated manner
RWS-230050

## Slide 3: Regenerative NTN
Regenerative NTN is a satellite payload that terminates a 5G NR signal, including at the minimum Layer 1 and at least portions of Layer 2
Service link represents a 3GPP defined interface based on 5G NR
Feeder link and Inter Satellite Links (ISL) are based on non-3GPP defined physical interfaces that carry 3GPP F1 or NG protocol packets
Full gNB in Satellite (or UAS platform)
gNB-DU in Satellite (or UAS platform)
in split CU-DU architecture
RWS-230050

## Slide 4: IAB Architecture for Regenerative NTN
IAB Architecture for Regenerative NTN with 5G NR-Based Service &
Inter-Satellite Links - Donor DU on Satellite
IAB Architecture for Regenerative NTN with 5G NR-Based Service,
Inter-Satellite & Feeder Links - Donor DU on the Ground
3GPP 5G NR-Based Service, Inter-Satellite or Feeder Links
RWS-230050

## Slide 5: Why Regenerative NTN with IAB Architecture?
  Enables sharing of Layer 1/2+ processing hardware on the satellite for operating service, inter-satellite and feeder links
  Consistent QoS handling of all links, since all radio interfaces are now based on 5G NR
  Compatibility among nodes on either side of the links (all 5G NR based)
  Increased spectral efficiency through potential co-channel operation of inter-satellite or feeder links with the service link
RWS-230050

## Slide 6: Proposals Regenerative NTN & IAB in Rel-19
We propose that 3GPP add support for the regenerative payload architecture for the service link in Rel-19
We further propose that 3GPP approve in Rel-19 at least an SI to investigate regenerative NTN architectures that utilize IAB-like approaches for serving service, feeder and inter-satellite links using 5G NR in an integrated manner
RWS-230050

## Slide 7: References
3GPP TR 38.821, “Solutions for NR to support non-terrestrial networks (NTN), V16.2.0 (2023-04)
3GPP TR 38.401, “NG-RAN Architecture description”, V17.4.0 (2023-04)
3GPP TR 38.473, “NG-RAN F1 Application Protocol (F1AP), V17.4.1 (2023-05)
RWS-230050