## Slide 1: AT&T Views and Priorities for Release 19
June 2023
RWS-230074

## Slide 2: General
Release 19
  Views on Release 19 timeline
  Views on Rel-19 SI/WI proposals
    Further enhancements from completed Rel-18 WIs/SIs
      including RAN Plenary-led SIs
    New WIs/SIs based on e.g., SA-led WIs/SIs
Meeting Efficiency Improvements
  Views on efficiency improvements for the Rel-19 meeting cycle
  e-meeting takeaways/efficiencies
  Alignment with SA
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 3
Release 19 Timeline

## Slide 4: AT&T views on the RAN Rel-19 Proposed Timeline*
R19 RAN1
R19 RAN2/3/4
R19 RAN1 Func. Freeze
R19 RAN2/3/4
Func. Freeze
R19
RAN Workshop
R19 Pkg
approved
(RAN1/2/3)
2023
Q1
Q2
Q3
Q4
2025
Q1
Q2
Q3
Q4
R19 Pkg
approved
(RAN4)
R19 initial ASN.1 review
RAN/CT/SA Code
Freeze (ASN.1/OpenAPI)
2026
Q1
Q2
R19
Proposals
consolidated
R18 RAN1 completion
R18 RAN2/3/4 completion
  “Stabilization” phase/alignment across WGs & TSGs
Although Q12024 would be the official start of Rel-19, Rel-18 maintenance/completion is expected in 1H2024 (no changes suggested to Rel-18 timing)
Rel-19 Package approved in Dec. 2023 (RAN4 March 2024)
Rel-19 RAN1 Functional Freeze Sept 2025 (RAN2/3/4 Dec. 2025)
Rel-19 Code freeze (ASN.1/OpenAPI) March 2026
*Aligned with RP-230800 “Rel-19 timeline alignment RAN/SA/CT” using endorsed RP-230050 “RAN Planning” as a starting point.
RAN/CT/SA Code
Rel-18 Freeze (ASN.1/OpenAPI)
R18 RAN1 Maintenance
2024
Q1
Q2
Q3
Q4
R18 RAN2/3/4 Maintenance

## Slide 5
Rel-19 Proposed Work/Study Items

## Slide 6: AT&T priorities to be Considered for Rel-19
RAN1-led items
  MIMO Enhancements
  Network controlled repeaters (NCRs)
  Integrated Communication and Sensing (ICAS)*
  Network Energy Savings (NES) enhancements
  Ambient IoT*
  AI/ML for air interface
  Further Sidelink enhancements, inc. SL/ranging positioning enhancements
  Evolution of NR Duplex Operation
    Follow-on WI, inc., extension to frequency-overlapped scenarios without UE impact
RAN2-led items
  Further UAV enhancements
  Further XR enhancements*
  Multicast/broadcast enhancements
  Further Sidelink enhancements
    Relay enhancements
    SL/ranging positioning enhancements
RAN3-led items
  AI/ML for NG-RAN
  Network reliability and efficiency enhancements*
    Security
    QoE
    SON/MDT
    5G Network Timing Resiliency and TaaS enhancements
  5G Femto
  Mobile Integrated Access Backhaul (IAB) enhancements*
  *Requires SA input/alignment

## Slide 7
MIMO Enhancements

## Slide 8: RAN1-led WI: MIMO enhancements
Motivation and justification
  UL coverage and capacity enhancements are of high importance for 5G, especially for FWA scenarios. Rel. 18 specified enhancements to enable 8Tx UL operation but more are needed
  Rel. 18 specified multi-TRP CJT with ideal time/frequency synchronization. There needs to be a follow-on item that evaluates and specifies a more practical implementation of CJT towards a more distributed MIMO deployment
  Beam management enhancements are still needed for enhanced beam acquisition and tracking building on Rel. 17/18 multi-beam operation enhancements
Key objectives
  Specify enhancements that improve UL MIMO performance, especially for FWA scenarios, including enhanced UL precoding schemes
  Study and specify enhancements that consider realistic deployment assumptions for the distributed TRPs in CJT mTRP
  Specify multi-beam operation enhancements related to reducing overhead and latency for beam indication and reporting
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 9
Mobile IAB enhancements

## Slide 10: RAN3-led WI: Mobile IAB enhancements
Motivation and Justification
    Public Safety and verticals use cases for dynamic coverage extension
    Support scalable deployments of vehicular and UAV-based IAB nodes
    Lower complexity/cost to support portable vs. fixed node form-factors
Mobile IAB enhancements
    UAV/NTN feature support and alignment (e.g., CHO/DAPS optimization)
    Architecture enhancements to support local gNB-CU/UPF
    Multi-hop, network-controlled topology adaptation
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 11
NCR enhancements

## Slide 12: RAN1-led WI: NCR enhancements
Motivation and Justification
    NCR portability: Public Safety and special-event use cases
    Deployment flexibility: Scalable and user-deployed (e.g., in-building NCR)
Network controlled repeaters (NCRs) enhancements
    CONNECTED mode RRM measurement reports
    Dynamic access/backhaul power control
    Multi-frequency support for NCR-MT (e.g., NR-DC/EN-DC/CA)
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 13
Integrated Communication & Sensing (Summary of RWS-230472)

## Slide 14: RAN1-led SI: Integrated Communication & Sensing (ICAS)*
Justification and Motivation
  Sensing provides valuable assistance information for communication to enable new use cases and scenarios
  3GPP SA1 study on use cases and requirements for integrated sensing and communication
  Current 3GPP channel model inadequate for use in identifying and characterizing sensing targets
Key Objectives
  Identify representative sensing use cases and their corresponding KPIs
  Prioritize possible candidate sensing modes/topologies
      Network to UE(s) bi-static sensing
      UE-gNB(s) bi-static sensing
      Network-based bi/multi-static sensing
  Study modifications to the 3GPP SCM to support the necessary parametrization to evaluate ICAS
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners
*RWS-230472: Views on Integrated Communication and Sensing for Rel-19

## Slide 15
Network Energy Savings enhancements

## Slide 16: RAN1-led WI: Network Energy Savings Enhancements
Justification and Motivation
Despite the lean design of 5G, the radio continues to be one of the main drivers of energy consumption in the radio access network
Power amplifiers (PAs) make up about half of the radio’s energy consumption and together, PAs and front-ends incl. data conversion make up the bulk of the radio’s energy consumption
The “greenest” transmission is the one that never happened, but utmost dynamicity is not always feasible and practically realizable
Key Objectives
Extend the “intra-carrier” 5G NR lean design into the frequency domain across carriers/cells
  Multi-carrier energy savings enhancements incl. further overhead reductions in time and frequency domain
Complete the Rel. 18 study on power domain techniques for potential standardization
  Over the air digital pre-distortion
  UE post distortion
Continue to drive simplification into the 5G NR specifications, specifically as it relates to massive antenna deployments
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners
?

## Slide 17
Ambient IoT

## Slide 18: RAN1-led SI: Ambient IoT
Justification and Motivation
  Follow-on WG-level Study Item that builds upon the recommendations and conclusions of the ongoing RAN-level “Study on Ambient IoT”, TR 38.848, and TR 22.840 that is being developed by SA1 to capture use cases, traffic scenarios, device constraints of ambient power-enabled Internet of Things
  For enhanced support of public safety applications that require critical infrastructure sensors and monitors
  Target new “green” types of devices that are powered by energy that is provided through the harvesting of e.g., radio waves, light, motion, heat, including devices that are batteryless or have limited energy storage capabilities.
Key Objectives
  Study a new type of IoT technology, independent from the existing 3GPP IoT technologies, e.g., NB-IoT, eMTC, RedCap, etc.
  Define device requirements, deployment scenarios and their characteristics, at least for the use cases/services agreed in SA1’s “Study on Ambient power-enabled internet of Things” and those defined in TR 38.848.
  Evaluation of potential target design characteristics and solutions for the relevant use cases, such as, power consumption, complexity, coverage, data rates, and positioning capabilities.
  Define device categorization based on ambient power characteristics (e.g., energy source, energy storage capability, passive/active transmission, etc.)
  Evaluation of higher layer solutions and protocols to support a new IoT device categorization
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 19
AI/ML (Summary of RWS-230473)

## Slide 20: AI/ML for NR Air Interface
Background and Motivation
  Continue to evolve common framework to support the AI/ML model training, transfer and LCM on PHY in (near) real time
  Limited use cases explored in Rel-18 due to workload
Key Objectives
  Prioritize WI for Rel-18 use-cases based on relative performance gain vs complexity
    Beam Management
    CSI enhancement
      CSI prediction
      CSI compression
    Positioning (Reduce number of sub use cases)
  Simple and common framework for LCM across the AI/ML use cases (RAN1/2)
  Optimized data collection enhancement for AI/ML use cases (RAN2)
  Test and performance requirements (RAN4)
  Study new AI/ML use cases for PHY
    Mobility enhancement (RAN2)
    RS overhead optimization (RAN1)
  Study framework enhancements for joint AI/ML use cases (RAN1)
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners
AI/ML
AI/ML
AI/ML

## Slide 21: AI/ML for NG-RAN
Justification and Motivation
  AI/ML algorithms embedded in the RAN to enable (near) real-time decisions with distributed data
  Interface enhancements to support training and LCM with fallback in multi-vendor deployments
  SI-phase for new use cases going beyond Rel-18
Key Objectives
  Further enhancements for Rel-18 use cases to support more dynamic optimization:
    AI/ML based mobility enhancement: Support for LTM and CHO (RAN3/RAN2)
    AI/ML based load balancing: Extend to CA/DC scenarios, DL/UL coverage + capacity metrics (RAN3)
  Dynamic cell-shaping with multi-cell/OAM coordination (RAN3/RAN1)
  User-clustering based scheduling and RRM (RAN3/RAN2)
  AI/ML based network slice management (RAN3)
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners
TRP
TRP
gNB
gNB

## Slide 22
Further Sidelink Enhancements

## Slide 23: WI Further Sidelink Enhancements
Justification and Motivation
  For enhanced support of applications and use cases requiring sidelink, further enhancements are necessary in order to introduce the solutions identified during the Rel-17 RAN FS_NR_SL_relay study item and ProSe phase 2 in SA investigating further 5G system enhancements to support Proximity Services.
    Additionally, remaining items down-scoped from NR sidelink evolution (NR_SL_enh2), e.g., SL CA, Power Saving enhancements, etc.
  Support of carrier aggregation facilitates the efficient use of fragmented SL frequency spectrum
    Enables larger bandwidths allowing for improved data rates and reliability, enabling public safety and commercial services.
  Support of UE-to-UE multi-hop relay is essential for the sidelink coverage and reliability improvements without relying on the use of uplink and downlink.
  Service continuity enhancements in UE-to-Network multi-path relay are necessary to cover the mobility scenarios not currently supported, provide higher data rate and higher reliability.
Key Objectives
  Specify mechanisms to support NR sidelink CA operation based on LTE sidelink CA operation for at least intra and inter-band CA for FR1 licensed spectrum
  Specify mechanisms for Power saving techniques, e.g., SL DRX enhancements, WUS and BWP adaptation for SL.
  Specify mechanisms to support multi-hop Layer-2 UE-to-UE relay (and possibly L3)
  Specify mechanisms to enhance service continuity for multi-path/hop Layer-2 UE-to-Network relay
  Accuracy, latency, and reliability improvements for SL positioning and ranging
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 24
XR

## Slide 25: RAN2-led WI: XR
Justification and Motivation
  Multi-device interactions and user mobility make XR traffic scalability challenging
  E2E QoE combines spatial, temporal and interactivity measures as a function of network KPIs
  Significant opportunities for cross-layer App/RAN optimizations to improve E2E QoE and network scalability
Key Objectives …
  Paired/tethered device status and user-context XR-awareness enhancements (RAN2)
  Real-time QoE monitoring within the RAN and/or UEs (RAN2)
  Multi-carrier scheduling and power savings enhancements (RAN1)
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 26
UAV enhancements

## Slide 27: RAN2-led WI: UAV enhancements
Justification and Motivation
  To enhance support for advanced UAS/UAV verticals
    Advanced application support, e.g., UAV-to-UAV communication,
  Remaining items down-scoped from earlier releases
Key Objectives …
RAN2 objectives
  Ongoing mobility enhancements potentially including UAV-specific CHO and flight-path reporting / prediction
  Refinement of measurement report triggering
  Enablement for airborne IAB
  PC5-based U2X
Additionally, from RAN1 perspective: Further study and specify UL interference mitigation solutions for uncrewed aerial vehicles, taking into consideration, e.g., beam-related information and capabilities.
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 28
Multicast/broadcast enhancements

## Slide 29: RAN2-led WI: Multicast/broadcast enhancements
Justification and Motivation
  Enhanced support of Multicast applications and use cases
    Focus on Mission Critical applications, i.e., output of MCOver5MBS work item
  Support Multicast mobility enhancements to support Mission Critical use cases
  Items down-scoped in prior releases
Key Objectives …
  Specification of:
    Enhanced Multicast Reliability, QoS
    Mobility between different RAT types
    MR-DC support
    Power Saving Enhancements
    Enhanced operation in RRC_INACTIVE
    Extensions for RedCap scenarios
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 30
Rel-19 Meeting Efficiency Improvements

## Slide 31: General Rel-19 productivity enhancements
Approaches to improve productivity and meeting efficiency
Meeting arrangements
  Mix of F2F and e-meetings beyond 2024
    bis meetings continue as e-meetings with limited scope/only certain AIs and WGs
    Maximum 3 TSG F2F meetings/yr. (remainder e-meetings)
    Continue to leverage, where appropriate, e-meeting tools, e.g., NWM, email discussions, etc.
Clear, realistic, and fixed release timelines and internal WG milestones
Aligned objectives and timelines between TSGs
  Coordination/(down)scoping as necessary
Carefully and well-defined WIs to ensure completion in the Release timing
© 2023 AT&T Intellectual Property. AT&T and globe logo are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners

## Slide 32
Thanks