## Slide 1: R19 RAN Slicing enhancement
3GPP TSG RAN R19 workshop
Taipei, 15th – 16th June, 2023
RWS-230089
Xiaomi

## Slide 2: Slice aware RACH partitioning in connected mode
Motivation
  In Rel-17, RAN Slicing only support Slice aware RACH partitioning for idle/inactive UE.
  In connected mode, RACH can be triggered by data arrival of LCH carring slice specific data if there is no valid SR resource configured for the LCH.
    Assuming LCH(s) belonging to slice(s) will always be configured with SR resources restrict network implementation.
    SR resources can become invalid when UL synchronization is lost.
Objective
  Specify Slice aware RACH partitioning in connected mode

## Slide 3: Slice aware RACH partitioning for MT traffic
Motivation
  In Rel-17, RAN Slicing only support Slice aware RACH partitioning for MO traffic.
  There is no slice information in paging, UE has to use common RACH resources for all the MT traffic, thereby suffering from congestion in the common RACH resource.
Objective
  Specify Slice aware RACH partitioning for MT traffic

## Slide 4: Fast access to the cell supporting the intended slice
Motivation
  In Rel-17, if the slice triggering RRC establishment/resume procedure is not supported by the camped cell, UE needs to access this cell first and then network can handover UE to a different cell supporting the slice or configure a SCell that supports the slice.
    It will introduce a lot of signalling and delay
Objective
  Specify mechanism to support UE fast access to the cell supporting the intended Slice if the slice(s) triggering RRC connection setup/resume is not supported by the serving cell.

## Slide 5: Summary
Objectives
  Specify Slice aware RACH partitioning in connected mode[RAN2].
  Specify Slice aware RACH partitioning for MT traffic[RAN2].
  Specify mechanism to support UE fast access to the cell supporting the intended Slice if the slice(s) triggering RRC connection setup/resume is not supported by the serving cell[RAN2].

## Slide 6: Thanks