## Slide 1: Views on Ambient IoT for R19
3GPP RAN-Release 19 workshop
Taipei, 15th – 16th June, 2023
RWS-230099
Xiaomi

## Slide 2: Brief conclusions from R18 RAN study
Use case | Topology
Grouping A: - Indoor - Outdoor - Indoor/outdoor | Topology 1: BS ↔ Ambient IoT device Topology 2: BS ↔ intermediate node ↔ Ambient IoT device Topology 3: BS ↔ assisting node ↔ Ambient IoT device ↔ BS Topology 4: UE ↔ Ambient IoT device
Device category | RAN design targets
- Device A: No energy storage, no independent signal generation/amplification, i.e. backscattering transmission. - Device B: Has energy storage, no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals. - Device C: Has energy storage, has independent signal generation, i.e., active RF components for transmission. | - Device power consumption - Device complexity - Coverage - User experienced data rate - Maximum message size - Latency - Positioning accuracy - Connection/device density - Moving speed of device
Grouping B:
- Inventory
- Sensors
- Positioning
- Command
Observation: The high level study of Ambient IoT in RAN shows extensive use cases and commercial prospect.
Proposal: Support R19 SI for Ambient IoT for detailed technical discussions.

## Slide 3: Objectives for R19 SI
Proposal: Based on RAN study, suggest RAN to consider the following objectives for R19 SI,
(1) Study waveforms for low power consumption for ambient IoT air interface, including evaluations on data rate/coverage/detection performance/coexistence performance.
(2) Study L1 channels design based on low power waveform.
(3) Study L1 procedures, including scheduling/resource collision avoidance, for the following devices and architectures
Device categories:
    Device A
    Device B
    Device C
Architectures:
    without intermediate/assisting node between gNB and ambient IoT device
    with intermediate /assisting node between gNB and ambient IoT device.
(4) Study lightweight protocol stack and convenient data transmission procedure based on non-state transition and non-dedicated bearer.
(5) Study the mobility and tracking of ambient IoT device.
(6) Study identification and lifecycle management of ambient IoT device.
Note: device A/B can be prioritized if to downsize the SI scope

## Slide 4: Thanks