## Slide 1: Motivation for Integrated Sensing and Communication
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
RWS-230105
Xiaomi

## Slide 2: Use cases from SA1 FS_Sensing
Observation 1: The use cases provided by SA1 need to be grouped/categorized/prioritized to facilitate the RAN study/evaluation.
3GPP TR 22.837 includes 32 use cases, which can be classified in RAN as follows:
Indoor (home, office and factory)
Highway (automotive, traffic monitoring and intrusion detection)
High-speed railway (autopilot and intrusion detection)
Weather forecast (rainfall and flooding)
UAV (flight trajectory tracing, UAV collision and intrusion detection)
Traffic management (tourist/sports hotspot detection and car parking)
Health monitoring (heart-beating, breathing and sleeping)
XR (gaming and metaverse)

## Slide 3: ISAC modes from SA1 FS_Sensing
Option 1: Mono-static sensing via UE
Option 2: Mono-static sensing via gNB
Option 3: Bi-static sensing from gNB to UE
Option 4: Bi-static sensing from UE to gNB
Option 5: Bi-static sensing from gNB to gNB
Option 6: Bi-static sensing from UE to UE
Observation 2: The ISAC modes discussed by SA1 need more RAN implementation details, e.g. how to calculate the corresponding measurements (e.g. range, angle and speed).

## Slide 4: ISAC metrics from SA1 FS_Sensing
Observation 3: The ISAC metrics provided by SA1 need to be selected and mapped to RAN metrics.
The metrics from 22.837:
Confidence level [%]
Accuracy of positioning estimate by sensing (for a target confidence level)
  Horizontal [m]
  Vertical [m]
Accuracy of velocity estimate by sensing (for a target confidence level)
  Horizontal [m/s]
  Vertical [m/s]
Sensing resolution
  Range resolution [m]
  Velocity resolution (horizontal/ vertical) [m/s x m/s]
Max sensing service latency [ms]
Refreshing rate [s]
Missed detection [%]
False alarm [%]

## Slide 5: Study procedure expected in RAN and SA2
5GC Architecture Option 2:
reusing eLCS/Ranging_SL architecture
5GC Architecture Option 1:
new NF and new reference point
SA2
RAN
RAN3: To define a new type of sensing PDU session with sensing QoS requirements provided from CN to gNB.
RAN2: To ensure the QoS requirements at the UE or the gNB via a new type of sensing PDU session.
RAN1: To ensure the QoS requirements at the UE or the gNB via proper sensing signal, controlling procedures, and sensing resource configuration, and to define the sensing measurement results.
RAN3: To enhanced NRPPa to provide sensing measurement results from gNB to CN and to provide the sensing resource configuration to the gNB via the coordination between CN to gNB.
RAN2: To enhanced LPP to provide sensing measurement results from UE to CN and to provide the sensing resource configuration to the UE via the coordination between CN to gNB.
RAN1: To provide proper sensing signal, controlling procedures, and sensing resource configuration required by NRPPa and LPP with certain QoS requirement, and to define the sensing measurement results.
QoS mechanism and QoS handling
Observation 4: The performance evaluation of sensing solution is required while specifying the control signaling and measurement reporting for ISAC.

## Slide 6: Channel Modelling for ISAC
To evaluate the performance of ISAC solutions, a new channel model is needed to characterize the concatenated links:
  1st link: Sensing signal is transmitted from sensing Tx to target
  2nd link: Sensing signal reflected/scattered by target is received by sensing Rx
  Clutter link: Sensing signal not reflected/scattered by target is received by sensing Rx
The channel model in TR 38.901 needs to be modified for the end-to-end channel from Tx to Rx with the reflecting/scattering by a (moving) target.
Tx/Rx
Target
Tx/Rx
Target
Tx/Rx
Target
Tx
Rx
Target
Tx
Rx
Target
Tx
Rx
Target
Tx sends sensing signal over 1st link.
Rx receives sensing signal reflected/scattered by target over 2nd link
Rx receives sensing signal not reflected/scattered by target, a.k.a. clutters.
Monostatic
mode
Bistatic
mode
Observation 5: To evaluate the performance of ISAC solutions, RAN needs to modify the channel model in TR 38.901.

## Slide 7: Conclusion
Considering all the commercial use cases studied by SA1 FS_Sensing, ISAC is expected to be a promising feature for 5G.
Observation 1: The use cases provided by SA1 need to be grouped/categorized/prioritized to facilitate the RAN study/evaluation.
Observation 2: The ISAC solutions discussed by SA1 need more RAN implementation details, e.g. how to calculate the corresponding measurements (e.g. range, angle and speed).
Observation 3: The ISAC metrics provided by SA1 need to be selected and mapped to RAN metrics.
Observation 4: The performance evaluation of sensing solution is required while specifying the control signaling and measurement reporting for ISAC.
Observation 5: To evaluate the performance of ISAC solutions, RAN needs to modify the channel model in TR 38.901.
Proposal 1: ISAC is included in Rel-19.
Proposal 2: The ISAC study in Rel-19 includes at least:
  Study of use cases
  Study of ISAC solutions
  Identification of evaluation metrics
  Design of channel models

## Slide 8: Thanks