## Slide 1: Motivation for dynamic UE capability update
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
RWS-230106
Xiaomi

## Slide 2: Background
RAN2 discussed/specified several solutions related to UE capability sharing and updating in different releases and items
  Rel-15
    Reduced capability (i.e. maximum CCs / BW / MIMO-layers) for overheating
  Rel-16
    FDM assistance information for IDC interference
    Preferred DRX / “Maximum bandwidth / CC(s) / MIMO-layers”/ “minimum scheduling offset” for power saving
  Rel-17
    Preferred “gap pattern” for MUSIM
    Reduced capability (i.e. maximum BW / MIMO-layers) for overheating
    Preferred “Maximum bandwidth / MIMO-layers”/ “minimum scheduling offset” for power saving
  Rel-18
    FDM and TDM assistance information for IDC interference
    Preferred UE capability for MUSIM (i.e. shared UE capability between two SIMs)
    Preferred UE capability for MBS (i.e. shared UE capability between unicast and MBS)
Observation 1: In each release, the UE is required to provide assistance information for its preferred capabilities for different purposes (e.g. overheating/IDC/MUSIM/power saving).

## Slide 3: Issues of the current RAN2 specification
The dynamic UE capability updating/sharing solutions specified in the current specification have the following issues:
  Some solutions can be unified for different purposes (e.g. TDM for MUSIM / IDC / power saving / MBS; maximum CCs / BW / MIMO-layers for power saving / overheating).
  No TDM solution for the UE capability sharing between MBS and unicast.
  The capability bits updating in each release would require the discussion for the dynamic UE capability updating/sharing solutions, which causes lots of standard effort.
  The fragmented solutions for the dynamic UE capability updating/sharing require lots of implementation efforts at the UE and the gNB.
According to the capability reporting procedure, the UE can only report its capability requested by the network, and unable to update its capability dynamically via the capability reporting procedure. Thus the UE is forced to use (re-)attach procedure to update its capability for MUSIM / IDC / power saving / overheating / MBS.
Observation 2: The fragmented solutions for the dynamic UE capability updating/sharing require lots of implementation efforts at the UE and the gNB.
Observation 3: The UE is not able to update its capability dynamically via the capability reporting procedure.

## Slide 4: Unified solution for UE capability sharing and updating
It is feasible to have unified solutions for UE capability sharing and updating for different purposes (e.g. overheating/IDC/MUSIM/power saving/MBS).
  The unified solution can be future-proof while new capability bits are added.
  The unified solution can be used for different MR-DC architecture and for intra-/inter-PLMN scenarios.
  The unified solution can be FDMed or TDMed or any capability updating via the control of the network.
  The unified solution can simplify the implementation at the UE and the network.
Observation 4: It is feasible to have unified and future-proof solutions for UE capability sharing and updating for different purposes (e.g. overheating/IDC/MUSIM/power saving/MBS).

## Slide 5: Conclusion
Observation 1: In each release, the UE is required to provide assistance information for its preferred capabilities for different purposes (e.g. overheating/IDC/MUSIM/power saving/MBS).
Observation 2: The fragmented solutions for the dynamic UE capability updating/sharing require lots of implementation efforts at the UE and the gNB.
Observation 3: The UE is not able to update its capability dynamically via the capability reporting procedure.
Observation 4: It is feasible to have unified and future-proof solutions for UE capability sharing and updating for different purposes (e.g. overheating/IDC/MUSIM/power saving/MBS).
Proposal: The dynamic UE capability update in Rel-19 RAN2 includes the following objective:
To specify unified solution(s) for dynamic UE capability update or sharing, due to different purposes (e.g. overheating/IDC/MUSIM/power saving/MBS)
Note 1: The solution(s) should be still applicable when new UE capability bits are added in the future release.
Note 2: The solution(s) should be applicable for different MR-DC architectures and for intra-/inter-PLMN cases.
Note 3: The solution(s) should be applicable for different UE capability reporting procedures, i.e. UE capability ID-based reporting procedure and UE capability enquiry procedure with/without capability filter.

## Slide 6: Thanks