## Slide 1
Huawei, HiSilicon
Integrated Sensing and Communications in Rel-19
RAN/CN support to enable wide-area
network-based sensing
3GPP TSG RAN Rel-19 workshop RWS-230186
Taipei, June 15 - 16, 2023

## Slide 2
Background
3GPP SA1 is studying use cases and requirements for integrated sensing and communications in NR
Work Item | SID | Status
Study on Integrated Sensing and Communication | SP-220717 (SA1#97e) | 80% (SA1#101)
The objectives of the study include: - Study use cases and potential requirements for enhancement of the 5G system to provide integrated communication and sensing services addressing different target verticals/applications, e.g. autonomous/assisted driving, V2X, aviation/UAVs, 3D map reconstruction, smart city/factories, public sectors, healthcare, smart home, maritime sector.
There are already 32 use cases in 5 categories captured in the TR 22.837
We propose to prioritize Transportation and UAV cases in Rel-19
Transportation
UAV
Smart Home
Smart City
Smart factory
Intrusion detection on a highway
Sensing assisted automotive maneuvering and navigation
……
UAV flight trajectory tracing
Sensing for UAV intrusion detection
……
Intruder detection in smart home
Health monitoring at home
……
Rainfall monitoring
Tourist spot traffic management
AGV detection and tracking in factories

## Slide 3
Sensing Modes & Frequency Range
For use cases that require wide range sensing capability, e.g., transportation and UAV detection, network-based sensing modes is the most suitable choice as gNB has much higher transmit power, larger antenna array than UE, and the necessary coverage for these use cases can be guaranteed by suitable network deployment
The sensing capability can be developed for both FR1 and FR2. From our experience, the sensing accuracy and resolution of FR2 is superior than FR1 due to its larger bandwidth and larger antenna array
Monostatic sensing mode (Prioritized)
Bistatic sensing mode

## Slide 4
RAN can support network-based sensing by implementation…
No RAN1 (Uu interface) impact for network-based sensing
Solution:
Sensing and communication can be multiplexed in time-domain, i.e., one or two symbols of DL slot are used for sensing only
Comm.
Sensing symbol
Time
Freq.
Specification support:
NR Rel-15 supports RB-symbol level reserved resource which can be used to make sensing symbols be rate-matched for PDSCH, which is transparent to UE
Prototype and Testing Results
The effectiveness for network-based sensing for transport and UAV scenarios have been verified by prototype (in FR2)
UI Display
BBU
AAU
Signal processing and information computing
Car sensing
Detection distance > 500m
Lane level detection
UAV detection
Detection distance >1km
Meter-level accuracy

## Slide 5
… but enabling E2E sensing service requires standardization work
Sensing
Communication
UE
Object (not a UE)
RAN
Sensing signal transmission, echo signal reception and measurement
5GC
Third party
…
Computing target characteristics
(Position, Velocity, Size, etc.)
Sensing service application
 | Content | Description
Time | t (s) | Instantaneous time snapshot.
Location | x (m) | The position of a target/scatter in 3D coordinate system.
 | y (m) | 
 | z (m) | 
Velocity | v (m/s) | The speed of a target/scatter.
Moving direction | dh (degree) | The moving direction of a target/scatter in horizontal and vertical domain
 | dv (degree) | 
1
2
Target
Point Cloud
scatter
RAN-CN
Interface
Sensed Object
RAN3 impacts：
RAN need to report sensing measurements to 5GC, and the data format for sensing procedures need to be specified between RAN3 and SA2
Examples: RAN provides the relevant information about the location and velocity of scatters/targets in contiguous time period units to 5GC

## Slide 6
About Channel Model
The channel model is generally used for Uu interface performance evaluation
The performance evaluation is used to justify the inclusion of proposed Uu interface solutions in the specifications
For Network-Based Integrated Sensing, specification impact on Uu interface is not expected in Rel-19
Thus the proposed work scope does not need a performance evaluation or channel model

## Slide 7
Integrated Sensing and Communications in Rel-19 Work Proposal
RAN signaling to support Integrated Sensing and Communications:
  Study and specify the procedures enhancement to support the Integrated Sensing and Communications architecture, as defined by SA2
  Study and specify signaling interactions to support Integrated Sensing and Communications including the sensing initiation, sensing result report and etc.
  Study and specify the sensing object result to report, e.g. Point Cloud, if needed in collaboration with SA2
  Note: the support of the transmissions/reception signals used for sensing by the base station, are assumed to avoid interference with signals/channels used for communication, by using reserved resources

## Slide 8
Appendix A: Use Case - Smart Transportation
Wireless sensing is becoming essence on roads
 | Frequency | Bandwidth | EIRP | Sensing Distance | Range Resolution | Angle Accuracy
ISAC | 26~28GHz | 400~800MHz | >70dBm | >1000m | 0.2~0.4m | 0.1°
Transport Radar | 24GHz | 200M | 13dBm | 200m | 1m | 0.5°
 | 77GHz | <100MHz LR | 42dBm | 500m | > 1.5m LR | 0.1°
ISAC has advantages compared to transport radar
Requirements:
Road owners require wireless sensing in important roads (highway, busy intersections) for better traffic monitoring and management
Wireless sensing has the advantages in all-weather and long distance sensing
Market:
There are already commercial deployments of Radar & Camera in highways, and the shipment of transport radar in China will reach 300 K units in 2024
26~28GHz mmWave ISAC vs 24GHz/77GHz transport radar
Wider Bandwidth leads to >4x improvement for range resolution
Higher EIRP leads to >2x improvement for sensing distance
Note: The typical value for long range (LR) of transport radar is from 100m to 500m.
Sensing in bad weather
Accurate Risk Finding
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 3.95 | 6.38 | 11.02 | 13.05 | 15 | 17.03 | 19.3347 | 21.6549 | 24.0369 | 26.4406 | 29.0847
Shipment of transport radar in China
(Unit: Ten thousand)
Source: from Internet

## Slide 9
Appendix B: Use Case - UAV invading detection
ISAC Has Both Cost and Performance Advantages
The requirement for UAV Invading Detection is urgent
 | ISAC | UAV Detection Radar | TDoA
Sites | Shared with communication | Need new sites | Need new sites
Spectrum | License bands Shared with communication | Ku/X (Need provisional application for spectrum in advance, cannot work in 7*24h) | 100MHz~6GHz (Passive)
Performance | Position Accuracy <10m | Position Accuracy >10m | Position Accuracy >50m
Others |  |  | Can not detect radio-silent UAVs
Requirements:
From Police: Protect the safety in public areas, especially important places
From Commercial: Prevent UAVs Invading from causing accident and stealing confidential information
Market:
In China: The total markets for Anti-drone from 2020 to 2025 will reach ￥33 billion, and touchable UAV detection market will be ￥ 16 billion.
DRONE INDUSTRY INSIGHTS (Germany): Anti-Drone market $6.6 billion by 2024, CAGR 41.4%, will reach $50 billion by 2030. The touchable UAV detection market will reach 12 billion by 2030
Stadium
Celebration
Enterprises
Source: from Internet