## Slide 1
Huawei, HiSilicon
Support for emergency services in Rel-19
flexible multi-hop and multi-path IAB network
3GPP TSG RAN Rel-19 workshop RWS-230187
Taipei, June 15 - 16, 2023

## Slide 2
Motivations
Emergency services need nationwide network
On-spot video backhaul to the command center
Forest Patrol
Forest Fire Fighting
Disaster Relief
In many countries around the world, the spectrum of emergency network is mainly 700 MHz, with a bandwidth of 10~20 MHz
Mesh network is resilient for onsite command links, and the maximum number of hops is less than 6
Emergency network
Helmet Camera
Backpack BS
Command Center
Video requirements
On-spot personnel should be equipped with video capture devices with resolution higher than 720p (about 2Mbps)
In China, "14th Five-Year Plan for National Emergency Response System" proposes to build a nationwide emergency broadband wireless network

## Slide 3
Scenarios
Scenario1: 20Km remote area
Scenario2: urban deep coverage
First Site
Vehicle BS
Backpack BS
UAV BS
Fixed BS
20 Km
Emergency scenario of remote area:
Out of coverage for dozens of kilometers (e.g. 20Km)
One fixed vehicle-mounted temporary base station at the edge of the first site, which serves as donor gNB.
Multiple mobile BS equipped on body or drone in the first site.
High transmit power to combat path loss and blockage
There are more than 40,000 cities, with an average area of about 200 square kilometers
Objective: achieve 95% coverage for 2Mbps on-spot video backhaul in 20km area and urban deep coverage area
Underground floor
High-rise building
Emergency scenario of urban deep area:
Poor coverage In the underground, tunnel, high-rise building, etc.
One fixed vehicle-mounted temporary base station or undamaged base station, which serves as donor gNB.
Multiple mobile BS equipped on body, drone, etc.
Limited transmit power to avoid interference in narrow space
In city, there are about 15,000 super high-rise buildings (above 100 meters), 5,000 subway stations and 25,000 highway tunnels

## Slide 4
Flexible multi-hop & multi-path topology
Tree Topology
DAG Topology
Mesh Topology
IAB-donor
Parent
Child
D
1
2
3
4
S
5
Path 1
Path 2
Path 3
D
1
2
3
4
S
5
1 hop
D
1
2
3
4
S
5
Multi-hops
Path 1
1-hop IAB
Rel-16
Multi-hop IAB
Rel-16
Multi-hop & Multi-path IAB
Rel-17
Rel-19 (path 3)
IAB-donor
node
Neighbor node
DU
MT
node1
DU
Donor
CU
DU
MT
node3
UE1
DU
MT
node2
DU
MT
node4
UE2
Node1&2 or node3&4 switch their parent-child relationship
Any node has more than two paths to against blockage or mobility
One example of multi-hop & multi-path topology
Rel-19 (path 3)

## Slide 5
Intermediate node fast rerouting
Disadvantages:
RLF-triggered rerouting usually has hundreds of milliseconds delay
When the latency exceeds 50 milliseconds, real-time video frame freezing and frame loss will happen
Advantages:
Intermediate node selects best path based on the path QoS without waiting for the RLF
Intermediate node directly performs rerouting decision, which doesn’t introduce extra delay
Rerouting based on RLF or congestion
Rel-16 & Rel-17
2) Intermediate node fast rerouting based on path QoS
Rel-19
Discover RLF
1
2
3
4
5
Path1
Path2
Path Switch
Path2 QoS > Path1 QoS
1
2
3
4
5
Path1
Path2
Path Switch

## Slide 6
Backhaul Adaption Protocol (BAP) duplication forwarding
Node1
Node2
Node3
BS
BAP duplication
TDM/FDM
Node4
Motivation:
Currently only support PDCP duplication, which can’t ensure the two duplicated packets routed in different paths
Advantages:
In multi-hop & multi-path scenarios, duplication ensures reliable coverage through redundant paths

## Slide 7
Slice-specific backhaul configuration
Motivation:
Only the access IAB-DU is aware of the S-NSSAI of each DRB
Upstream IAB(Donor)-DUs: unaware of the slice(s) held on each Backhaul RLC Channel
The backhaul link cannot implement slice-specific RRM
Advantages:
Appropriate backhaul radio resource processing for different emergency service types (e.g., on-spot video, on-site command, and telemedicine. etc) can be achieved

## Slide 8
Support for emergency services in Rel-19 Work Proposal
Specify mechanism with minimum specification impact to support flexible multi-hop and multi-path topology based on IAB architecture only for intra-CU case:
  Flexible topology enhancement, allowing e.g. switch parent/child relationship, service continuity against node moving (leaving or joining), more than two paths, …
  Intermediate node selection of better path based on path QoS
  BAP duplication forwarding to ensure the same date routed in different path
  Slice-specific backhaul configuration

## Slide 9
Parameter | Value
Bandwidth | 15M@700M
Area | 20*20Km
Donor BS number | 1
Mobile BS number | 16
Mobile BS distribution | random
Maximum TX power | 2*10W
Traffic concurrency ratio | 50%
on-spot multiple 2Mbps videos backhaul to the donor BS
Scenario1: Remote Area
Appendix – A: System Level Simulation Results
Parameter | Value
Bandwidth | 15M@700M
Area | 500*500m
Donor BS number | 1
Mobile BS number | 16
Mobile BS distribution | random
Maximum TX power | 2*1W
Traffic concurrency ratio | 50%
on-spot multiple 2Mbps videos backhaul to the donor BS
Scenario2: Urban deep coverage

## Slide 10
Parameters | Value
Carrier frequency, SCS | 700M, 15KHz
System bandwidth | 2*15MHz
Antenna | Fixed BS:4TX4RX, Mesh Node:2TX2RX
Duplexing | FDD
Deployment | Scenario: Indoor, 2 outdoor sites, 6 cells ISD 500m, O2I 20dB loss
Traffic | Periodic (720p 2Mbps Application Rate)
Number of nodes | 100 / 6 cells
Delay budget | 50 ms
Maximum hops number | 4
Target BLER | 10%
HARQ | On
Scheduler | PF scheduling
Node speed | 3 km/h
Node distribution | Random, 20% mobility, 80% non-mobility
MIMO | SU-MIMO (rank2 adaptation)
Urban deep coverage
Remote Area
Appendix - B: simulation configurations
Parameters | Value
Carrier frequency, SCS | 700M, 15KHz
System bandwidth | 2*15MHz
Antenna | Fixed BS:4TX4RX, Mesh Node:2TX2RX
Duplexing | FDD
Deployment | Scenario: Rural Area, 2sites, 6 cells ISD 20Km
Traffic | Periodic (720p 2Mbps Application Rate)
Number of nodes | 100 / 6 cells
Delay budget | 50 ms
Maximum hops number | 6
Target BLER | 10%
HARQ | On
Scheduler | PF scheduling
Node speed | 3 km/h
Node distribution | Random, 20% mobility, 80% non-mobility
MIMO | SU-MIMO (rank2 adaptation)