## Slide 1
Huawei, HiSilicon
AI/ML for NG-RAN in Rel-19
support more use cases
3GPP TSG RAN Rel-19 workshop RWS-230188
Taipei, June 15 - 16, 2023

## Slide 2
General Introduction
Summary of Rel-18
  Artificial Intelligence / Machine Learning (AI/ML) for NG-RAN principles achieved in Rel-18
    AI/ML algorithms and models are out of 3GPP scope
    Details of AI/ML model's performance feedback are out of 3GPP scope
    Base on existing RAN architecture, data security and privacy should be respected
    Signalling procedures between network nodes (mainly on Xn so far) used for the exchange of AI/ML related information (e.g., input, output, feedback, …) are use case and data type agnostic
  RAN3 should finalize the following three use cases
    Network Energy Saving, Load Balancing, Mobility Optimization
  View on AI/ML for NG-RAN in Rel-19
  AI/ML principles achieved in Rel-18 shall still apply to Rel-19
  Rel-19 should enhance Rel-18 use cases if any, and continue to work on potential new use cases which benefit from using AI/ML techniques

## Slide 3
RACH Optimization
Backgrounds
Backgrounds & Challenges
  The conventional RACH optimization is based on RACH configuration information exchanged between NG-RAN nodes and UE RA reports
Challenges
  The current optimization methods only focus on solving RACH problems pop-up
  The NW side currently is not able to foresee potential RACH problems and optimize in advance
Solutions
Solutions & Specification Impacts
  RACH report enhancements and information exchange to predict potential RACH problems
  Inference-based RACH resource optimization
Input for inference
gNB1
gNB2
RACH cfg info
RACH Report
gNB1
UE
gNB2
RACH report enh.
Predicted RACH problems
RACH resource optimization in advance
Specification Impacts
  Additional information exchange over network interfaces, e.g. the optimized RACH configuration based on prediction

## Slide 4
DC mobility optimization
Backgrounds
Backgrounds & Challenges
  The current operations for SN, e.g. SN change, is mainly based on MN-configured UE measurement results
  Both MN and SN can trigger operations for SN
Challenges
  The UE measurement results only reflect the real-time radio quality of neighbor cells
  If MN and SN simultaneously trigger different SN operations, it is necessary to evaluate which one is more rational
Solutions
Solutions & Specification Impacts
  Take UE predicted trajectory from MN and SN into consideration and respectively inference DC operation decisions
  Interaction between MN and SN about inferenced decisions
Interaction about
Inferenced results
MN
SN
Procedures for DC
Measurement
results
MN
UE
SN
AI based DC operation decisions with consensus.
Specification Impacts
  Enabling signaling decision about inferenced results e.g. recommended SN change/addition/release based on AI inference
  The work is limited to NR-DC
Trigger DC operations

## Slide 5
Coverage and Capacity Optimization
Backgrounds
Backgrounds & Challenges
  Each NG-RAN node may be configured with alternative coverage configurations by OAM
  The CCO configuration is usually adjusted when there is a coverage problem or notification of CCO configuration adjustment from neighbor nodes
Challenges
  The coverage and capacity problem currently cannot be foreseen and prevented in advance
Solutions
Solutions & Specification Impacts
  AI-based prediction for cell capacity and coverage, based on e.g. UE trajectory
  Inference-based CCO information exchange between nodes with predicted timing information
Interaction of
Inference CCO strategies
gNB1
gNB2
NG-RAN node
cfg update
gNB1
gNB2
Predicted cell capacity and coverage
Related CCO strategies adjustment
Specification Impacts
  Additional information exchange over network interfaces, e.g. the AI-inferenced CCO configuration, as well as the reason, timing information and advantages to adopt the new CCO configuration
OAM
Alternative coverage cfgs
AI function

## Slide 6
AI/ML for NG-RAN in Rel-19 Work Proposal
The AI/ML principles achieved in Rel-18 apply to Rel-19
Specify signalling support within existing NG-RAN interfaces and architecture (including non-split architecture and split architecture) for potential new use case, such as RACH Optimization, DC mobility optimization, Coverage and Capacity Optimization, etc.