## Slide 1: Overview of LGE’s Proposals on Rel-19 5G-Advanced

## Slide 2: General overview [1/3]
Proposals
Rel-19 time schedule should be kept tightly
  The Rel-19 completion time is closely related to the start of Rel-20, when the 6G study is expected to begin
  Workload of Rel-19 should be controlled moderately to be completed on time within 18 months per WG
2022
2023
2024
2025
2026
2027
2028
2029
2030
Vision
Technical requirements
Evaluation
Decision & Rec
Trends
Vision
Req.
IMT-2030
Recommendation
WRC26
WRC27
R19 6G
channel model SI1)
Stage 1
Requirements
R20 Stage1 Req. SI
R22 6G phase 2 WI
6G Technical
Study Item
Earliest
Possible
6G start time
(‘25.6)
2nd possible
6G start time
(‘25.9)
RAN level requirements
R21 6G phase 1 WI
6G
R21 5G-Adv.
R20 5G-Adv.
R19 5G-Adv.
RAN1
freezing
Core part
freezing
ASN.1
freezing
Important milestones for 6G
  6G channel model study in R19
  6G RAN req. SI: ’24.12 or ‘25.03
  6G technical SI: ‘25.06 or ‘25.09
  Initial phase 6G in R21
  2nd phase 6G in R22
1) sub-THz channel, upper mid-band, RIS channel model, JCAS channel model, etc
R18 5G Adv.

## Slide 3: General overview [2/3]
General consideration on Rel-19
  Rel-18 already includes big SIs or new features (e.g., duplex enhancements, AI/ML for air interface, XR enhancements, Ambient IoT, Positioning evolution, NES, etc.) which may be continued to normative works, or needs to be further enhanced in Rel-19
  Rel-19 should be mainly featured by continuation from Rel-18 SIs and enhancements of Rel-18 features, rather than commencing new big things
  For a couple of features (e.g., JCAS, RIS, upper mid-band, sub-THz etc.,) where industry enthusiasm is observed (mainly targeting for 6G), RAN level (or RAN WG level) preparation study item(s) might be proceeded focusing on deployment scenarios, use cases, and design targets, just as in the case of RAN level study item of ambient IoT within Rel-18
    Earnest technical studies for these features would be better to be commenced in Rel-20 as part of presumably 6G study item
Areas of further evolution for Rel-19
  eMBB evolution
    Further enhanced performance in terms of performance such as throughput, coverage, etc
  Cross Functionalities
    Functionalities applicable both for eMBB and non-eMBB use cases
  Non eMBB evolution
    Further proliferation of 5G NR to more diverse vertical applications
This presentation contains several items of our interest. Of course, Rel-19 package may include other items of great interest to the industry in addition to the items proposed in this presentation

## Slide 4: General overview [3/3]
MIMO further
enhancements
Full Duplex
NR positioning
enhancements
eMBB-driven Functionalities
Rel-19
Functionalities
NTN further enhancement
Sidelink
enhancements
AI/ML for Radio
AI/ML for NG-RAN
ML-aided Predictive mobility
XR enhancements
MBS further
enhancements
Non eMBB-driven
Functionalities
Support for
Cross Functionalities
Network Energy Saving enhancements
Ambient IoT
Rel-19 functionalities provided in this presentation can be categorized as in the following figure
Sidelink relay
enhancements
SDT enhancements
LTM
enhancements
Overhead reduction
* Above categorization is just for the purpose of explanation. Different companies may have different understanding

## Slide 5: eMBB-driven Functional Evolution
MIMO further enhancements
In Rel-17/Rel-18 MIMO, UE multi-panel features such as panel-specific beam report, simultaneous Tx across multi-panel (STxMP), and panel/TRP-specific TA have been introduced to improve UL performance.
Duplex enhancements
These features are useful especially for various applications of vehicle UEs in FR1 as well as in FR2 as indicated in the LSs from 5GAA[RWS-210360][R1-2205116].
However, these features are still under quite limited scope and need further enhancements
Start normative work based on conclusion from Rel-18 duplex enhancement SI
Rel-19 WI consists of normative work for:
SBFD operation
Co-channel CLI handling for SBFD and dynamic/flexible TDD
eMBB is still quite important service area for commercial telecommunication

## Slide 6: Support for Cross Functionalities [1/2]
Rel-19 should provides further enhancements for cross functionalities in order to better support eMBB commercial use cases and help proliferation of NR technology into various vertical use cases at the same time
AI/ML for radio/
AI/ML for NG-RAN
Mobility Enhancements
(Predictive Mobility,
LTM Enhancements)
Predictive mobility based on predictive measurement results can reduce handover problems, such as HO failures or unnecessary handoff due to myopic HO decisions and frequent link failures in high frequency ranges. ML-based model management specific to predictive mobility is needed
Network Energy Saving Enhancements
Network energy saving needs to be further enhanced to make this feature more usable in further extended scenarios such as multi-TRP, NCR and unlicensed band
For air interface, performance benefit, implementation flexibility, and privacy/proprietary issues, more focused work scope for Rel-19 should be provided, taking into account of completeness of study item
For NG-RAN, AI/ML can be better utilized for couple of use cases such as more robust dual connectivity operation of better support of QoE
LTM needs to be further enhanced to support more robust LTM operation, reduction of CSI measurements and reporting for LTM candidates, inter-CU LTM, deactivation of candidate cell

## Slide 7: Support for Cross Functionalities [2/2]
SDT enhancements
L2 overhead reduction
In order to increase resource utilization, it is necessary to study L2 overhead reduction
NR positioning enhancements
For CPP, further enhancements on the positioning accuracy for various scenarios are necessary in addition to basic functionalities defined in Rel-18
In order to make SDT feature more applicable, SDT specific BWP is needed to provide enough bandwidth for data transmission/reception and avoid congestion on initial BWP
In order to alleviate processing burden required for UPIP (user plane integrity protection) while not jeopardizing security concerns, low burden UPIP aspects need to be studied
For RedCap positioning, low power/low cost UEs and BW limited scenarios need to be considered in addition to the scenario requiring special UE implementation of FH and BW capability
For sidelink positioning, supported bandwidth needs to be extended further by means of utilizing unlicensed spectrum for better positioning accuracy. CPP can be applied for sidelink positioning as well possibly with a narrow bandwidth in FR1 ITS band. Power saving aspects need to be taken into account for battery-driven devices
Longer than 4s SDT procedure is needed to support interactive communication
SPS is needed to support periodic MT-SDT traffic

## Slide 8: Non-eMBB evolution [1/2]
Rel-19 should provides technical advancements in order to accelerate proliferation of 5G NR into more diverse vertical applications
XR Enhancements
MBS Enhancements
Multicast CFR in R18 is quite restrictive and hence needs to be more generalized to support multicast reception from multicast CFR by UEs in RRC_INACTIVE, minimized multicast interruption caused by switching between multicast CFR and initial BWP, and cell re-selection enhancements to guarantee reception quality of multicast in RRC_INACTIVE
In Rel-18, traffic awareness enhancement is limited to discard operation based on PSI (PDU Set Importance) at network congestion. But, it does not fully satisfy requirement of PDU set importance. It is necessary to improve reliability and scheduling for important PDU set.
NTN Enhancements
Remaining service time based mobility needs to be considered for NTN, because NTN cells have limited service time due to the satellite movement
In Rel-18, power saving enhancement is limited to handling non-integer periodicity and SFN wrap around problems in DRX operation. But, it does not bring considerable power saving gain for multiple flows and jitters. It is necessary to improve power saving gain for multiple flows and jitter
Avoidance of RLF/BF declaration at temporal discontinuous coverage needs to be supported taking into account NTN may have discontinuous coverage due to the deployment of satellites and declaration of RLF/BF at discontinuous coverage does not bring any gain

## Slide 9: Non-eMBB evolution [2/2]
Sidelink Communication
Enhancements
Wide channel bandwidth which can be found in FR2, needs to be utilized for various use cases including raw sensor data sharing in V2X and high definition video and XR streaming among devices
To fully address the V2X requirements and potentially make the sidelink CA more useful in other applications, at least Rel-15 LTE features need to be specified for sidelink CA
A frequency domain power saving mechanism is necessary so that a UE can shrink its sidelink operation bandwidth when there is no active traffic
Sidelink Relay
Enhancements
Multi-path relaying aspects needs to be further enhanced to support power saving and reduced UE complexity for intra-gNB
Enhance non-3GPP based UE-to-UE link for intra-gNB case without CN impact (as specified in Rel-18) e.g. for in-car passenger device connectivity using relay in the vehicle mounted UE
Ambient IoT
During Rel-18, RAN level SI for Ambient IoT studies deployment scenarios, design targets and rough estimation of feasibility of Ambient IoT. Further study is necessary for more details focusing on practical scenarios for specification of Ambient IoT
SI should focus on (or prioritize) connectivity topology 1 (BS   Ambient IoT device)
SI should include study on PHY layer DL/UL signal design & L1 procedures to support A-IoT, collision/interference/load handling, and coexistence/harmonization with existing NR signals/channels

## Slide 10: Summary of LGE’s Proposals for each WG
RAN1-led Proposals
WI on duplex evolution [RWS-230193] WI on AI/ML for air interface [RWS-230194] WI on MIMO enhancements [RWS-230195] WI on Positioning enhancements [RWS-230196] WI on enhancements for network energy saving [RWS-230197] SI on ambient IoT (continuation from Rel-18 SI) [RWS-230198] WI on sidelink communication enhancements [RWS-230199]
RAN2-led Proposals
SI on ML-Aided Predictive mobility [RWS-230200] WI on SDT enhancements [RWS-230201] WI on XR enhancements [RWS-230202] WI on LTM enhancements [RWS-230203] WI on sidelink relay [RWS-230204] SI on Layer 2 overhead reduction [RWS-230273] WI on MBS enhancements WI on NTN enhancements
Order of the items in the list has no implication on LGE’s prioritized items
RAN3-led Proposals
WI on AI/ML for NG-RAN enhancements

## Slide 11: Annex: More detailed proposals from LGE

## Slide 12: RAN1-led Rel-19 Proposals

## Slide 13: Duplex evolution
Motivation
  Rel-18 SI on duplex enhancement includes
    Duplex enhancement at gNB side assuming half duplex operation at UE side
    No restriction on frequency range
    SBFD and potential enhancements on dynamic/flexible TDD
  Rel-18 SI is limited to the gain from coexistence handling
    Further evolution on duplexing is expected by spectrum-shared full duplex operation
Proposals
  Start Rel-19 normative work based on Rel-18 duplex enhancement SI
  Rel-19 WI consists of normative work for:
    SBFD operation
    Co-channel CLI handling for SBFD and dynamic/flexible TDD
  While it is desirable to continue study on spectrum shared full duplex operation as the next step of duplex evolution, this work can be considered in further releases (e.g. Rel-20) to focus on normative work for duplex evolution and to keep moderate work load of Rel-19
Objective for Rel-19 Normative Work
  SBFD operation
    Semi-static/dynamic SBFD (SBFD symbol/slot time configuration, Subband configuration)
    Operation in SBFD symbol and non-SBFD symbol (FDRA, MCS, TBS, CSI-RS, CSI Measurement and reporting, PUCCH, SRS, Multi-antenna, CORESET, Search Space, etc.)
    UE behavior for supporting spectrum non-overlapped full duplex capable gNB (DL Rx and UL Tx, Timing advance, Power control, etc.)
  Co-channel CLI handling for SBFD and dynamic/flexible TDD
    gNB-to-gNB CLI handling (co-channel CLI and/or channel measurement, Timing alignment, Time/frequency resource coordination, Spatial domain coordination)
    UE-to-UE CLI handling (L1/L2 based CLI measurement and reporting including co-channel intra-/inter-subband CLI)
DL
UL
DL
Frequency
Subband-wise Full Duplex operation in Rel-19
DL
Carrier BW
UL
Frequency
Spectrum-shared Full Duplex operation for further study
Carrier BW
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 14: AI/ML for NR Air Interface
Motivation
  Rel-18 AI/ML SI studies general framework and 6 sub-use cases including CSI feedback, beam management and positioning. Each sub-use case evaluates performance benefit and assesses potential specification impact.
  In general, AI/ML model based operation provides potential gain compared to existing scheme in terms of performance and/or overhead.
  Some challenging parts are
    Model transfer
    Dataset delivery
    Model identification over-the-air
  In order to facilitate AI/ML applications in NR air-interface, it will be beneficial to start work item with focused scope in Rel-19
  The work scope should be selected based on the following aspects
    Completeness level of study
    Easier adaptation to vendors (e.g. keeping vendor-specific proprietary information)
    Expected performance gain
    Expected amount of specification impact
Proposals for AI/ML WI in Rel-19
  Specify enhanced UE capability framework to facilitate UE-side AI/ML operation (e.g. dynamic update of applicable UE functionality).
  Study and, if needed, specify CSI prediction (1st priority) or CSI compression with limited training collaboration type(s) (2nd priority).
  Specify spatial/temporal DL Tx beam prediction based on one-sided AI/ML model.
  Specify direct AI/ML positioning based one-sided model.
  Above use cases should be considered following aspects
    Focus on signaling-based collaboration without model transfer (collaboration level y only).
    Focus on offline training only.
    Specification impact on
      Data collection without RS enhancement,
      Inference,
      Functionality/model based LCM operation.
Figure 1. Illustration of CSI compression
Figure 2. Illustration of beam prediction
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 15: MIMO enhancements
Motivation
  In Rel-17/Rel-18 MIMO, UE multi-panel features such as panel-specific beam report, simultaneous Tx across multi-panel (STxMP), and panel/TRP-specific TA have been introduced to improve UL performance. These features are useful especially for various applications of vehicle UEs in FR1 as well as in FR2 as indicated in the LSs from 5GAA[RWS-210360][R1-2205116]. However, there features are still under quite limited scope.
    R18 STxMP
      supports limited combination only, i.e. PUSCH+PUSCH and PUCCH+PUCCH
      does not support asymmetric panel implementation, which is useful for vehicles (e.g. large panel(s) on upper body and small panel(s) on lower body)
      supports up to 2 panels and up to 4 layers only
      supports SFN scheme that does not provide coherent combining for URLLC applications
    R18 2TA
      supports only with multi-DCI mTRP operation, while different TA for different panel/TRP is needed in any mTRP operation (e.g. dynamic TRP switching, sDCI mTRP)
    R17 panel-specific beam report
      does not support symmetric panels
      does not support dynamic SRS port number adaptation according to the beam report
Objective
  STxMP enhancements
    STxMP for various channel/RS combinations (e.g. SRS+SRS, PUCCH+PUSCH)
    STxMP with asymmetric panels
    >2 panel and >4 layer STxMP
    Coherent SFN STxMP
  2TA enhancement
    Support of 2TA feature without multi-DCI mTRP restiction
  Enhancements for dynamic switching across symmetric and asymmetric panels
    Extension of panel-specific beam report for symmetric panels
    Support of dynamic SRS port number adaptation for asymmetric panels
  RS enhancement
    Support for 3 and 4 UL PT-RS ports for >2 panels
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 16: Positioning Enhancements [1/2]
Motivation
  Rel-18 positioning introduces basic features to enhance positioning accuracy based on CPP. Further enhancements on the positioning accuracy for various scenarios is necessary
    Specifying PRU specific signaling and behavior would be beneficial from positioning accuracy and resource overhead/complexity reduction perspective.
    Several remaining works for CPP enhancement needs to be consider further (e.g. integer ambiguity resolution, multipath mitigation, and resource efficiency)
  Rel-18 RedCap positioning requires special UE implementation of FH and BW capability, and may not be suitable for low power/low cost UEs and BW limited scenarios. In addition, Rel-18 CPP utilizing time-based positioning measurements for resolving integer ambiguity may not meet the target requirements if the UE receives/transmits narrowband positioning reference signals (e.g. RedCap UEs).
    It is necessary to investigate narrowband positioning support without FH, such as angle-based positioning enhancements to achieve higher accuracy.
    Methods to support high accuracy with CPP using narrowband reference signals needs to be investigate, especially for RedCap UEs.
Objective
  NR CPP enhancement
    Enhancement on signaling and measurement report for the carrier phase positioning
      PRU specific enhancements
      Further integer ambiguity resolution (e.g. Multiple RF frequencies for the carrier phase measurements report )
    The carrier phase measurement report together with legacy positioning measurements other than time-based positioning measurements (e.g. angle-based positioning measurement)
  Positioning enhancement for narrowband RS transmission/reception without FH
    CPP support for RedCap positioning (or narrowband UEs)
    UL AoA Enhancements
    Others (time/angle-based positioning without FH)
Fig. 1 PRU specific signaling and behavior
Fig. 2 Rel-18 CPP performance with 20MHz BW
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 17: Positioning Enhancements [2/2]
Motivation
  Rel-18 sidelink positioning is limited to FR1 ITS and licensed bands, where the supported bandwidth may not be sufficient in achieving all the accuracy requirements.
    Rel-18 did not exclude SL positioning in FR2, but the detailed operation was not specified
  Carrier-phase positioning(CPP) was specified in Rel-18 Uu link positioning to improve the positioning accuracy. The same benefit of positioning accuracy improvement can be achieved in sidelink, possibly with a narrow bandwidth in FR1 ITS band.
  Sidelink positioning will mostly be used for battery-driven devices. Power saving is one of the most important aspect for successful sidelink positioning deployment.
Objective
  Sidelink positioning enhancements
    Support of sidelink positioning in FR1 unlicensed band, FR2 ITS and licensed band, and FR2 unlicensed band [RAN1, RAN2]
      Unlicensed channel access and physical layer structure with applying Rel-18 design whenever possible
      Introduce a beam management mechanism for sidelink positioning in FR2
    Support sidelink carrier-phase positioning for UE-based and network-based sidelink positioning
      Mechanism for sidelink carrier phase estimation with applying Rel-18 design whenever possible
      Combined Uu link and sidelink based carrier-phase positioning
    Support power saving for sidelink positioning
      Introduce a power saving mechanism for sidelink positioning with applying Rel-17 design (i.e., SL DRX, partial sensing) whenever possible
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 18: Enhanced NW Energy Saving
Motivation
  Rel-18 NW Energy Saving (NES) WI introduces S/P-domain techniques focusing on single TRP operation, while adaptation of TRPs in multi-TRP operation has shown performance gain during SI phase.
  Rel-18 NES SI/WI has been initially considered/evaluated assuming deployment scenario without NCR and focusing on licensed band operation.
  To make NES feature more versatile, support of NES can be extended to additional scenario/deployment such as multi-TRP operation, NCR and unlicensed band environment.
Objective
  Dynamic TRP adaptation (on/off) mechanism for NW energy savings in multi-TRP operation
    Enhancements of CSI, TCI, beam management and repetition related procedures to enable efficient adaptation of TRPs
  Enhancement to support NES techniques under NCR deployment and unlicensed band operation
Multi-TRP operation with enhanced NES
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 19: Ambient IoT
Motivation
  Rel-18 A-IoT SI studies deployment scenarios, design targets and rough estimation of feasibility of A-IoT
  Further study is necessary for more details focusing on practical scenarios for specification of A-IoT
Proposals for A-IoT SI in Rel-19
  Introduce RAN WG-level SI for the feasibility study of A-IoT in Rel-19
    The study to be led by RAN1
  SI focuses on (or prioritize) connectivity topology 1 (BS  Ambient IoT device):
    Further consideration: whether to additionally study connectivity topologies 2 and 3 in Rel-19
    Further consideration : whether to focus on Device C [and B] for topology 1, or consider device A/B/C
  SI focuses on (or prioritize) the licensed spectrum in FR1:
    Licensed TDD in FR1
    Further consideration : licensed FDD
  SI includes study on
    PHY layer DL/UL signal design & L1 procedures to support A-IoT
    Collision/interference/load handling
    Coexistence/harmonization with existing NR signals/channels
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 20: Sidelink communication
Motivation
  Some sidelink use cases require wide channel bandwidth which can be found in FR2. Such use cases include raw sensor data sharing in V2X and high definition video and XR streaming among devices.
    RAN1 is conducting sidelink beam management study in Rel-18.
    It should be noted that 63.72 – 65.88 GHz band is harmonized for ITS in Europe.
  RAN decided to activate sidelink carrier aggregation objective in Rel-18, but some features supported even in Rel-15 LTE were excluded due to the time limitation. To fully address the V2X requirements and potentially make the sidelink CA more useful in other applications, at least Rel-15 LTE features need to be specified.
  With increasing bandwidth of sidelink in unlicensed band and FR2, UE power consumption can be an issue. A frequency domain power saving mechanism is necessary so that a UE can shrink its sidelink operation bandwidth when there is no active traffic.
    In order to avoid bandwidth fragmentation, such a narrowband operation should be able to share resources with a wideband operation.
Objective
  Enhancements for the beam-based sidelink operations [RAN1, RAN2]
    Support of sidelink beam management, by taking Rel-18 study outcome as the starting point
      The operation scenarios include FR2 standalone operation and FR1 assisted FR2 operation.
    Study the impact of beam management on the sensing operation and specify necessary resource allocation enhancements if any
  Enhancements for sidelink carrier aggregation [RAN1, RAN2]
    Enhancements for mode 1 operations under sidelink carrier aggregation, including SL HARQ feedback report to gNB, …
    Handling limited transmission/reception capability of a UE
  Sidelink power saving in the frequency domain [RAN1, RAN2]
    Study and specify a mechanism which enables a UE operating sidelink on a narrowband sidelink to share resources with another UE operating sidelink on a wideband sidelink.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 21: RAN2-led Rel-19 Proposals

## Slide 22: ML-aided Predictive Mobility
Motivation
  Myopic handover decisions lead to HO failures or unnecessary HOs.
    Predictive mobility based on predictive measurement results can reduce HO problems.
  High frequency ranges suffer from frequent link failures.
    Predictive failure detection and recovery can avoid RLF/BF proactively.
  ML-based model management specific to predictive mobility is needed.
    Model selection/monitoring/switching/fallback for predictive mobility is necessary.
Objective
  Predictive mobility for NW-triggered HO and conditional HO.
    Predictive measurements and reporting conditions.
    Predictive mobility execution conditions.
  Predictive failure detection and recovery.
  ML-based model management for predictive mobility.
(a) Too Late HO
(b) Too Early HO
(c) Ping-pong
RSRP in ENDC (LTE B13 + NR FR2 n261) for mobile UE
Predictive Measurements for future time , and at
Model management for predictive mobility

## Slide 23: SDT enhancement
Motivation
  In Rel-17/18, SDT is performed only on initial BWP. But, the initial BWP does not provide sufficient bandwidth for data transmission/reception, and become crowded due to increased number of SDT UEs.
    SDT specific BWP is needed to provide enough bandwidth for data transmission/reception and avoid congestion on initial BWP.
  In Rel-17/18, the maximum duration of SDT procedure is 4s. But, this maximum duration is not suitable for interactive short data exchange, e.g. chatting with instant messaging. In addition, the maximum CG-SDT periodicity is extended in Rel-18 but the maximum duration of SDT procedure is not extended.
    Longer than 4s SDT procedure is needed to support interactive communication and the extended CG-SDT periodicity.
  SPS is beneficial to support periodic MT-SDT traffic and reduces signaling overhead, but SPS is not considered in Rel-18.
    SPS is needed to support periodic MT-SDT traffic.
Objective
  Support for SDT specific BWP.
    Support SDT specific BWP for UL and DL, respectively.
  Support for longer duration of SDT procedure.
    Mechanism to support longer duration, e.g. restart T319a at every transmission/reception.
    Enhancement to power saving for longer duration SDT, e.g. SDT specific DRX.
    Enhancement to resource selection for longer duration SDT, e.g. SSB reselection during SDT.
  Support for SPS

## Slide 24: XR enhancement
Motivation
  In Rel-18, traffic awareness enhancement is limited to discard operation based on PSI (PDU Set Importance) at network congestion. But, it does not fully satisfy requirement of PDU set importance.
    It is necessary to improve reliability and scheduling for important PDU set.
  In Rel-18, power saving enhancement is limited to handling non-integer periodicity and SFN wrap around problems in DRX operation. But, it does not bring considerable power saving gain for multiple flows and jitters.
    It is necessary to improve power saving gain for multiple flows and jitter.
Objective
  Traffic awareness enhancement
    Reliability improvement for important PDU set, e.g. selective PDCP duplication.
    Prioritized scheduling for important PDU set, e.g. transmission via different RLC entities.
  Power saving enhancement
    Support for multiple flows, e.g. multiple DRX configurations.
    Jitter efficient DRX operation, e.g. additional onDuration.
Selective PDCP duplication
multiple DRX configurations
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 25: LTM enhancement
Time gap between
UE measurement and LTM execution
degrades mobility robustness
Support for conditional LTM (CLTM)
UE measurement burden and amount of CSI reporting are excessive
with multiple LTM candidate
CSI measurements and reporting
for a subset of LTM candidates
Support for inter-CU mobility
No support for LTM for inter-CU mobility.
Support for activation and deactivation of LTM candidates
Frequent LTM setup/release/modification
increases signaling overhead
and UE processing burden
Reduce necessary tasks
for LTM candidates
while keeping candidates
Applicable for network-triggered LTM and conditional LTM
Objective
Motivation
No LTM for iner-CU mobility
Frequent candidate management
Weakened mobility robustness
Excessive UE measurement and CSI reporting
Reduce time gap between
UE measurement and LTM execution
to almost zero.
Reduce CSI measurements and reporting for LTM candidates
Support inter-CU LTM and subsequent mobility between different CUs
Enhancement

## Slide 26: Sidelink relay enhancement
  Motivation
    Rel-18 multi-path relaying can be further enhanced for power saving and reduced capability.
      The UE configured with Rel-18 multi-path relaying should always maintain both direct path and indirect path regardless of which path is actually selected for user data transmission, otherwise frequent path addition, modification and/or removal are required.
      Multi-path relaying is beneficial especially when the remote UE is at cell edge. Direct uplink transmission can be restricted for the remote UE for power saving and reduced UE complexity
    In Rel-18 Scenario 2, UE-to-UE link is hidden in 3GPP with some restrictions which can be removed for inter-operability and usage extension e.g. for in-car passenger device connectivity using relay in the vehicle mounted UE; smart watch connectivity using smart phone or vehicle as relay; and better control of indirect path under gNB.
  Objective
    Support power saving and reduced UE complexity for intra-gNB multi-path relaying [RAN2]
      Restriction to direct uplink data transmission
      Dynamic path activation/deactivation
        Support multiple indirect paths with or without direct path (e.g. smart watch via vehicle and smart phone)
        Only one active indirect among one or more configured indirect paths under a same gNB
      Based on current CN operation i.e. without CN impact
    Enhance single path or multi-path relaying with non-3GPP based UE-to-UE link for intra-gNB case without CN impact [RAN2]
      Support non-ideal UE-to-UE link and adaptation layer i.e. no Rel-18 bearer mapping restriction
      Support multiple candidate relay Ues
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 27: Layer 2 Overhead Reduction
Motivation
  Layer 2 header overhead
    L2 header is always attached to each packet, and L2 header overhead problem is more severe for small packet transmission, e.g. VoIP over NTN, IIoT application, pose control in XR, etc.
    It is necessary to study L2 header overhead reduction to increase efficiency of resource utilization.
  Layer 2 processing overhead
    It is required to support UPIP (User Plane Integrity Protection) for full rate, but the processing burden is too high at high data rate.
    It is necessary to study low burden UPIP while not jeopardizing security concerns.
Objective
      Introduce L2 header with reduced overhead.
    E.g. data transmission via TM RLC, header-less/partial subheader MAC subPDU.
  Support low burden UPIP.
    E.g. apply UPIP to selective packets or part of each packet.

## Slide 28: MBS enhancement
Motivation
  Restrictive multicast CFR in R18: Multicast reception in RRC_INACTIVE on multicast CFR fully containing CORESET#0 or initial BWP
    Network cannot release UEs receiving multicast from multicast CFR not containing CORESET#0, even if those UEs do not have active unicast traffic.
  While receiving multicast from multicast CFR not fully containing CORESET#0,
    The UE is still required to monitor initial BWP for paging
    Multicast interruption occurs when switching to initial BWP for paging monitoring.
    Best-ranked cell derived from measurement on initial BWP may not be the best cell for multicast reception
    UE in RRC_INACTIVE may camp on a cell, where QoS requirements of multicast is not satisfied.
Objective
  Support generalized multicast CFR (i.e. multicast CFR not containing CORESET#0 or initial BWP)
    Multicast reception from multicast CFR by UEs in RRC_INACTIVE.
    Minimize multicast interruption caused by switching between multicast CFR and initial BWP.
    Cell re-selection enhancement to guarantee reception quality of multicast in RRC_INACTIVE.

## Slide 29: NTN enhancement
Motivation
  Remaining service time based mobility
    NTN cells have limited service time due to the satellite movement. (e.g. feeder link switch, service link switch)
    UE may conduct mobility to a cell having a short service time, which causes another mobility soon.
  Handling discontinuous coverage of NTN
    NTN may have discontinuous coverage due to the deployment of satellites.
    Declaration of RLF/BF at discontinuous coverage does not bring any gain since there is no other coverage.
Objective
  Service time based cell reselection and conditional handover.
    Prioritize a cell having relatively longer remaining service time.
  Avoidance of RLF/BF declaration at temporal discontinuous coverage.
Link lost upon service termination of second serving cell
Discontinuous coverage in different service link scenario
(left: earth-moving, right: quasi-earth-fixed)

## Slide 30: RAN3-led Rel-19 Proposal

## Slide 31: AI/ML for NG-RAN enhancements
Motivation
  In Rel-18, some use cases such as load balancing, mobility optimization, and energy saving are being specified. This can select/decide the target secondary node more accurately, and avoid RLF for DC and SN change ping-pong.
    Use case/solution of AI for DC needs to be introduced.
  In Rel-18, RAN visible QoE measurement and reporting in NR-DC are being specified in Enhancements on NR QoE WI. This can make a decision for UE(s) on a better resource allocation for a specific service, handover/offloading a specific service/UE to other node.
    How to apply AI/ML for the QoE feature needs to be introduced.
Objective
  Support of intelligent dual connectivity
  Support of intelligent QoE
Intelligent dual connectivity
Intelligent QoE