## Slide 1: Proposal on Positioning Enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - June 16, 2023
RWS-230196

## Slide 2: Carrier Phase Positioning Enhancement
Motivation
  Rel-18 positioning introduces basic features to enhance positioning accuracy based on CPP.
  Further enhancements on the positioning accuracy for various scenarios is necessary.
  Integer ambiguity
    When timing measurement is used, integer estimation accuracy will be limited by the bandwidth size of reference signals.
    Further enhancements to mitigate some error sources(e.g. ARP error) that affects CPP accuracy, including integer accuracy, is required.
  PRU specific signaling and behavior
    It is expected that only basic features (e.g. simultaneous measurement/transmission) for PRU assisted CPP will be specified in Rel-18.
    Several aspects, including positioning accuracy and resource overhead/complexity reduction, needs to be considered for more efficient PRU supports.
  Following issues may be required to further discussed if it is not specified in Rel-18
    Additional techniques for multipath impact mitigation (e.g. additional path reporting)
    Support for standalone reporting of carrier phase measurements
Objective
  Enhancement on signaling and measurement report for the carrier phase positioning
    PRU specific enhancements (including signaling, measurements and reporting)
    Further integer ambiguity resolution
    Other remaining issues (e.g. standalone CPP, Multipath mitigation, etc.) from Rel-18
  The carrier phase measurement report together with legacy positioning measurements other than time-based positioning measurements (e.g. angle-based positioning measurement)
Fig. 1 PRU specific signaling and behavior
Fig. 2 Rel-18 CPP performance with 20MHz BW
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Narrowband positioning Enhancement
Motivation
  Rel-18 RedCap positioning requires special UE implementation of FH and BW capability.
  Rel-18 CPP focus on supporting UEs with normal BW capability.
  Narrowband positioning supports without FH
    FH for communication is not supported by RedCap UEs.
     RS transmission/reception with FH may not be suitable for low power/low cost UEs.
    FH based solution is not applicable in some scenario, e.g. dedicated spectrum less than 5MHz
    In general, performance of angle-based positioning methods are less dependent on BW size, but further enhancement may be required to meet target requirements of RedCap positioning.
  CPP supports for narrowband capable UEs
    With support of precise integer value estimation, CPP can guarantee precise positioning accuracy.  It is challenging to reliably resolve integer ambiguity with Rel-18 CPP feature when BW size is limited.
    Both FH based and non-FH based solution can be considered
Objective
  Positioning enhancement for narrowband RS transmission/reception without FH
    UL AoA Enhancements
    Others (time/angle-based positioning without FH)
  CPP support for RedCap positioning (or narrowband UEs)
Fig. 4 Angle based measurements assisted CPP
Fig. 3 Positioning accuracy with AoA measurements with narrow bandwidth
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Sidelink Positioning in FR2/Unlicensed Band
Motivation
  Sub-meter level accuracy is crucial for safety and enhanced V2X application.
  There are increasing demands for commercial use cases e.g. a positioning service in home environment.
  Large bandwidth and spectrum availability are huddle for high accuracy positioning.
  Location-based service should be available even in out-of-network-coverage area.
  Rel-18 sidelink positioning is limited to FR1 ITS and licensed bands, where the supported bandwidth may not be sufficient in achieving all the positioning accuracy requirements.
Objective
  Support sidelink positioning in FR2
    Higher sidelink positioning accuracy can be achieved through using FR2 band.
    Beamforming based sided positioning reference signal transmission is required.
  Support sidelink positioning in FR1/FR2 unlicensed band
    Unlicensed band provides increased positioning availability and wider bandwidth.
    Rel.18 SL-U channel access and the physical layer structure can be reused
AGV
AGV
TRP
Fig. 5 Concept of SL positioning in FR2/Unlicensed band
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Carrier-phase based Sidelink Positioning
Motivation
  In ITS dedicated band, a higher positioning accuracy cannot be achieved due to the limited bandwidth.
  Carrier phase based positioning developed in Rel.18 NR positioning can be applied for sidelink positioning in that it can provide better positioning accuracy with a smaller bandwidth.
    Note that GPS signal occupies a bandwidth less than 20MHz.
  Road-side unit (RSU) can be used to provide a function as a Positioning reference unit (PRU).
Objective
  Support carrier-phase based sidelink positioning
    Higher positioning accuracy of error less than 1m
  Specify a solution for carrier phase estimation ambiguity
    Rode side unit (RSU) as a positioning reference unit (PRU)
    More stringent synchronization requirement between anchor UEs
Fig. 6 Carrier phase based SL positioning
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 6: Power Saving for SL Positioning
Motivation
  UE such as e.g. vulnerable road user or wearable device operates with battery, where a low power consumption is essential.
  For sidelink positioning, UE’s sensing to determine the available transmission resources consumes a large portion of UE power.
  Power saving feature is necessary for successful deployment of sidelink positioning.
Objective
  Support power saving mode of sidelink positioning.
    Sidelink positioning under sidelink DRX
    Partial sensing for sidelink positioning
  Reuse Rel.17 SL power saving features as much as possible.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 7: Summary
Carrier Phase Positioning Enhancement
  Enhancement on signaling and measurement report for the carrier phase positioning
    PRU specific enhancements
    Further integer ambiguity resolution
    Other remaining issues from Rel-18
  The carrier phase measurement report together with legacy positioning measurements other than time-based positioning measurements (e.g. angle-based positioning measurement)
Narrowband positioning Enhancement
  Positioning enhancement for narrowband RS transmission/reception without FH
    UL AoA Enhancements
    Others (time/angle-based positioning without FH)
  CPP support for RedCap positioning (or narrowband UEs)
Sidelink Positioning in FR2/Unlicensed Band
  Support sidelink positioning in FR2
    Higher sidelink positioning accuracy can be achieved through using FR2 band.
    Beamforming based sided positioning reference signal transmission is required.
  Support sidelink positioning in FR1/FR2 unlicensed band
    Unlicensed band provides increased positioning availability and wider bandwidth.
    Rel.18 SL-U channel access and the physical layer structure can be reused
Carrier-phase based Sidelink Positioning
  Support carrier-phase based sidelink positioning
    Higher positioning accuracy of error less than 1m
  Specify a solution for carrier phase estimation ambiguity
    Rode side unit (RSU) as a positioning reference unit (PRU)
    More stringent synchronization requirement between anchor UEs
Power Saving for SL Positioning
  Support power saving mode of sidelink positioning.
    Sidelink positioning under sidelink DRX
    Partial sensing for sidelink positioning
  Reuse Rel.17 SL power saving features as much as possible.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.