## Slide 1: Proposal on network energy saving in Rel-19
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - June 16, 2023
RWS-230197

## Slide 2: Background
During Rel-18 NW Energy Saving (NES) SI phase, various T/F/S/P-domain NES techniques were studied, as enumerated below.
Considering impacts on legacy NR UEs and performance analysis, some out of studied NES techniques (i.e., B-1-1, A-4, C-1, D-1 techniques) are included in Rel-18 NES WID.
Domain | Technique
Time | A-1: Adapting transmission/reception of common channels/signals A-1-1: Simplified SSB without PBCH or with partial PBCH A-1-2: Skipping of SSB/SIB1 transmission occasion A-1-3: Configuration/adaptation of longer periodicity of SSB/SIB1 and/or uplink random access opportunities A-1-4: Adapting paging or SSB transmission patterns A-1-5: Dynamically adapting PRACH periodicity and occasions A-1-6: Scheduling of SIB1 without PDCCH
 | A-2: Adaptation of UE specific signals and channels
 | A-3: UE wake up signal (WUS) for gNB A-3-1: UE WUS triggering gNB for SSB/SIB/RACH A-3-2: UE WUS triggering gNB to wake up in case of uplink traffic arrival
 | A-4: Adaptation of DTX/DRX
 | A-5: Adaptation of SSB/SIB1 A-5-1: SSB- and/or SIB1-less operation for non-CA A-5-2: On-demand SSB/SIB1
Domain | Technique
Frequency | B-1: Multi-carrier energy savings enhancements B-1-1: SSB- and/or SIB1-less operation for inter-band CA B-1-2: Dynamic UE-group PCell switching
 | B-2: Adaptation of bandwidth part of UE(s) within a carrier
 | B-3: Adaptation of bandwidth of UE(s) within a BWP
Spatial | C-1: Adaptation of spatial elements
 | C-2: Adaptation of TRPs in mTRP operation
Power | D-1: Adaptation of transmission power of signals and channels
 | D-2: Over the air digital pre-distortion
 | D-3: Tone reservation
 | D-4: PA power bias adaptation
 | D-5: UE post-distortion
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Motivation
Rel-18 NES WI introduces spatial domain techniques focusing on single TRP operation.
For adaptation of TRPs in multi-TRP operation (C-2 technique),
  Substantial network energy saving gain has been shown during NES SI phase.
  As captured in TR 38.864, no impact for legacy UEs is foreseen if the adaptation technique is used on a UE-specific basis.
To enable efficient adaptation of TRPs, the enhancements of CSI, TCI, beam management and repetition related procedures can be considered in Rel-19.
Multi-TRP operation with enhanced NES
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Motivation
Rel-18 NES SI/WI has been initially considered/evaluated assuming deployment scenario without NCR and focusing on licensed band operation.
To make NES feature more versatile, support of NES can be extended to additional scenario/deployment such as NCR and unlicensed band environment.
The following aspects can be considered to support NES techniques under NCR deployment and unlicensed band operation:
  Backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR, to consider the case where the gNB would operate with S/P-domain adaptation or cell DTX/DRX adaptation for NW energy saving
  NES techniques adjustment based on outcome of channel access (LBT) procedure in unlicensed band, to efficiently support NW (and associated UE) energy saving in unlicensed band operating with energy-consuming LBT/COT procedure/detection
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Proposal on network energy saving in Rel-19
Dynamic TRP adaptation (on/off) mechanism for NW energy savings in multi-TRP operation
  Enhancements of CSI, TCI, beam management and repetition related procedures to enable efficient adaptation of TRPs
Enhancement to support NES techniques under NCR deployment and unlicensed band operation considering:
  Backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR
  NES techniques adjustment based on outcome of channel access (LBT) procedure in unlicensed band