## Slide 1: Proposal on SDT enhancement in Rel-19

## Slide 2: Motivation for SDT specific BWP
With introducing SDT, initial BWP becomes more crowded.
    All UEs in RRC_IDLE/RRC_INACTIVE use initial BWP for RA procedure, and even UEs in RRC_CONNECTED can use initial BWP for data transmission as well as RA procedure.
    SDT makes UEs in RRC_INACTIVE stay more time in initial BWP since data transmission/reception is possible without state transition to RRC_CONNECTED.
Pushing all functionalities into initial BWP has limitation from network operation perspective.
    RACH resources are already segmented to support many functionality(e.g. RedCap, Slice, CE, SDT) on initial BWP.
      Available RA resource for legacy UE should be reduced and limited RA resource can be used for each functionality.
      Both legacy UE and new UE with new functionality may have RA problems due to limited RA resources on initial BWP.
Separate BWP for SDT is already discussed in NR Rel-17.
    RAN2 identified that SDT specific BWP has benefits to alleviate congestion on initial BWP and concluded to support SDT specific BWP.
      However, RAN1 did not reach a consensus on support for SDT specific BWP and nothing has been discussed since then.
To give more flexibility on resource management to network and avoid congestion on initial BWP, it is important to introduce separate BWP for SDT.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Motivation for longer duration of SDT procedure
  Maximum duration of SDT procedure is not sufficient for services targeted by SDT.
    With the current maximum duration (up to 4s), SDT procedure is initiated frequently for interactive short data exchange.
      Chatting using instant message is not likely to end in the current duration of SDT procedure.
    The maximum CG-SDT periodicity is extended in Rel-18, but the maximum duration of SDT is not extended.
      The SDT procedure needs to be kept longer than the CG-SDT periodicity.
    Frequent SDT procedure initiation leads to signal overhead problem.
  If duration of SDT procedure is extended, enhancements on power saving and resource selection should be considered together to use longer duration SDT efficiently.
  Longer than 4 s SDT procedure should be supported and related enhancements for long duration of SDT procedure are needed in Rel-19.

## Slide 4: Motivation for SPS in SDT procedure
  Periodic traffic is an important use case of SDT.
    CG-SDT is introduced to support periodic uplink traffic in Rel-17 and further enhancement on CG-SDT is considered to support longer periodicity of periodic uplink traffic in Rel-18.
    However, MT-SDT does not support SPS for periodic downlink traffic in Rel-18.
  There is no strong motivation not to consider periodic downlink traffic in SDT, while periodic uplink traffic is considered.
  SPS is beneficial to reduce signaling overhead and support periodic downlink data.
  SPS should be supported for SDT procedure in Rel-19.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: Objectives
  Support for SDT specific BWP
    Support SDT specific BWP for UL and DL, respectively.
  Support for longer duration of SDT procedure.
    Mechanism to support longer duration, e.g. restart T319a at every transmission/reception.
    Enhancement to power saving for longer duration SDT, e.g. SDT specific DRX.
    Enhancement to resource selection for longer duration SDT, e.g. SSB reselection during SDT.
  Support for SPS in SDT procedure
    Support SPS for periodic downlink traffic in RRC_INACTIVE.