## Slide 1: Proposal on LTM enhancement in Rel-19

## Slide 2: Conditional LTM
Limitation of network-triggered cell switch in R18 LTM
  There is a time gap between when receiving the LTM cell switch command and when reporting L1 measurement. Since the network decides to execute an LTM based on L1 measurements of serving and candidate cells, the time gap would degrade mobility robustness in particular when channel is very dynamic (e.g., in FR2 bands).
  Conditional LTM can minimize the time gap, thereby increasing LTM robustness.
Proposed enhancement
  Support for conditional LTM (CLTM) to minimize gap between L1 measurement and LTM execution
    LTM execution conditions based on UE measurements (L1 measurement and/or RRM measurements)
    NOTE: Avoidance of excessive ping-pong needs to be considered.
Case 1: During the time gap, the superiority of channel quality between serving and candidate cells is reversed.
Case 2: During the time gap, the channel quality of serving cell becomes too poor to transmit the LTM command successfully.

## Slide 3: Selective Candidate Cell Management
Motivation
  Performing candidate cell management operation, such as CSI measurements, TA management, etc, for all candidate cells are burdensome to UE. Frequent L1 measurement reporting incurs high signaling overhead. Furthermore, the configurable number of candidate cells are restricted by UE capabilities of simultaneous L1 measurement cells.
  Selective candidate cell management operations allows UE to reduce measurement and other processing burden. Signaling overhead due to L1 measurement reporting can be also reduced.
Proposed enhancement
  Selective candidate cell management operation in order to reduce UE burden and signaling overhead
    CSI measurement & reporting, TA managements for a subset of candidate cells
    NOTE: Criteria to (re)select an available list of candidate cells cell can be considered.
L1 measurements and reporting for multiple candidate cells

## Slide 4: Inter-CU LTM
Motivation
  Restriction to intra-CU LTM
    Rel-18 LTM is supported only for intra-CU mobility, but not for inter-CU mobility. So, legacy handover is used for inter-CU mobility. Furthermore, upon handover to a inter-CU cell, previous LTM configuration is released.
    If LTM is supported for inter-CU mobility, mobility performance is even further enhanced on top of intra-CU LTM.
    Support for subsequent LTM between candidate cells belonging to different CUs can maximally exploit LTM-enabled enhanced mobility performance and minimize signaling overhead.
Proposed enhancement
  Support for LTM in inter-CU mobility
    Subsequent mobility between cells of different CU
    Reference configuration enhancement for inter-CU LTM (e.g., reference configuration per CU)
  NOTE:
    Security handling upon inter-CU LTM should be considered.
CU1:
Intra-CU subsequent LTM
CU2:
Intra-CU subsequent LTM
No LTM
CU1:
Intra-CU subsequent LTM
CU2:
Intra-CU subsequent LTM
Inter-CU LTM
Rel-18 LTM
Rel-19 LTM

## Slide 5: Deactivation of LTM Candidates
Motivation
  Unnecessary LTM release and setup
    When UE moves out of LTM cell cluster, LTM configuration of the UE is released. When the UE moves into the same LTM cell cluster again, LTM configuration has to be setup again, incurring significant signaling overhead and UE processing burden.
      Deactivation of LTM is beneficial to avoid unnecessary LTM release and setup
    Releasing LTM configuration upon entering RRC_INACTIVE requires another LTM setup upon RRC resumption
      Maintaining LTM context in RRC_INACTIVE can allow UE to restore LTM configuration upon resumption
  Unnecessary candidate cell release and addition
    For conditional LTM, network may want UE to consider only a subset of the candidates among configured candidates. If the rest candidates are released, these candidates cannot be considered for subsequent mobility unless they are added again as candidates.
      Deactivation of some LTM candidate is beneficial to avoid unnecessary LTM candidate release and addition
Proposed enhancement
  Support for deactivation of LTM
    Deactivation of some LTM candidates
  Restoration of LTM configuration upon RRC resumption
    Maintaining LTM context in RRC_INACTIVE and LTM configuration resumption
  NOTE: Network-triggered LTM and conditional LTM are both considered.

## Slide 6: Objectives for R19 LTM Enhancement
Support for conditional LTM (CLTM)
  LTM execution condition
  NOTE: Avoidance of excessive ping-pong needs to be considered.
Reduction of candidate cell management task in order to reduce UE burden and signaling overhead
  Selective link management (e.g. CSI measurement & reporting, TA maintenance) for a subset of candidate cells
  NOTE: Criteria to (re)select an available list of candidate cells cell can be considered.
Support for inter-CU LTM
  Subsequent mobility between cells belonging to different CUs
  Reference configuration enhancement (e.g., reference configuration per CU)
  NOTE: Security handling upon inter-CU LTM should be considered.
Support for activation/deactivation of LTM candidates
  Support for deactivation of LTM
  Restoration of LTM configuration upon RRC resumption
  NOTE: Network-triggered LTM and conditional LTM are both considered.