## Slide 1: Views on IDLE/INACTIVE enhancements
3GPP RAN-Release 19 workshop
Taipei, 15th – 16th June, 2023
RWS-230265
Xiaomi

## Slide 2: Motivations
Observation: Currently, flexible initial BWP configuration for more purposes (e.g. paging, MBS, SDT) are not considered
Proposal: Support Rel-19 WI for IDLE/INACTIVE enhancements for initial BWP configuration.
Background:
Currently, the Spec can already support to configured separate initial BWP configuration for (e) Redcap UEs for the following cases:
    RAR;
    SDT; (if the separate initial BWP does not CD-SSB, NCD SSB will be configured)
    Paging (if the separate initial BWP contains coreset#0 and CD-SSB)
However, flexible initial BWP configuration (e.g. multiple initial BWPs) for more purposes are not considered:
    Paging (if the separate initial BWP does not contains CD-SSB)
    MBS;
    Slice;
One cell/frequency could be too overloaded and be congested for initial access in a hot spot, e.g. due to RACH partition and/or uneven UE distribution of single frequency priority;
One cell/frequency could be too overloaded and be congested for paging in a hot spot, e.g. due to uneven UE distribution of single frequency priority;

## Slide 3: Objectives for R19 WI
Proposal: Considerations on IDLE/INACTIVE enhancements, suggest RAN to consider the following objectives for Rel-19 WI:
Specify flexible initial BWP configuration (e.g. multiple initial BWPs) for different purposes:
Different use cases:
    (e) Redcap;
    MBS;
    Slicing;
    SDT;
    …
(2) Specify the UE distribution solution for multiple initial BWP/cell/frequency：
UE distribution for paging monitoring;
(3) Specify the enhancement for initial BWPs :
the NCD-SSB for initial BWP can be considered for IDLE/INACTIVE UE.

## Slide 4: Thanks