## Slide 1: Rel-19 SDT enhancements
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
Source: ZTE, Sanechips
Agenda: 5
RWS-230297

## Slide 2: Further enhancements for SDT – Motivation (1)
  Small and infrequent data transmissions are very typical in mobile networks
    Common to both smart phone applications as well as other devices such as wearables, sensors, smart meters, IoT devices
  INACTIVE state is mandatory for UEs since Rel-15, but is seldom used in real networks
    Standalone 5G deployments typically fail to exploit INACTIVE state because of small and/or infrequent data keeping the UE in CONNECTED state
    UEs are typically kept in power hungry CONNECTED state or the system incurs a large signalling overhead when moving back and forth from IDLE/INACTIVE to CONNECTED
    Many operators that deployed 5G SA, simply disabled (or never use) INACTIVE state as a result
Source: 3GPP TR 36.822

## Slide 3: Further enhancements for SDT – Motivation (2)
  Rel-17 and Rel-18 5G enhancements provide benefits for small data transmissions by enabling data transmission in INACTIVE state
  Some networks are now enabling the usage of INACTIVE state with SDT feature
  However, SDT feature still needs further enhancements for it to enable the networks to fully exploit the possible gains
  Some of the possible enhancements over Rel-17/Rel-18 include:
    Enablers for new SDT applications:
      RRC-less SDT: To further reduce the signalling overhead
      SDT for IDLE mode: To extend the power saving benefits and to enable similar gains as LTE/EDT
      Pre-configured resources for MT-SDT: To further reduce DL overhead for SDT traffic
    Further enhancements for the SDT feature:
      Larger payload sizes/Longer period for SDT: Low hanging fruit. These simple enhancements enable large gains and support new use cases
      SDT on non-initial BWP: To avoid congestion over initial BWP and to improve the efficiency of SDT
      Robustness and efficiency improvements: Prevent unnecessary transitions to IDLE upon SDT failure and minimize back-haul signalling overhead)

## Slide 4: SDT enhancements to enablers new applications/verticals
  RRC-less for SDT
    Main motivation: Further signalling overhead reduction
      Both Rel-17 and Rel-18 is based on RRC-based SDT
      RAN2 extensively studied both RRC-based and RRC-less SDT and acknowledged the benefits of RRC-less SDT (especially for the same cell case)
    RRC-less SDT further enables very low signalling overhead and improves the overall system performance
    Especially suitable with pre-configured resources (e.g. CG/SPS in UL/DL), but in general can be supported when the UE is in the same cell
  SDT for IDLE mode
    Main motivation: Further power saving and enabling new use cases that require the UE to be in IDLE mode (e.g. IoT applications)
      LTE/EDT enables IDLE mode for small data transmissions using the stored NAS security context and already works with 5GC
    Enabling SDT for IDLE mode will bring 5G RAN on-par with the EDT feature and exploits the already existing building blocks in 5GC for early data transmission over control plane
  Pre-configured resources for MT-SDT
    Main motivation: Further signalling overhead reduction for periodic MT traffic
      In Rel-18, MT-SDT uses paging triggered SDT procedure to initiate SDT procedure for Mobile terminated traffic
      This is not optimal in case of periodic DL traffic and further gains can be realized if periodic DL resources could be used for MT traffic.
    The gains are especially attractive if this is combined with RRC-less transmissions

## Slide 5: Enhancements for SDT feature
  Larger payload sizes and longer SDT period
    SDT currently only supports up to 96 kB of data and the SDT session has to finish within 4sec
    Larger payload sizes for SDT can be enabled with very minimal changes to the specs (e.g. 512 kB to cover a 2MP image)
    Longer SDT session period would also be useful to avoid unnecessary session failures but may need further sparse PDCCH monitoring periodicity or enabling UE specific DRX for SDT
  SDT for non-initial BWP
    Only initial BWP can be used for SDT until Rel-18
    Congestion over initial BWP is bad and severely restricts the system capacity for SDT UEs
    Non-initial BWP for SDT makes the feature more widely deployable and significantly increases the number of SDT UEs in the cell
  Robustness and efficiency improvements
    Failure recovery during SDT session relies on the suboptimal NAS recovery procedure (i.e. UE moves to IDLE mode and initiates new connection):
      Enabling a light-weight mechanism for error recovery (similar to reestablishment) would significantly improve the SDT performance
    SDT uses stored RLC context and this decision was made to simplify the design
      Results in unnecessary signalling over Xn to perform context fetch for SDT even when anchor relocation is not used
      Using default RLC configuration could avoid this and simplify the design and enable lower signalling overhead over Xn

## Slide 6: Conclusion and proposals
  Further enhancements for SDT feature will benefit the overall system and improve the system efficiency
  SDT enhancements will enable the operators to exploit the INACTIVE state which is seldom used in 5G networks today
  Proposal : RAN should consider the following SDT enhancements and enable a SDT enhancements WI in Rel-19 with a selected set of the features from below
    Enhancements to Enable new SDT applications:
      RRC-less SDT
      Pre-configured resources for MT-SDT
      SDT for IDLE mode
    Further enhancements for the SDT feature:
      SDT on non-initial BWP
      Robustness and efficiency improvements
      Larger payload sizes/Longer period for SDT

## Slide 7: Thanks