## Slide 1: Considerations on Rel-19 SI on AI/ML for NR air interface
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-230313
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Status of Rel-18 SI on AI/ML for NR air interface
  General aspects of AI/ML framework:
    Good progress on inference-related LCM procedures,
      Functionality-based and Model ID-based LCM are identified.
    Some progress on model monitoring and data collection. Open issues expected to be resolved in August WG meeting.
      Data collection requirements/framework will be considered per use case per LCM purpose (i.e. model training/monitoring/inference)，pending on RAN1 reply LS for further down-selection.
    Limited studies on model transfer and model training.
      Both CP-based and UP-based model transfer are still under estimation in RAN 2. But the feasibility highly depends on RAN1 guidance/requirement.
  Use cases
    Identified 6 sub use cases: CSI compression, CSI prediction, spatial domain beam prediction, temporal beam prediction, direct AI/ML positioning and AI/ML assisted positioning.
    Comprehensive evaluations for the all 6 use cases. Observed performance gain in some scenarios.
    Good progress on the potential specification impacts of 5 sub use cases. But study on AI/ML based CSI prediction only focuses on evaluation yet.
    Two-sided model for CSI compression. One-sided model for the other 5 use cases.
    Evaluations and studies on online training/tuning/updating are not touched in R18.

## Slide 3: Status of Rel-18 SI on AI/ML for NR air interface (Cont’)
  RAN4 status：
    Agreed to study model interference.
    LCM is under discussion.
      Agreed to study model monitoring, model select/switch/activate/deactivate/fallback.
      Training is deprioritized.
      FFS data collection, model update/delivery.
    Agreed to study all 6 sub use cases, and kick off with good progress on performance requirement and core requirement of each case.
      Candidate KPIs for different sub cases are identified.
    Test method for two-sided model is not clear.
      Introduction of reference model is a challenge work in RAN4.
      How to test LCM and ensure the practical effectiveness of AI/ML solutions remains more study.

## Slide 4: Rel-19 RAN2-led SID: Motivation
  R18-left LCM topics are mainly within RAN2 scope
    E.g., Model training/transfer/registration and data collection
  Untouched use cases in R18 deserve more study time
    E.g., AI-based mobility and joint channel estimation and CSI feedback
  Mobility is usually RAN2-led and brings in new features that differ from PHY AI
    E.g., privacy concerns for UE location report
  UE impact on AI-based mobility has not been considered by NG-RAN
    E.g., UE-specific trajectory characteristics

## Slide 5: Rel-19 RAN2-led SID: Proposal
  A RAN2-led SID is proposed for Rel-19, with the following focuses:
    LCM framework: advanced features unfinished/untouched in R18
      E.g., model transfer
    New use case(s) that gain interests from many companies
      E.g., AI-based mobility
    New use case(s) that may show illuminating insights
      E.g., joint channel estimation and CSI feedback (RAN1-led)

## Slide 6: Rel-19 RAN2-led SID: LCM Framework
  Study Advanced features unfinished/untouched in R18 :
    Model identification Type B
      Compared to offline based model identification, i.e. Type A, online based model identification is more efficient for model info alignment in multi-vendor scenarios.
    Model registration
      The NW should have the capability to avoid the unauthorized user to acquire NW stored model.
    3GPP signaling-based model transfer
      Signaling and QoS aspect;
      Delta model update/transfer.
    Offline/Online Model training
      Data collection for training;
      Training task management including training task generation/deployment/performing/validation/testing/feedback/ retraining/tuning.

## Slide 7
  Motivation
    AIML can enable more flexible parameter tuning (e.g., hysteresis, TTT, CIO, and T304) to reflect dynamic environments
    With historical T304 configurations and performances in mind, AIML achieves 32.9% throughput gain compared to legacy L3 mobility.
    AIML supports the further reduction of interruption time, short time-of-stay, ping-pong rate, and re-establishment/HO overheads
  Potential specification impact
    Evaluate gains brought by AIML in mobility
    UE-assisted data collection and network-configured parameter tuning
    Model transfer between gNB and (multiple) UE(s)
    Notes: Focus on UE-based AIML model execution/inference to differentiate the work from RAN3 WID
  Settings: Overlapped UMi with 38 sites; 1000 UE walk randomly within a 400m x 400m square in the middle of the scenario. Contextual bandit with T304 configurations as arms and the future sum of RSRPs as rewards
New use case for Rel-19 RAN2-led SID
AI-based mobility: Dynamic parameter tuning
  Procedure for AI-based mobility parameter tuning
  Throughput gain due to less interruption and better cell choice
Notes: Correct prediction: the prediction results are the same as real data
False alarm: there is no failure but we predict there is
Missed failure: there is failure but we predict there is not

## Slide 8
METIS II dense urban information society, Input: coarse-grained locations (3m maximum error), Encoder-decoder LSTM uses UE locations in the prior 5s to predict trajectory in the next 5s
  Motivation
    Cell HO and beam switch is more frequent as cells become denser and beams go narrower
    Wrong HO may occur due to insufficient use of environment information (e.g., load) and user information (e.g., mobility pattern/behavior)
    CHO reserves many resources for candidate cells due to the uncertainty of user trajectory
    Trajectory prediction can be accurate enough to facilitate intelligent HO decision even with positioning error
  Potential specification impact
    Post-process of model inference (e.g., impact of model output on legacy mobility procedure)
    Reuse/extend LCM for AIML-based mobility (e.g., two-sided model with intermedia data transferring over the air to avoid the transmission of sensitive data like UE location)
    UE-initiated HO/beam switch with UE-sided model
New use case for Rel-19 RAN2-led SID
AI-based mobility: Handover decision optimization

## Slide 9: New use case for Rel-19 RAN2-led SID AI-based mobility: Failure avoidance
UE speed | ≤15km/h | >15km/h
Correct prediction | 91.53% | 90.2%
False alarm | 0.77% | 4.63%
Missed failure | 60.62% | 50.76%
  Motivation
    RLF/HOF/BF becomes more frequent as cells become denser and beams go narrower
    Reactive strategies instead of proactive methods (e.g., fast RLF recovery rather than RLF avoidance) are applied
    AIML can, to some extent, predict the happening of failure and take proactive HO to avoid channel deterioration
Real data analysis: Technical University of Denmark LTE drive test from IEEEDataPort. Encoder-decoder LSTM uses UE’s locations and RSRPs in the prior 20s to predict RSRPs in the next 20s
  Potential specification impact
    Data collection and model update to reflect real-time channel state change (e.g., the existence of coverage holes or obstacles can be learned with real-time reports from UEs)
    Model monitoring mechanism design (e.g., false alarm discovery and fallback to the original serving cell)
    UE-based/UE-assisted channel prediction and HO procedure
  Prediction accuracy of worsening channel states based on drive test data
Notes: Correct prediction: the prediction results are the same as real data
False alarm: there is no failure but we predict there is
Missed failure: there is failure but we predict there is not

## Slide 10: New use case for Rel-19 RAN2-led SID Joint channel estimation and CSI feedback
  Motivation
    AI-based CSI feedback enhancement has been well studied in Rel-18, but the potential impact of channel estimation was not considered,
      How the channel estimation accuracy affects the final CSI acquisition performance is still unknown
    In contrast to study AI-based enhancement for single module individually, Rel-19 can kick off studies/evaluations on AI-based cross-module design, e.g., joint channel estimation and CSI feedback
  Potential specification impact
    Performance enhancement
      RS enhancement & overhead reduction, potential CSI performance enhancement
    Related LCM procedure on cross-module design
Note1:
  CDL-C, 3.5GHz, 32T4R, 52RB, 13 subband, SNR=10dB, 3km/h
  Baseline：LMMSE channel estimation + SVD + CSI feedback based on eType II codebook
  AI: AI-based E2E solution
  Mixer backbone
Note2:
  UMa, 3.5GHz, 32T4R, 52RB, 13 subband, mixed SNR(0/10/20/30dB), 30km/h
  Baseline：LMMSE channel estimation + SVD + CSI feedback based on eType II codebook
  AI: AI-based E2E solution
  Backbone from 3rd WAIC competition
Channel Model | Feedback bits | Pilot Density | SGCS performance |  | 
 |  |  | Non-AI CE&CSI (Baseline) | Traditional CE& AI-based CSI | AI based joint CE&CSI
CDL-C [Note1] | 62 | 4/52 | 0.70 | \ | 0.83
 |  | 13/52 | 0.71 | \ | 0.84
 |  | 26/52 | 0.71 | \ | 0.85
 | 168 | 4/52 | 0.80 | \ | 0.90
 |  | 13/52 | 0.85 | \ | 0.91
 |  | 26/52 | 0.85 | \ | 0.91
UMA [Note2] | 64 | 6/52 | 0.66 | 0.73 | 0.77
 |  | 26/52 | 0.69 | 0.78 | 0.79