## Slide 1: Positioning technologies for Rel-19 Ambient IoT
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-2300317
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Outline
Motivation on Ambient IoT positioning
Typical use cases and requirement of Ambient IoT positioning
Technical challenge and candidate Techniques for Ambient IoT positioning
Summary and proposals

## Slide 3: Motivation on supporting Ambient IoT positioning in 5GA
  An ambient power-enabled Internet of Things device is an IoT device powered by energy harvesting ( e.g. from radio waves, light (solar), motion, heat etc.), being either battery-less or with limited energy storage capability (e.g., using a capacitor).
  Ambient IoT provides a promising scheme to fulfil the service requirements that can’t be met using the existing IoT technologies.
  An SA1 study item is ongoing to study the use cases and service requirements. Based on the discussion, 4 functionalities of ambient IoT has been identified, including inventory, sensors, positioning and actuators.
  Positioning is one of the most important function and it is required in about 12 use cases among the agreed use cases in SA1.
  Early support of ambient IoT positioning in 5GA is critical to fulfill the urgent requirement from verticals.
…
…

## Slide 4: Representative UC#1: Items discovery in Smart home scenario
  Ambient IoT can be used in the following applications:
    Asset management: finding home belongings
    Home environment monitoring: e.g., temperature, humidity, gas leakage etc.
    Home security: intruder detection
  Requirements
    Low complexity and small size, e.g., thickness of 1mm and area of several cm2
    Long service life., e.g., more than 10 years.
    No need to replace/recharge a conventional battery, e.g. Maintenance-free for battery
    Coverage up to 10m
    Positioning accuracy of 1~3m

## Slide 5: Representative UC#2: Indoor positioning
  Currently, there is no effective low-cost techniques for indoor positioning.
  Ambient IoT device can serve as anchors for indoor positioning. It can be used to build an indoor positioning and navigation system.
    For Car parking
    Navigation in shopping center
    For manufacturing and logistics
  Requirements of the Ambient IoT devices:
    Communication range: 10~30m
    Positioning accuracy: 1~3 m horizontal accuracy and 2m vertical accuracy (i.e., can locate the specific floor)

## Slide 6: Representative UC#3: Intra-Logistics and warehousing
  Ambient IoT device can be attached on the packet for goods tracking when they are being transferred, stored, loaded/unloaded, and inventoried for logistics and warehousing.
  Requirements of the IoT devices:
    Battery-less, thus no need to use a battery
    Low complexity and small size
    Coverage: up to 30m for indoor case, up to 100m for outdoor case
    Processing (i.e., reading IDs) hundreds to thousands of devices per second.
    Positioning requirement: 1-3m for indoor and 10m for outdoor

## Slide 7: Representative UC#4: Smart manufacturing
  Ambient IoT tags attached on the product tray can be used to monitor the position of the product and its manufacturing Information.
  Real time quality inspection and tracing of the assembly line
    The Product line occupies an area of 25 thousand m2 and it supports more than 20 process
  Potential Requirements
    Small size, maintenance-free, battery-free, and ultra-low-cost IoT devices
    Coverage: 10-30 meters for indoor
    Positioning accuracy: 1~3 m horizontal accuracy

## Slide 8: Role of ambient IoT Tags and the technique challenges
  It faces more challenges for Ambient IoT device to support positioning due to its ultra-low device complexity(e.g. narrow bandwidth, poor timing stability etc.) and its ultra-low power constraints.
  In order to fulfill the services requirement from verticals, poisoning methods need to be studied for ambient IoT.
  There are two possible roles for ambient IoT devices:
Tag to be positioned
Anchor Tags used to position other devices

## Slide 9: Possible candidate techniques for ambient IoT positioning
Timing based positioning
Phase based positioning
RSRP(RSRP-map) based positioning

## Slide 10: Timing based positioning
  BS/readers: transmit PRS and measure the TOA of PRS signals from tags，e.g. TOA, TDOA, RTT
  TOA ->Propagation delay -> Distance between BS and tag/UE
  The accuracy for TOA detection is highly dependent on PRS bandwidth
The distance ambiguity is about 60m with 24RB

## Slide 11: Positioning using Carrier Phase difference (1)
Assuming two signals @f1/f2 can be transmitted/backscattered by the ambient IoT tag:
Assuming t =0 when the signal departs from the tag and t=T when receiver(gNB) receives the two signal @f1/f2 :
Therefore, if phase difference of two signals @f1/f2 can be measured, the distance d can be derived.

## Slide 12: Positioning using Carrier Phase difference (2)
Simulation setting:
  f2−𝑓1=0.9𝑀
  The unambiguous positioning range is 3e8/0.9M/2=166m for backscattering
  The distance between tags and gNB is randomly generated within [0, 70]m
  SNR_dB=𝑇𝑥_𝑝𝑜𝑤𝑒𝑟−𝑁𝑜𝑖𝑠𝑒−(𝑃𝐿−𝑆𝐹)−𝐹_𝐵𝑎𝑐𝑘𝑆𝑐𝑎𝑡𝑡𝑒𝑟, where PL is dependent on distance
Single-tap channel with fixed SNR
Multi-tap channel with fixed SNR
Multi-tap channel with real SNR
accuracy could be achieved by increased Tx power or repetitive PRS symbols

## Slide 13: RSRP based positioning
  A UE can be positioned using the reference ambient tags
    The map is [20m * 20m] and UE position is randomly generated within the map
    RSRP value for each tag can be measured by the UE (Smart Phone)
    The location of the reference tag is pre-known
    Random LOS or NLOS for each tag
    The weight for a selected reference tag, e.g.

## Slide 14: Summary and proposal
Observation:
  Positioning is one of the most important function for ambient IoT and there are urgent needs from verticals.
  It faces more challenges for Ambient IoT device to support positioning due to its ultra-low device complexity(e.g. narrow bandwidth, poor timing stability etc.) and its ultra-low power constraints.
  Legacy TOA or TDOA methods may not be workable for ambient IoT, but it is still feasible to support positioning method using phase difference and achieve considerable performance based on the evaluations.
Based on the above observations:
  It is proposed to support ambient IoT positioning in Rel-19.
  It is proposed to study Ambient IoT positioning in Rel-19 positioning study/work item.