## Slide 1
Huawei, HiSilicon
Multicarrier operation enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230322
Taipei, June 15 - 16, 2023

## Slide 2
Contents
Multicarrier operation enhancements
Single PDCCH for different SCS among co-scheduled cells
UL Gbps with low DL complexity
Fast DL carrier switching via L1 signalling
Multicarrier CSI measurement enhancement
Flexible cross-cell scheduling and HARQ retransmission
Summary

## Slide 3
Single PDCCH for different SCS among co-scheduled cells
In Rel-18, to reduce the control overhead, multi-cell PUSCH/PDSCH scheduling with a single scheduling DCI is introduced.
Due to limited TU, only same SCS among co-scheduled cells are specified, which limits the applicable scenario for this feature. For example, typical F+T scenario is not applicable, such as 3.5GHz/2.6GH TDD + Sub-3GHz FDD.
In Rel-19, multi-cell PUSCH/PDSCH scheduling with a single scheduling DCI should be extended to support different SCS among co-scheduled cells in order to achieve similar benefits for TDD+FDD scenario.
Rel-18 for co-scheduled cells with different SCS
Rel-19 for co-scheduled cells with different SCS
FDD CC1
TDD CC2
PDCCH
PDSCH/PUSCH
PDSCH/PUSCH
15KHz
30KHz
FDD CC1
PDCCH
PDSCH/PUSCH
TDD CC2
PDCCH
PDSCH/PUSCH
15KHZ
30KHz

## Slide 4
Motivation
Rel-19: Enable UL Tx switching with low DL complexity
  Rel-18 baseline
  To support higher UL throughput, R18 MC configuration requires UE to support 3 or 4 CC DL CA, which leads to relatively high complexity for DL and limits availability of UE for MC deployment in real field.
  As the Rel-18 MC design, 3, 4 or even more DL RF chains and baseband resources need be kept open for the UL centric service, which leads to unnecessary power consumptions and shorter battery life .
  Multiple SUL associated with one DL carrier
  1 Cell = 2-SUL + 1-NUL + 1-DL
Rel-18
Rel-19
R18 : (4DL CC) TDD+TDD+SUL
TDD Band B
TDD Band A
100MHz
30MHz
60MHz
SUL Band C
100MHz
60MHz
1.174Gps peak data rate
UL Gbps with low DL complexity

## Slide 5
Fast DL carrier switching via L1 signaling (1/2)
Motivation:
  Typically the number of carriers available at the network side is more than that can be supported by UE CA capability, especially more and more spectrum will be deployed in the future by operators.
  Network can decide the best carrier for PDSCH transmission based on the traffic and/or channel condition, and indicate UE to switch among carriers. However, the interruption time is quite long based on the current switching mechanisms, which would have significant impact on the UE experience.
Candidate cell1
PCell
SCell
Candidate cell2
Candidate cell1
PCell
SCell
Candidate cell2
6~10ms
~50ms
BWP1
BWP1
PCell
SCell1
SCell2
SCell3
Interruption time: 1~2ms for SCell switching
PDSCH1
PDSCH2
Dormant BWP
BWP1
Dormant BWP
BWP1
Dormant BWP
BWP1
PDSCH2
Dormant BWP
BWP1
Dormant BWP
BWP1
PDSCH1
BWP1
Dormant BWP
Rel-19
Carrier switch via L1-based BWP switching
  The network configures multiple BWPs in each cell with at least one dormant BWP, only the activated carrier with non-dormant BWP as the current BWP are relevant from UE capability perspective, i.e. the number of configured activated carriers can be larger than the number of DL carriers supported by UE CA capability
  Rel-15 1~2 ms BWP switching is reused to switch transmission cells.
Rel-18
Cell switch by L1/L2 signalling
  The Network pre-configures more cell(s) including serving cell(s) and candidate cell(s), only the serving cell(s) are relevant from UE capability perspective.
  L2 signaling indicates cell switching. Note that SCell switching is not specifically enhanced in RAN2 and RAN4 in Rel-18.
Rel-17
1~2ms
  The Network configures serving cell(s) and BWP(s) configuration to comply with capabilities, regardless of activated/deactivated or not.
  L3 signalling indicates cell switching.
Cell switch by L3 signalling
PCell
SCell
PCell
SCell
Interruption time: ~ 50 ms for PCell and SCell
~50ms
Active
Inactive
  Interruption time:
~50ms
  PCell: 6~10 ms
  SCell: ~ 50 ms (if SCell needs to be
  added and released by RRC)

## Slide 6
Performance Evaluation
Simulation assumption
R18
Each UE
PDSCH 1
PDSCH 2
CC3
CC1
CC2
CC4
R19
PCell switching (with SCell or without) : 6 ms
SCell switching: 50 ms
Compared with Rel-18, fast DL carrier switching via L1 can obtain 15~ 24% average UPT gain.
Parameters | Values
Deployment | 3GPP Dense Urban, 7 sites, 3 sectors/site
Frequency and BW | 3.5G(8:2) 100MHz+100MHz 2.1G 50MHz 1.8G 50MHz
BS antenna | TDD: 32T; FDD: 32T
UE antenna | Total 8R (max. 4 per band)
ISD | 200m
BS Tx power | 49 dBm
Number of UEs | 840/ All cells
MIMO mode | MU-MIMO with rank adaptation
Traffic model | FTP model 3, 1 Mbyte
Scheduling | PF
Simultaneous PDSCH capability | 2
PCell switching (with SCell or without) : 6 ms
SCell switching: 1 ms
Fast DL carrier switching via L1 signaling (2/2)
Chart: UPT (Mbps)
| RU=10% | RU=40% | RU=70%
R18 | 42.5678 | 38.4529 | 32.673
R19 | 52.6837 | 46.2242 | 37.4101
23.8%
20.2%
14.5%

## Slide 7
Motivation
Rel-19: Joint CSI measurement across multiple carriers
Massive MIMO in CA scenario requires high UE complexity of CSI computation in Rel-18. It is even worse considering mTRP.
UE cannot obtain full channel information with limited capability of CSI measurement, e.g., 32 ports across all carriers.
32T
32T
32T
FDD CC1
FDD CC2
FDD CC3
8 ports
8 ports
8 ports
CSI1
CSI2
CSI3
The CSI is measured for each CC individually but with limited ports
Rel-19: Joint CSI measurement across multiple carriers
32T
32T
32T
FDD CC1
FDD CC2
FDD CC3
32 ports
CSI1
Single CSI is measured for all CCs
Rel-18: Independent CSI measurement among multiple carriers
UE can measure multiple co-located neighboring CCs jointly, with the restriction that the total bandwidth of all CCs cannot exceed the maximum bandwidth per CC (i.e. 100 MHz for FR1).
Joint measurement across multiple carriers in R19 has similar UE complexity as measurement of single carrier in R18.
Preliminary evaluation
Parameters | Value |  | 
Frequency | 1.8 GHz | 2.1 GHz | 2.6 GHz
Bandwidth | 10 MHz | 10 MHz | 10 MHz
Deployment | UMA, 21 cells |  | 
BS antenna | 32Tx |  | 
Channel model | 3GPP channel model (Correlation modelling for multi-frequency simulations) |  | 
Traffic model | FTP3 |  | 
Codebook | Type I |  | 
TAE among multi-CCs | 0~3us |  | 
Chart: Average UPT Gain (Type I codebook)
| RU 30% | RU 50% | RU 70%
R19 vs R18 baseline Gain | 0.08 | 0.25 | 0.3
Rel-19 joint CSI measurement across multiple carriers can obtain 8~30% gain
Multicarrier CSI measurement enhancements

## Slide 8
Motivation
  Latency reduction can be achieved by cross-cell related features (i.e. cross-cell scheduling, cross-cell HARQ-ACK feedback and cross-cell HARQ retransmission), especially for TDD CA with different UL/DL configurations.
  Control channel load balance is another motivation for flexible cross-cell scheduling and HARQ feedback.
  Some cross-cell related features are already supported, but some are still missing
  Cross-cell scheduling
    Supported: SCell cross-cell schedules PCell while PCell can still schedule PCell itself
    Supported: Single DCI scheduling multiple cells
    Not supported: PCell cross-cell schedules SCell while the SCell can still schedule the SCell itself
  Cross-cell HARQ-ACK feedback
    Supported: with DCI based mode and semi-static mode by slot-based PUCCH-cell pattern
  Cross-cell HARQ retransmission
    Not supported: Limited by HARQ entity per cell in current standard
  PCell cross-cell schedules SCell while the SCell can still schedule the SCell itself
  Cross-cell HARQ retransmission
Rel-19: Flexible cross-cell scheduling and HARQ retransmission
Flexible cross-cell scheduling and HARQ re-tx

## Slide 9
Summary
Proposal: Specify the following enhancements for multi-carrier enhancements in Rel-19
Multi-cell PUSCH/PDSCH scheduling by DCI format 0_3/1_3 with different sub-carrier spacing among co-scheduled cells [RAN1]
Support of one cell with multi-SUL and one NUL associated with the single DL carrier [RAN1, RAN2, RAN4]
Fast DL carrier switching via L1 signaling, assuming that the number of configured activated carriers can be larger than the number of DL carriers supported by UE CA capability [RAN2, RAN4]
Joint CSI measurement across multiple carriers with one CSI report for all the carriers [RAN1, RAN4]
Flexible cross-cell scheduling and HARQ retransmission [RAN1]
  PCell cross-cell schedules SCell while the SCell can still schedule the SCell itself
  Cross-cell HARQ retransmission