## Slide 1
Huawei, HiSilicon
Views on AI/ML for PHY in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230323
Taipei, June 15 - 16, 2023

## Slide 2
Contents
Overview
Preliminary observations on performance of use cases in Rel-18 SI
Main open issues for Rel-18 SI
RAN1 part main open issues for Rel-18 SI
RAN2 part main open issues for Rel-18 SI
RAN4 part main open issues for Rel-18 SI
New sub use case for Rel-19 study
TSF-CSI compression
BM for large antenna array

## Slide 3
Overview
Overview of Rel-18
Views for Rel-19
Temporal-spatial-frequency domain CSI compression
SSB/CSI-RS
Accurate analog BF
RS measures
(RSRP + phase)
Optimal ABF
Beam management for large antenna array
  For Rel-19, whether to continue study or to have normative work is dependent on the outcome of Rel-18 study
Study more sub use cases in Rel-19
  Temporal-spatial-frequency domain CSI compression
  Beam management for large antenna array
Progress of RAN1
  Select 6 representative sub use cases and draw some observations
  Identify main components for LCM framework and recognize some of the candidate solutions
  Remaining main open issues:
    Functionality/model identification, training collaboration, model transfer/delivery, and data collection
Progress of RAN2
  Discuss candidate directions/solutions of protocol aspects and procedures according to the outcome from RAN1
  Remaining main open issues:
    Functionality/model identification and control, model transfer/delivery, data collection, and UE capability
      Some aspects needs to be studied per sub use case
Progress of RAN4
  Study core/performance requirements and test metrics per use case
  Remaining main open issues:
    Test framework for two-sided model, testability of potential test metrics, and verification of generalization

## Slide 4
Preliminary observations on performance of use cases in Rel-18 SI
CSI
Beam Management
Positioning
CSI compression
  Baseline: R16 Type 2 codebook
  Observation:
  about 0.23%~9% mean UPT gain over baseline (max rank 1 and RU>=70%);
  about -0.2%~15% mean UPT gain over baseline (max rank 2 and RU>=70%);
  about -1%~17% mean UPT gain over baseline (max rank 4 and RU>=70%);
  Lower UPT gain for lower RU cases (e.g. RU <=39% & RU 40%~69%);
CSI prediction
  Baseline: non-AI prediction method
  Observation:
  About 0.7% ~ 7.0% mean UPT gain over baseline with max rank 1, based on inputs from two sources
Spatial-domain BM *
  Setting: Set B is a ¼ subset of Set A
  Observation:
    DL Tx beam prediction accuracy
    [about 70-80%] prediction accuracy achieved by AI for Top-1 case
    [more than 90%] prediction accuracy achieved by AI for Top-2 case
    RSRP difference
    [below or about 1dB] achieved by AI for Top-1 case
    Lower gain observed when Set B is a 1/8 subset of Set A
Temporal-domain BM *
  No formal observation achieved yet
* Lack of sufficient observations on UPT gain
Direct positioning
  Scenario: InF-DH heavy NLOS
  Baseline: conventional positioning method
  Observation:
  <1m@90% horizontal positioning accuracy as compared to >15m for baseline
Assisted positioning
  Scenario: InF-DH moderate/heavy NLOS
  Baseline: conventional positioning method
  Observation:
  <0.4m@90% horizontal positioning accuracy as compared to >9m for baseline in moderate NLOS scenario
  <1m@90% horizontal positioning accuracy as compared to >15m for baseline in heavy NLOS scenario

## Slide 5
RAN1 part main open issues for Rel-18 SI
Aspects | Progress till RAN1#113 | List of main open issues | Dependency with other WGs?
Functionality identification (UE side/part model) | Concept identified, functionality identification based on UE capability. Discuss dynamic update of functionality (including necessity). | Necessity and content (per sub use case) of additional conditions. Detailed signalling/procedure of UE-NW interaction. Applicable sub use cases/ collaboration levels. | RAN2: study signaling design and other essential aspects.
Model identification (UE side/part model) | Concept identified, model identification based on model ID report. Discuss model identification type A/B1/B2 (including necessity). Discuss dynamic update of applicable model (including necessity). | Further study/Down-selection among Type A/B1/B2. Detailed signalling/procedure for Type A/B1/B2. How to associate with additional conditions. Boundary/relationship with functionality identification. Applicable sub use cases/collaboration levels. | RAN2: study signaling design and other essential aspects, e.g., model ID structure, model ID assignment, details on Type A/B1/B2 if needed.
Training collaboration (two-sided model) | 3 training types identified; pros/cons initially analyzed yet no official observation. Spec impact of Type 2 deprioritized. | Performance justification of 3 types. Further study Type 1/3, including whether it is dominated by NW or UE. Dataset delivery method | RAN2: study the signaling for dataset delivery.
Model transfer/delivery | Case y/z1~z5 identified. | Further study Case y/z1~z5. Applicable sub use cases for model transfer. Model transfer direction (NWUE and/or UENW). | RAN2: study options of gNB/CN, CP/UP.
NW side data collection (DC) | CSI: agreed to further study ground-truth CSI content/type/format for DC for Training/monitor (including necessity) . BM: 3 options identified for the content of DC. Pos: Types of data identified: labels, measurements, etc. | CSI: RRC and/or L1 signaling to be further studied for DC for monitoring; necessity to be confirmed for DC for training, content/type/format to be decided. BM: Details/combination of the 3 options; Signaling for DC, e.g. whether air-interface is used. Pos: Need of spec impact for data report for each case (Case 1/2a/2b/3a/3b). | RAN2: study the signaling (L1/L3/MDT, etc.) to report the data.

## Slide 6
RAN2 part main open issues for Rel-18 SI (1/2)
Aspects | Progress till RAN2#122 | List of main open issues | Dependency with other WGs?
Functionality related | RAN2 agreed on a functional diagram, which aims to cover both model and functionality based LCM aspects. Model/functionality control (e.g. selection, switching) can be UE-initiated or NW-initiated. | Solutions should be defined per LCM component per use case. Open issues include: Need of functionality identification, data collection and functionality control. If needed, detailed design of functionality identification, data collection and functionality control. Whether/how to differentiate model-based LCM aspects and functionality-based LCM aspects. | RAN1: RAN2 has made some assumptions, and needs RAN1 to further check and confirm.
Model identification | One option is currently under RAN2 discussion: RAN2 assumes the model ID can be used to identify a model in model transfer/delivery, model control. RAN2 assumes model ID is unique “globally”. RAN2 assumes that some information may be required for model management and control. | Open issues include: For model ID, the ID structure is FFS. FFS on how to achieve globality of the Model ID (e.g. pre-defined, assigned id via a management node). For meta data, FFS on content, and applicable use cases. | RAN1: needs to discuss which of meta data parameters are need, and how to define them. SA2/SA5: may need to check the feasibility of model ID & how to achieve globality. SA3: may need to check security&user privacy aspect.
Model transfer/delivery | RAN2 agreed to aim to at least analyze the feasibility and benefits of some model transfer/transfer solutions, i.e. gNB/LMF/CN to UE via CP/UP manner, OTT server to UE. RAN2 agreed on some initial analysis on pros/cons for model transfer/delivery solutions. | Solutions should be defined per LCM component per use case. Open issues include: In order to better comparing solutions, some factors need to be defined, e.g. model size, model transfer frequency. For gNB/LMF/CN related solutions, pros/cons need to be further analyzed. | RAN1: needs to decide which of use cases needs which of model transfer/delivery solutions. SA2/CT1: may need to check the feasibility of LMF/CN related solutions. SA3: may need to check. security&user privacy aspect.

## Slide 7
RAN2 part main open issues for Rel-18 SI (2/2)
Aspects | Progress till RAN2#122 | List of main open issues | Dependency with other WGs?
Data collection (for model/functionality) | RAN2 endorsed a table as a starting point, which includes existing data collection mechanisms, i.e. logged MDT, immediate MDT, L3/L1 measurement, UAI, early measurement, LPP. RAN2 agreed to add 3 columns into the table, i.e. inference, monitoring and training. RAN2 expects RAN1 to provide more information on the requirement, so RAN2 agreed on a LS to RAN1. | Solutions should be defined per LCM component per use case. Open issues include: Define the dimensions for evaluating candidate solutions. RAN2 to wait for RAN1 replies on the data collection requirements, and then discuss pros/cons. | RAN1: based on the RAN2 LS, RAN1 needs to provide requirements for the RAN2 study. SA3: may need to check security&user privacy aspect.
Model/functionality control | For CSI/Beam use cases, model control or functionality control can be UE-initiated or gNB-initiated. For Positioning use case, model control or functionality control can be UE-initiated or LMF/gNB-initiated. | Solutions should be defined per LCM component per use case. Open issues include: Feasibility of UE-initiated or LMF/gNB-initiated. Whether different solutions need to be defined for different use cases. | RAN1: for a LCM for a use case, RAN1 needs to provide requirements, e.g. relevant measurements and which entity is to use it for some purposes (e.g. monitoring).
UE capability reporting (for model/functionality) | FFS if existing UE capability mechanisms (e.g. RRC/LPP) can be used for UE capability for AIML purpose. | Solutions should be defined per LCM component per use case. Open issues include: Requirements of static UE capability reporting definition, e.g. per LCM component per sub use case, possible KPIs. Whether/how to define dynamic UE information reporting. | RAN1: needs to provide requirements and corresponding scenarios.

## Slide 8
RAN4 part main open issues for Rel-18 SI
RAN4 SI AI/ML | Progress till RAN4 #107 | List of main open issues | Dependency with other WGs?
Test framework for two-sided model | 4 options are identified for further study to define encoder/decoder used for TE. | Whether/how to define encoder/decoder used for TE. | RAN1/RAN2: provides agreements on model training types and the corresponding signaling design.
Test metrics | Potential performance requirements for model inference are identified for further study. Potential core requirements for model monitoring and model management procedures are identified for further study. | Study the testability of test metrics and how the test metrics can be tested in RAN4. | RAN1: provides agreements on model training types. RAN1/RAN2: provides related procedure, e.g. model monitoring procedure.
Dataset generation | 3 options are identified for defining testing dataset for further study. | Identify typical simulation assumptions for which AI/ML performance gain is testable. | RAN1: provides typical simulation assumptions for RAN4 test.
Verification of model generalization | RAN4 agreed to study whether it is needed/feasible to introduce generalization related requirements for different scenarios/configurations. | Necessity and feasibility to introduce generalization related requirements for different scenarios/configurations, and if needed how to define the corresponding test cases. | RAN1: provides the scenarios/configurations for verifying the model generalization.

## Slide 9
New sub use case for Rel-19 study: TSF-CSI compression
For further exploring benefits of AI/ML on CSI compression, AI/ML model can learn time domain correlation of channels on top of spatial-frequency domain compression.
Past/historical information from previous slots are stored and used to compress/recover the CSI of the current slot
Performance
Further study on TSF CSI compression
  Performance evaluation
    Higher UE speed, generalization over UE speed, different training type, etc.
  Potential specification impact
    Robust mechanism when UCI missing, e.g., reset, re-transmission missing UCI, etc.
Initial results
  TSF-CSI compression can provide 14% addition gain on top of SF CSI compression, total 29% gain over R16
Chart: 
| R16 | SF | TSF | Ideal
FB, Rank ？ | 0.63 | 0.725 | 0.815 | 1
~29%
15%
Rank2 throughput gain, RU=80%, 80 bits
AI/ML model diagram of TSF-CSI compression
Motivation

## Slide 10
Large antenna array is critical for the successful deployment of mmWave.
With the current data collection mechanisms in Rel-18, the number of beams in Set B would be still large for mmWave with large antenna array
  Large BM sweeping overhead at the BS side, e.g. 256 beams to sweep
  Large latency for BM sweeping
Throughput improvement
SSB/CSI-RS
Accurate analog BF
RS measures
(RSRP + phase)
Optimal ABF
Enhanced data collection mechanism for BM for large antenna array
  Both L1-RSRP and phase based on the measurement collected during data collection
Performance gain
  BS sweeps less beams, giving more time for data transmission
  More accurate ABF increases throughput
1024 array，
64 DFT beams
Enlarged array
4096 array，
256 DFT beams
CSI-RS 1
CSI-RS 256
CSI-RS
1024
DFT beams
Dense oversampling beams for ensuring coverage
DFT B1
DFT B3
Oversampling beams
New sub use case for Rel-19 study: BM for large antenna array
Performance
Motivation