## Slide 1
Huawei, HiSilicon
NR positioning enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230325
Taipei, June 15 - 16, 2023

## Slide 2
Content
Motivation
mmWave positioning
Carrier Phase based Positioning (CPP) enhancements

## Slide 3
Motivation of centimeter level accuracy
R15
Basic 5G positioning
Regulatory: horizontal 50m@80%
Features
Network based NR CID and cell portion positioning
R16
Basic NR positioning
Regulatory: horizontal 50m@80%
Commercial outdoor: 10m@80%
Commercial indoor: 3m@80%
Features
6 NR positioning methods
New positioning reference signals
Positioning measurement (UE/gNB)
Physical layer procedure
Positioning signaling and procedure
UE-based positioning support
PPP-SSR assistance data
Broadcast assistance data (NR PosSIB)
SI request in CONNECTED state
R17
IIoT positioning
Accuracy: 0.2m/0.5m@90%
Latency: 100ms
Features
LOS/NLOS identification
Group delay labeling
Multi-path assisted positioning
Angle-based positioning enhancements: (AoA/AoD)
PRS measurement without measurement gap
INACTIVE state positioning
On-demand PRS
GNSS integrity
R18
IIoT and V2X positioning
Battery life: 1 year
Accuracy: 0.2m@90%
Features
INACTIVE state positioning with SRS validity area and eDRX
BW aggregation for intra-band contiguous CCs
RSCP measurement for CPP
Ranging/SL positioning
Frequency hopping positioning
NR positioning integrity
IDLE state DL positioning
Basic 5G positioning (regulatory requirements)
Basic NR positioning functionality: 0.5m@90%
IIoT positioning evolution:
1 year battery life & 0.2m@90%
R19
IIoT AGV positioning
Accuracy: 0.1m@90%
Features (Huawei proposal)
Path-based SRS Tx beamforming for mmWave positioning
Dual-subband RS and subband RSCP reporting
Centi-meter accuracy: 0.1m@90%
AGV requires 10cm level accuracy

## Slide 4
mmWave positioning
Legacy baseline
Multi-TRP positioning for FR2
UE Tx beam sweeping
TRP
TRP
TRP
Tx beam sweeping
UE Tx beam alignment
TRP
TRP
TRP
Tx beam alignment
Drawbacks of Tx beam sweeping
Tx beam sweeping wastes resources: UE-TxBeam# times BS-RxBeam# sweeping.
Transmission of multiple beams could suffer clock drift.
Drawbacks of Tx beam alignment
Multi-UE SRS transmission direction should be coordinated to be received at the same time by a TRP.
DL Rx beam training effort across multiple TRPs.
Single-TRP positioning for FR2
Drawbacks of RTT+AoA
Group delay error compromises the RTT measurement
2ns contributes to the distance error of 0.6m
Rx group delay
Tx group delay
Rx – Tx time difference BB
Rx – Tx time difference RF
TRP
UE
RTT+AoA
Multiple LoS TRPs (at least 3) are needed

## Slide 5
mmWave positioning
Rel-19 enhancement
Rel-19 should prioritize single-TRP positioning for FR2, using reflection to cancel the group delay error in RTT.
x
z
Ground
UE
y
h
d
UE
Location algorithm
Location evaluation InF-DH: (Central frequency=30GHz, ISD=20m) |  |  |  |  |  |  | 
 | Single-BS, RTT+AOA | Bandwidth | Group delay error STD | 50% | 67% | 80% | 90%
Horizontal | LOS only | 400MHz | 2ns | 0.364 | 0.527 | 0.704 | 0.882
 |  | 800MHz | 2ns | 0.361 | 0.522 | 0.694 | 0.875
 | LOS + Ground reflection | 400MHz | 2ns | 0.028 | 0.055 | 0.091 | 0.177
 |  | 800MHz | 2ns | 0.014 | 0.026 | 0.043 | 0.084
Vertical | LOS only | 400MHz | 2ns | 0.145 | 0.221 | 0.314 | 0.432
 |  | 800MHz | 2ns | 0.145 | 0.220 | 0.312 | 0.430
 | LOS +Ground reflection | 400MHz | 2ns | 0.009 | 0.015 | 0.021 | 0.030
 |  | 800MHz | 2ns | 0.004 | 0.006 | 0.009 | 0.014
Evaluation results
Proposed enhancement (spec impact)
Support UE to perform UL Tx beamforming based on path RSRP (RSRPP).
Study the identification/path tracking for the ground reflection or any other reflection type
: horizontal distance (unknown)
: UE height (unknown)
: ZoA (measurement)
: TDOA between LoS path and reflection path (measurement)
Considered enhancement
(1) SRS Tx beamforming based on path RSRPP
This allows multiple SRS associated with a single DL RS as the path spatial relation
UE beam 1
UE beam 2
Same DL PRS
(gNB Tx beam)
LoS path
A useful reflection
(2) Path association reporting
Tracking the NLoS (reflection path) for better identification

## Slide 6
CPP enhancements
Rel-18 CPP considers existing Rel-17 PRS/SRS with single RSCP measurement report per carrier
Rel-18 baseline
Legacy RS
TOA uncertainty
(ambiguity)
O
Intersection based on joint integer ambiguity hypothesis from multiple TRPs/TRP pairs
gNB ARP error (e.g. 2cm)
Ground truth gNB ARP
Used gNB ARP
TRP#1
TRP#2
TRP#3
TRP#3
TRP#1
TRP#2
Ground truth UE location
Estimated UE location
Without gNB ARP error
With gNB ARP error
ToA uncertainty
The integer ambiguity values within the ToA uncertainty range are of equal likelihood for a single RSCP measurement and reporting.
No likelihood difference between and for a single RSCP/RSCPD measurement
Rel-19 enhancement
Rel-19 CPP could consider dual-subband RS and subband RSCP reporting
TOA uncertainty
O
Good linearity
Poor linearity
Poor linearity
Estimated UE location
gNB ARP error (e.g. 2cm)
TRP#2
With gNB ARP error
TRP#3
TRP#1
The linearity between origin, and two subbands RSCP measurement is considered as the likelihood of the integer ambiguity
InF-SH location error @90% | perf gNB loc | 2cm gNB loc error
UL- TDOA | 0.1501 | 0.1952
UL-DPDOA | 0.0018 | 0.1355
Multi-Freq (100MHz) | 0.0668 | 0.1035
Multi-Freq (DS-RS with Power Boost) | 0.0301 | 0.0536
Evaluation results
Proposed enhancement (spec impact)
Specify dual-subband RS pattern on the same symbol
Specify multiple subband RSCP/RSCPD reporting

## Slide 7
Overall work/study item proposal
Specify enhancement of reflection based positioning [RAN1]
  Specify positioning SRS Tx beamforming based on path RSRP (RSRPP)
  Study, if needed, the identification/path tracking for the ground reflection or any other reflection type
  Note this objective targets FR2
Specify enhancement of carrier phase positioning [RAN1]
  Specify a dual-subband RS pattern on the same symbol for both DL-PRS and UL-SRS
  Specify multiple subband RSCP/RSCPD measurements for both UE and gNB
Specify necessary signaling to support the procedure [RAN2/RAN3]
Specify corresponding RRM requirements [RAN4]