## Slide 1
Huawei, HiSilicon
MBS enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230326
Taipei, June 15 - 16, 2023

## Slide 2
Contents
Overview
MBS enhancements
  Extended CP
  Multicast optimization in RAN sharing scenario
Potential objectives

## Slide 3
Overview
Rel-17
Efficiency improvement
Further efficiency improvement
Rel-18
Rel-19
Broadcast
Multicast
(NR new function)
Basic broadcast support
  DL only broadcast, support any RRC states
  scheduled by G-RNTI on PDSCH without HARQ feedback/re-transmission
  Areas (cells list/TA list) based MBS session start/stop
Basic multicast support
  only for RRC Connected state
  scheduled by G-RNTI on PDSCH, supporting HARQ feedback/re-transmission
  multicast group is managed by CN
  supporting PTP/PTM dynamic switch controlled by RAN
  supporting lossless handover for MBS Multicast
  Enhancement for better spectrum efficiency
  Support extended CP
Enhancement on simultaneous reception of broadcast and unicast
  Enhance the UE capability and MII procedure for higher unicast scheduling efficiency
  Broadcast optimization in RAN sharing scenario
  Support the gNBs identifying the same service of different sessions from different PLMNs to reduce Uu resource consumption
  Support for multicast reception in RRC_INACTIVE state
  Extend multicast reception to RRC_INACTIVE state for UE power saving
  Multicast optimization in RAN Sharing scenario to reduce Uu resource consumption
Addressing lower QoS services
Providing best effort QoS
  Addressing higher QoS services
  providing multicast group management and same level QoS fulfillment as unicast
Basic Support of MBS

## Slide 4
Extended CP
SFN of 7 cells (12 reserved cells)
Chart: 0.7GHZ, SE / SFN size
| 7(12) | 19(18) | 37(24) | 61(30)
4.7us | 0.32691 | 0.52614 | 0.58146 | 0.71992
16.7us | 0.56059 | 0.95883 | 1.3415 | 1.5967
33.3us | 0.46715 | 0.79902 | 1.1179 | 1.3305
Motivation
  SFN is supported in R17/R18 within one single gNB by network implementation
  TV/video broadcast services can benefit from SFN to achieve better performance at cell edge.
  The CP length limits the size of SFN area and the size of SFN area limits the spectrum efficiency gain.
Potential objective
  Extend CP length for 15kHz SCS and 30kHz SCS [RAN1/2]
    Need to consider coexistence between extended CP and normal CP in a cell

## Slide 5
Multicast optimization in RAN sharing scenario
UE group in CN1
UE group in CN2
CN1
CN2
MBS service
PTM
sharing node
TMGI 1
TMGI 2
Motivation
  Rel-18 has only been specifying the enhancement to MBS broadcast for RAN sharing scenario
    - For the same MBS broadcast service, in shared RAN (with different CNs), there will be only one copy of MBS broadcast packets delivered over Uu
  MBS Multicast was not enhanced for RAN sharing. Radio resource can be significantly saved if shared transmission in Uu for the same multicast service is supported
Potential objective
  The shared gNB identifies the same multicast service from different PLMNs [RAN3]
  Mobility handling between RAN-sharing and non-RAN-sharing gNBs [RAN2/3]

## Slide 6
Potential objects
Proposal: Specify the following enhancements for MBS in Rel-19
    Support extended CP [RAN1/RAN2]
    Optimize MBS multicast transmission in RAN sharing scenario [RAN3/RAN2] Note
          Note: coordination with SA2 is needed